RARE COLLECTIONS LIBRARY

Office of Commonwealth Libraries

PA Department of Education

Performance requirements for the

Misting System Fire Suppression System Service Contract

SUMMARY:

The Pennsylvania Department of Education (PDE), Office of Commonwealth Libraries (OCL) seeks quotes from qualified companies/contractors henceforth identified as the “contractor” to provide comprehensive maintenance, service and emergency service for the installed Marioff water misting fire suppression equipment and systems which protect multiple areas within the Rare Collections Library (RCL) within the State Library of Pennsylvania (SL), located in the Forum Building, Capitol Complex, Dauphin County, Harrisburg, PA.

PURPOSE:

Maintain all misting suppression equipment and controls with little or no operational downtime.

- Ensure uninterrupted operation with the exception of scheduled maintenance

- Ensure system performs to original design parameters.

- Maintain work records to establish future needs and priorities.

BACKGROUND:

The RCL of the State Library houses some of the rarest and most historically significant books for which the Commonwealth of Pennsylvania is responsible.  The Exhibit Hallway, Archivist’s Office and Reading Room are not candidates for either a conventional wet sprinkler or any type of gas or clean agent fire suppression system due to existing building design elements and required HVAC systems for these and adjacent spaces dedicated to providing correct environments for various segments of the RCL.  The climate controlled areas of the RCL are a product of multiple environmental systems which are maintained at pre-established environmental set points (temperature, humidity, etc.) creating pollutant-free stable environments for the preservation of historic paper-based collections. All environmental equipment used for sustaining this multiple climate-controlled environment, including the air filtration media/housing, must perform within their respective design tolerances 24/7/365.  There is no off season.

AREA(S) SERVICED:

The RCL is located in the north and south sides of the east wing (EW) of the Forum Building.  The RCL Library consists of six (6) primary spaces and several ancillary spaces.  The combined holding capacity of the primary spaces is approximately a half million volumes and other rare, irreplaceable and historic paper-based materials.

The water misting suppression equipment under this maintenance contract supports three (3) of these multiple preservation-based environments for the following spaces:

Area(s)				Location

- Exhibit Hallway				Ground Floor, EW, Forum Building

- Archivist’s Office 				Ground Floor, EW, Forum Building

- Reading Room				Ground Floor, EW, Forum Building

CONTRACT WORK:

Provide semi-annual preventive routine maintenance, and emergency service(s) for water misting fire suppression equipment which is part of the RCL environmental systems.

SERVICES INCLUDE BUT ARE NOT LIMITED TO:

- Inspecting fire detection, protection and suppression equipment and checking for proper operation and mechanical function.

  - Adjusting valves, actuators, sensors, control units and other associated equipment.

    - All adjustments must be completed during scheduled visit.

- Performing a full psychometric analysis of the equipment’s performance using calibrated gauges and tools.

- Providing standard contractor report and a required OPR to the  Bureau of State Library Director or his/her designee after each service event regardless if the call is for routine maintenance or emergency service.

- Providing two (2) hours of on-site emergency service.

- Work with the Commonwealth’s staff monitoring the equipment and areas through WebCtrl to insure the systems are reporting correctly to the system

- Insuring that environmental conditions of all areas being serviced are trended at 10 minute intervals to ensure no uncontrolled deviation from design parameter(s) occurs within the areas monitored.

CONTRACTOR REQUIREMENTS:

- Contractor Experience

  - Have at least five (5) years of documented experience with misting type fire suppression systems installation, maintenance and service, as supported by a resume with bid submission.  Contractor’s work experience in certified clean rooms, museums, archival housing or any comparable facility in which contractor’s primary experience was/is maintaining environmental systems which were/are maintained under similar design parameters as those of the RCL will be viewed favorably.

  - Provide contact information in the event that the OCL requires further clarification of services provided for referenced facilities.

Name							Title

__________________________________________________________________

__________________________________________________________________

__________________________________________________________________

- Management Personnel

  - Contractor must have access to technical personnel and/or an engineer on staff of five (5) years’ experience in misting fire suppression systems.  A resume of the person designated for this position is required.

  - Contractor’s staff and representatives must be trained by Marioff Corporation.

- On-Site Technician(s)

In addition to the service technicians being fully capable of performing the general maintenance duties of their respective trade(s) they must:

  - Prepare a written Optimum Performance Report (OPR) provided by the OCL after each service session for each piece of equipment. Information included in the report but not limited to:

    - Detail any modifications, service or operating parameter changed with recommendations

    - List of items to be monitored if applicable

    - Recommended in-place repairs and/or future repairs required

    - Replacement parts installed

    - System modifications and routine maintenance suggestions.

    - Consumables left on site.

    - Identified and cataloged per model number and unit ID.

  - Along with a copy of the contractor’s service report, a signed copy of the OCL’s OPR must be provided to the Bureau of State Library Director or his/her designee before the service technician leaves the site.

  - Provide routine maintenance, suggestions and clarifications as well as fault troubleshooting and problem-solving to OCL staff.

  - It is the contractor’s responsibility to ensure that correct service manuals/ updates from the manufacturer are kept on file both at his place of business and on file at the RCL for each piece of equipment covered under the maintenance contract.

  - All tools, equipment, carry bags, and clothing must be thoroughly cleaned prior to being admitted into the RCL and its support spaces.

  - Current calibration certificates, for any testing equipment, used on site, must be provided to the OCL’s Bureau of State Library Director or his/her designee.

  - Contractor’s technicians must be trained in the use of Tyvek clean suits, booties, gloves, etc.

    - Each technician must have their own personal gear for admission into the RCL to perform any maintenance.  Refer to SOP # 10.06 – Tyvek Suits

EMERGENCY SERVICE:

- For emergency service calls, the contractor must have qualified controls technician available by telephone 24/7/365.

  - This technician must be able to respond to “on-site” personnel questions for immediate evaluation and stabilization of water misting fire suppression system.

  - If emergency situation cannot be corrected by on-site personnel, contractor must be able to dispatch a service technician within 24 – 48 hours for repairs of failed equipment.

    - An emergency phone number for 24/7/365 access to the designated person is a mandatory requirement and must be maintained throughout the course of this water misting fire suppression system.

ACCESS/SECURITY:

- The RCL is a controlled access facility with varying degrees of security for the protection of the collections and for maintaining the multiple environments which support the collection.

  - Security protocols must be followed at all times.

    - Refer to SOP # 10.03 - Security

- Access protocols must be adhered to

  - If a walkthrough of certain areas is required for inspection prior to a bid proposal, this must be scheduled through the Bureau of State Library Director or his/her designee .

  - Refer to SOP # 10.01 – Site Access

    - Parking is limited in the Capitol Complex, therefore all service calls must be scheduled in advance through the OCL Administrative Officer.

STANDARD OPERATING PROCEDURES (SOPs):

- The Rare Collections Library has instituted standard operating procedures put into place to ensure the long-term preservation of the Library’s holdings.

  - These SOPs are not to be countermanded, except with written, signed and dated instructions directly from the Bureau of State Library Director or his/her designee to the contractor.

- In the event of a catastrophic emergency, as decreed by the OCL, verbal instructions given by the OCL may supersede a written SOP.

  - After the event, the OCL will provide written clarifications as to why it countermanded protocol and directed the Contractor not to follow standard protocol.

    - After the safety of the collection(s) has been secured and is out of immediate danger, a report must be completed by each entity engaged in securing the safety of the collections.

    - The report will indicate the reason(s) instructions were given, manner in which work was carried out, suggestions and observations, signed and dated by site personnel and submitted to the OCL’s Administrative Offices for future reference.

SOPs ATTACHED:

      - SOP #10.01 – Site Access

      - SOP #10.02 – Facility Access

      - SOP #10.02a – Work Admin

      - SOP #10.03 – Security

      - SOP #10.03a – ID Badging

      - SOP #10.03b – Security Plan

      - SOP #10.04 – Clean

      - SOP #10.05 – Equipment Storage

      - SOP #10.06 – Tyvek Suit

      - SOP #10.07 – Dehumidification Back-up

      - SOP #10.09 – Steam Shut-Down

The OCL, at a future date, may issue additional SOPs for clarity, uniformity, but most importantly the protection and preservation of its collections. From the date of issue forward, any new SOP must be followed as if listed above.

MAINTENANCE MANUALS:

A complete set of operating manuals, inclusive of contractor service reports, OPRs, equipment records and updates will be kept in the OCL Administrative Offices for each clean agent fire suppression systems as part of this contract.

- It is the Contractor’s responsibility to keep all records of the equipment covered by this contract up-to-date of last service, including the most recent manufacturer’s update(s).

  - Maintenance Contract

  - Standard Operating Procedures (SOP)

  - Contractor’s Service Reports

  - OCL’s Optimum Performance Reports (OPR)

  - Emergency Reports

  - Equipment Manuals

  - Manufacturer Updates

  - MSDS sheets for substances used during service

- It is the OCL’s responsibility to maintain these records in book form for easy access when needed by this contractor or other maintenance contractor who may require such information to perform their respective duties.

SAFETY:

Due to the nature of equipment and work being performed by the maintenance contractor, this maintenance work and service duties are deemed dangerous work.  It is the contractor’s responsibility to train their staff in all safety procedures regarding the type of work which this maintenance contract entails so as to protect maintenance staff, library staff and public from injury.

- A safe working environment assists in maintaining the service equipment within proper operating parameters so as to minimize possible inadvertent damage to the equipment being serviced.

- A copy of all safety training which staff personnel receive must be provided to the RCL EO.

- Any staff personnel sent to the RCL for service calls is certified by the contractor as to having all the required safety training for his/her classification and type of work which may be performed.

CONFIDENTIALLITY CLAUSE:

The RCL is a repository of historic, rare, irreplaceable paper-based collections, a one-of-a-kind primary source library.  The value of individual items housed in this facility cannot easily be stated, to have original one-of-a-kind collections intact, makes these collections a true national treasure.  As such, security for these collections is a constant concern, as is their preservation.

As a maintenance contractor for this RCL, the Contractor is privy to information that in the wrong hands could result in possible damage or loss of portions or all the collections.  At no time without written approval from the Bureau of State Library Director or his/her designee and counter signed by the Deputy Secretary of Education for Commonwealth Libraries is the Contractor or any personnel under their authority allowed to discuss details of the Library’s collections, security, mechanical/electrical systems, physical layout of the Library, protocols, or any other type of information which could possibly compromise the protection or preservation of the Rare Collections Library’s holdings.

All inquiries, regarding the Rare Collections Library must be directed to the Office of Commonwealth Libraries Administrative Offices, no exceptions.