Diesel Generator

Maintenance and Repair Site 41

Statement of Work

- Service Location:

- I-80 Eastbound Mile Post 295, Monroe County, Scotrun, PA

- General:

- This service will be for a period of one (1) year with one (1) option to renew, upon mutual consent, for an additional three (3) year period.  A one-time four percent (4%) price increase shall be applied to all of the original bid rates for the term of the renewal period.

- The Department of Transportation, hereto referred as the Department, reserves the right, upon notice to the contractor, to extend the term of any purchase order for up to ninety (90) days upon the same terms and conditions.

- The Department reserves the right to award any or all of the bid items.  All quantities and items are estimates.

- Prior to the start of any work, the contractor shall provide the Department with the business phone, cell phone, fax and e-mail of the contractor’s representative(s) who will be responsible for all contract related matters including but not limited to scheduling, billing and personnel.

- Upon the contractor’s arrival at the rest area, the contractor is required to sign the attendant’s daily log book located in the attendant’s office documenting time of arrival.  Upon departure from the rest area, the contractor is responsible for documentation of the repairs completed during the service visit.

- The Roadside Rest Area is open to the public 24 hours a day 7 days a week.  All maintenance and repairs shall be performed with this in mind.

- For the purposes of the work “regular business hours” shall be defined as Monday through Friday 8:00AM to 4:00, and holidays shall be defined as New Year’s Day, Memorial Day, Independence Day, Labor Day, Thanksgiving Day, and Christmas Day.

- Contact shall be made with the District Roadside Specialist or designee 24 hours in advance of regularly scheduled service visits to ensure there will be no conflicts. An approved contact list and phone numbers will be provided to the awarded contractor prior to the start of any work.

- Description of Work:

- Generator Service shall consist of regular scheduled preventative maintenance and unscheduled on call repair as needed to the Power Generation System and automatic transfer switch(s) (ATS).  At each visit, the contractor shall include in their report any upgrades or improvements that could benefit the system.

Power generation System: 	MTU Onsite

Model MTU 6R0120 DS200

Serial 95130600615

ATS: 		ASCO

480V Single Phase 600A ATS

- The contractor will be required to perform all the following in addition to any manufacturer suggested maintenance once yearly during the Annual Full Service visit.  The contractor shall mark every filter and or replacement part, when reasonably feasible, in permanent marker or paint pen with the date of replacement and the initials of the contractor’s representative that replaced it.  All labor, tools, equipment, fluids, lubricants, and filters shall be incidental to the lump sum bid price per Annual Full Service Visit.

- Check all components of the AC electrical system

- Check air intake system

  - Replace filter

  - Check belts and hoses and clamps

- Check Cooling system

  - Add or Change fluid if needed

  - Check hoses clamps and belts

- Check DC electrical system

  - Check for proper voltage

  - check battery operation by conducting a load draw test

  - check battery fluid and add if needed

  - check and clean battery terminals if needed

  - check condition of all cables and wiring

  - check operation of the alternator

- Exhaust System

  - Inspect all piping, muffler and rain caps for wear or leakage

- Fuel System

  - Inspect and change filter if needed

  - Inspect all lines for leakage

- Lube Oil System

  - Completely drain and replace oil

  - Replace oil filter

  - Check all lines for leakage

- Safety Settings

  - Check to insure settings are in place and operational for emergency shutdown including

    - Engine overheat

    - Oil pressure

    - Over crank

    - Over speed

- Auto Transfer Switches (ATS)

  - Check operation

  - Wiring condition

  - Lubricate as needed.

- Three times annually, the contractor shall perform a “quarterly inspection” of the Power Generation System and ATS’s.  This visit shall include the following and any other manufacturer recommended maintenance.  The contractor shall mark every filter and or replacement part, when reasonably feasible, in permanent marker or paint pen with the date of replacement and the initials of the contractors representative that replaced it. All labor, tools, equipment, fluids, lubricants, and filters shall be incidental to the lump sum bid price per Quarterly Inspection Service Visit.

- Check all components of the AC electrical system

- Check air intake system

  - clean filter if needed

  - Check belts and hoses and clamps

- Check Cooling system

  - Add fluid if needed

  - Check hoses clamps and belts

- Check DC electrical system

  - Check for proper voltage

  - check battery operation by conducting a load draw test

  - check battery fluid and add if needed

  - check and clean battery terminals if needed

  - check condition of all cables and wiring

  - check operation of the alternator

- Exhaust System

  - Inspect all piping, muffler and rain caps for wear or leakage

- Fuel System

  - Inspect filter

  - Inspect all lines for leakage

- Lube Oil System

  - Check engine oil and add if needed

  - Check all lines for leakage

- Safety Settings

  - Check to insure settings are in place and operational for emergency shutdown including

    - Engine overheat

    - Oil pressure

    - Over crank

    - Over speed

- Auto Transfer Switches (ATS)

  - Check operation

  - Wiring condition

  - Lubricate as needed.

- Once annually the contractor shall perform a load bank test on the generator.  Provide a load bank with sufficient capacity for testing.  Provide all labor, equipment, cables, and testing instruments needed to perform the load bank test.  Perform the load bank test over not less than 1.5 hours.  Run the unit at not less than 50% of the nameplate KW rating continuous for a minimum of one half hour and at not less than 75% of the name plate KW rating for a minimum of one continuous hour.  All labor, tools, and equipment shall be incidental to the lump sum bid price per Load Bank Test visit.  At the conclusion of the test submit a report to the District Roadside Specialist.  The report shall at a minimum list the following in ten to fifteen minute intervals:

  - Time (military time)

  - Oil pressure

  - Water Temperature in Fahrenheit

  - Exhaust Temperature in Fahrenheit

  - Hertz

  - Volts

  - Amps

  - Kilowatt output

  - Any relevant comments about the performance of the unit

- The contractor will be responsible for the cleanup and disposal of all waste fluids and filters.

- Only manufacturer approved parts and fluids shall be used.  The Department reserves the right to inspect all parts and fluids provided by the contractor.

- All parts and labor shall be warranted for thirty (30) days.

- Service shall be available on a 24-hour 365 day a year basis.  The contractor shall provide a 24-hour phone number where they can be reached.  All requests for service shall be acknowledged by the contractor by a return telephone call to the requestor within two (2) hours following the request and shall indicate the estimated time of the technician’s arrival to the facility.

- The contractor shall be onsite within four (4) hours of all service requests for emergency break down or emergency.

- Service Schedule:

This service schedule shall be considered a guide:

Annual Full Service 		October of each year

Quarterly Inspections		January

April

July

Load Bank Test			Perform within 2 weeks of request

- Qualifications of Contractor:

      - All work shall be performed by factory trained technicians.

      - Only one technician shall respond to service requests unless approved by the District Roadside Specialist or Designee.

- Materials and Payment:

      - The cost of materials, parts or replacement equipment, that are not included in the scheduled service visits, shall be invoiced at suppliers invoice price plus 15%. All material in excess of $200.00 will require approval by the District Roadside Specialist prior to purchasing.  A copy of all invoices for materials must be submitted along with the invoice to the Department.

      - All labor and materials used for work performed must be documented on a mutually agreed upon form that would include but not be limited to the following

      - Date of Services

      - Equipment Serviced

      - Arrival time of the technician

      - Departure time of the technician

      - Description of services performed

      - A list of parts replaced

      - Any recommendations or observations

      - Signature of the contractor’s representative.

      - The quoted rates will include all tools or any equipment necessary to perform routine maintenance for service calls.

      - Repairs made without the authorization of the proper Department personnel are subject to non-payment.  Prior to the effective date of the contract, the Department will provide a list of authorized personnel responsible for requesting repair work and directing work onsite.  The Department will not be responsible for payment of any work performed that is directed by unauthorized personnel.

      - Travel time is not included as hours of service and cannot be charged for any work performance under this contract.  Contractor’s time begins upon arrival at site and ends upon departure from site.  No additional time allowance is made.

      - Invoices for payment shall be submitted to the address listed on the first page of the Purchase Order in the “Please Bill To” box.  A copy of the invoice shall be submitted to the attention of the District Roadside Specialist at the below address or through email at rboronyak@pa.gov.

PennDOT Engineering District 5-0

Maintenance Unit – Ray Boronyak

1002 W Hamiltion St

Allentown, PA 18101

Failure to do so may result in delayed or non-payment.

- Insurance Requirements:

- Refer to the attachment for Insurance Requirements.

- Safety Requirements:

- All work shall be performed in a safe and orderly manner with minimum interference to person(s) using the safety rest area.  The safety rest areas are available to the public on a 24-hour basis.  Should the contractor require an interruption of service, the contractor must immediately notify the Department, prior to any work being performed.

- Non-Compliance:

- In the event that any materials furnished by the contractor are found to be defective, unsuitable, or otherwise unacceptable, the materials shall be removed by the contractor and replaced with acceptable materials and installed anew to the satisfaction and approval of the District Roadside Specialist at the cost and expense of the contractor.

- If for any reason the contractor fails to respond within the timeframe as outlined in these specifications, liquidated damages in the amount of $150.00 will be charged per occurrence.  For three or more occurrences, the Department will find the contractor in non-compliance with the contract requirements.  This action may result in immediate termination of the contractor.