NO MANUFACTURER SUBSTITUTIONS ARE ALLOWED FOR THIS REQUEST

Gemini S5 FTIR / Raman Spectroscopic Detector:

Description  - Gemini Analyzer -  Gray Boot

Weight (English):   4.2 lbs

Weight (Metric):   1.9 kg

Spectral Range FTIR:      4,000 cm-1  to  650 cm-1

Raman:   250 cm-1  to  2875 cm-1

Data Export Formats:   SPC file (for use in standard spectroscopic software), text file, or JPEG report

Temperature (Metric) Operating:   -20°C to +50°C

Collection Optics:   FTIR: ATR diamond crystal, single bounce Raman: NA= 0.33

Survivability:   Certified to MIL-STD-810G and IP67; full test report available on request

Dimensions (L x W x H):  10.1 in x 5.7 in x 2.4 in (25.6 cm x 14.6 cm x 6.1 cm)

Languages:   English

Power Supply:  Internal 3.7V lithium polymer (QTY 1) battery pack Internal CR123A (QTY 3) batteries DC wall adapter, 12 V DC 1.25 A

Including 5 years Warranty, 5 years Support, and On-Site Training within the Continental United States(CONUS; One 4-hour course per instrument for up to 12 students. Expires 9 months after date of purchase).

Must include at least a 25% discount from the manufacturer for trade in of instruments noted below.

Instrument Trade-In

Ahura Scientific 1st Defender XLS-5   s/n   FD 5778

Ahura Scientific 1st Defender XLS-5   s/n   FD 5779

Smiths Detection HAZMATID    s/n   004140604A

Smiths Detection HAZMATID    s/n   004150604A

Shipping to zip code 15208:

DO NOT USE     FED EX     FOR EQUIPMENT SHIPPING!!