STATEMENT OF WORK

Curtain Wall for SCI Forest

IFB

- CONTRACT SCOPE/OVERVIEW: This invitation for Bid (IFB) is being issued by the Department of Corrections (DOC), Pennsylvania Correctional Industries (PCI).  Pennsylvania Correctional Industries (PCI) is installing a wheel refurbishing plant located at SCI Forest.

- METHOD OF AWARD:  Award be awarded based on the lowest responsive and responsible bidder.

- PRICING: Bidders must submit pricing through eMarketplace vendor portal.  Electronic bids only.  No emails or paper bids will be accepted.

- SPECIFICATIONS:

Curtain Wall

  - 18-ounce vinyl fabric is fire retardant and meets NFPA-701 standards

  - SCL stationary non-insulated curtain wall system, 18oz BLUE FR vinyl fabric.

  - Curtain sizes as follows:

- Curtain A: 30'-0"W x 36'-0"H

- Curtain B: 45'-0"W x 36'-0"H

- Curtain C: 30'-0"W x 36'-0"H

  - Curtains to include fabric corner/wall/tee connectors as required by layout.

  - Curtains supplied in nominal 5’W panels, with hook/loop closure strips along each vertical edge for field joining.

  - Hemmed top edge for mounting with Tek screws and fender washers (by others).

  - Curtains include 8”H integral trimmable bottom sweeps, same fabric and color as main curtain cover fabric.

6x7 double pedestrian door

  - 6’W x 7'H pedestrian door.

  - Doors come pre-mounted in free-standing 2x4 steel tube welded frame with 6” x 6” x 3/8" bolt-down floor anchor plates.

  - Frames painted black at factory.

  - Door panels are clad in light gauge steel with interior wood blocking and Styrofoam insulation.

  - Std. brass plated hardware supplied.

  - Door equipped with ADA lever/latch set on active door, and 10"W x 10"H vision lite in each panel.

  - Door panels are primed white.

Price to include mounting curtain to the bottom of a solid beam or truss

Layout:	A

C

B

- INQUIRIES:  Direct all questions concerning this bid and any subsequent awarded Contracts to the Contracting Officer:

Michele Ametrano-Warford,

Purchasing Agent 2

mametranow@pa.gov

717-728-4038.