#### ATTACHMENT “A”

October 31, 2018

###### Specifications for Plumbing Services

I.	Description

This Contract will be utilized for maintenance repair of all plumbing fixtures and piping, both for water and wastewater at the Departments Welcome Center sites within Engineering District 1200. Piping is both interior and exterior, located above and below grade, in confined spaces and under concrete flooring. Contractor shall have capabilities to repair, replace and / or cleanout in these areas or any other area within the site complex.

The Department Welcome Centers are located in:

Greene County (Site “D”) Interstate 0079; Northbound at approximately 6-mile marker Whitely Township, Pennsylvania

Washington County (Site “A”) Interstate 0070; Eastbound at approximately 5-mile marker Donegal Township, Pennsylvania

A.	This work shall consist of servicing, maintaining and/or repairing sewage and water systems as required; including both the Wastewater Treatment Plant at the Greene County Welcome Center (Site D) when required and the Wastewater Lift Station at the Washington County Welcome Center (Site A). The contractor shall be responsible for the disposal of items / materials removed to an approved site unless otherwise retained by the Department.

B. 	The plumbing contractor shall be qualified to perform plumbing work and shall be licensed in Pennsylvania by the Pennsylvania Department of Labor and Industry.  All work shall be performed in accordance with the Pennsylvania Department of Labor and Industry Building Code and all materials utilized must be originally manufactured or approved substitutes. The plumbing contractor, upon notification of the District Roadside Specialist, shall proceed and complete the work as promptly as possible.  In the event of a plumbing failure during non-business hours, the plumbing contractor shall be prepared to mobilize and report to the work site upon notification by the District Roadside Specialist and proceed with the work upon arrival.  The contractor must be able to perform non-business hour work on a 24-hour basis. When notified of a non-business hour plumbing failure the contractor shall be on site (either Welcome Center) within three hours of notification.

C.	By mutual consent of both parties, this contract is renewable for two (2) - two-year periods.  Each renewal will receive a four percent (4) percent increase on the unit price for each item.

- Anticipated Effective Date --- February 1, 2019

- Anticipated Expiration Date -----January 31, 2020

D.	The cost of materials, parts, or repair equipment not to exceed total dollar amount of contract shall be FOB the job site and invoiced at the contractor’s cost plus 15%. No material purchase more than $300 may be initiated without approval of the District Roadside Specialist.

E.	All labor and materials used at the interstate Welcome Center will be documented District1200 Roadside Daily Cost Report Form (attached to these specifications). This report shall serve as basis for payment.  Prepare current Form OS-501 Confirmation of Service Form for work satisfactorily completed and submit as directed, as work is completed.

Suppliers invoice shall be required for all furnished parts costing $20.00 or more. The District Roadside Specialist or his designee following completion of each work assignment and the contractor’s representative will sign this report.  This report shall serve as a basis for payment.  Invoices will be submitted in triplicate monthly to the District Roadside Specialist as work is performed.

F.	The quoted hourly rates include all contractor costs, including transportation, hand tools and small equipment, necessary to perform the required work.  The contractor’s attention is directed to the fact that the number of work hours on the Service Bid Contract (SBC) and the material amount are estimates for one year only.  The actual demand may be as determined by the need for plumbing services.

G.	The awarded contractor and their primary plumber that will be performing repair work shall as an integral part of this contract review the jobsite and contract requirements with the District Roadside Specialist.  This meeting will be limited to two (2) hours per Welcome Center site and no payment will be made for this meeting.

H.	The contractor upon arrival at the Welcome Center will report to the custodial Office, sign the site diary and punch the timecard assigned to his contract.  After completing the assigned work, the contractor will punch their time card out.  Timecards will be crosschecked with District1200 Roadside Daily Cost Report Form documentation and invoices.

- Items, for plumbers’ helper: Use of these items will be directed by the Department.

J.	Both Buildings have an existing Occupancy Permit and they have a PA L&I Annual Permit that allows day-to-day maintenance and repairs to the system. If any additional work requires a permit, the Contractor shall coordinate with the District Roadside Specialist and the Facility Administrator for Welcome Centers and Roadside Rests. If any permits are required, the contractor shall be responsible to obtain them at no additional cost to the department.

II.	Safety Requirements

A.	All work shall be performed in a safe and orderly manner with minimum interference to persons using the Welcome Center area.  The contractor shall be aware of the latest safety regulations when entering confined areas. When working in such areas, all precautions shall be taken as required by these regulations.

##### B.	The contractor shall comply with all State and Federal laws and to OSHA Safety requirements.

III.	Non-Compliance

- If, for any reason, the contractor fails to comply with the requirements of the Contract, Section 108.90 of the current PennDOT Specifications, PUB 408 shall prevail.  If any materials or workmanship furnished by the Contractor are found to be defective, unsuitable or otherwise unacceptable, the materials shall be removed by the contractor and replaced with acceptable materials and installed anew to the satisfaction and approval of the District Roadside Specialist at cost and expense of the contractor.

- ASSIGNABILITY AND SUBCONTRACTING CLARIFICATION

The Contracting officer will not permit any Subcontracting of any contract work or the assignability in whole or part, of this contract or its rights, duties, obligations, or responsibilities.

The awarded contractor or persons in his employment shall perform all contract related work.

The contractor shall at the Departments request provide verification (certified payrolls or other information as determined by the Department) of employment for any individual who performs duties under this contract.

IV.	DISTRICT 1200 DIRECTIONS FOR PAYMENT

A.	The Contractor may invoice the Department only after acceptance of the completed contract work.

B.	The Contractor shall prepare the current version of the District1200 Roadside Daily Cost Report Form (attached to these specifications) daily, or as directed by the Department. The contractor’s representative must sign this report.  These reports will serve as the basis for payment. The original District 1200 Roadside Daily Cost Report Form (s) along with a completed Confirmation of Services Form (Form OS-501) completed by county or crew (as directed by the Department) is to be forwarded to the District Roadside Unit. The contractor should make appropriate copies for their records.

All payrolls and invoices shall be correlated with the Payment paper work and processed through the Address listed on the Purchase Order for payment. NO INVOICING IS PERMITTED PRIOR TO THE CONTRACTOR RECEIVING notification that the completed work has been accepted.

C.	Payment shall be based on the total number of verified item units worked per specification requirements as reported on the District1200 Roadside Daily Cost Report Form.

The DRS will notify the Contractor if corrections are needed.  Each Form OS-501 shall be itemized, include sufficient detail, and coordinate with the line items on the Purchase Order.  Untimely or incomplete submissions of Form OS 501 and required supporting documentation may delay processing of a “proper invoice” as required by the Payment section of the Terms and Conditions.

Invoices shall be submitted by the Contractor on a “Per approved weekly submitted OS-501 package” (with support documentation).  For further instructions regarding invoicing, see the Billing Requirements section of the Terms and Conditions.