Scope of Work

The Department of Transportation, hereafter referred to as PennDOT, requires an Electrical Contractor to provide general maintenance, inspections and repairs for our Engineering District 8-0 office located at 2140 Herr Street, Harrisburg, PA, 17103. The services provided shall meet or exceed the electrical regulations of the Pennsylvania Department of Labor and Industry and requirements, contained in the latest edition of the National Electrical Code of the National Board of Fire Underwriters. The work shall be performed in accordance with all State and Local laws, codes and ordinances which relate to the work. This contract includes but is not limited to-furnishing material, equipment and labor necessary to service, maintain, inspect, replace, repair, or relocate existing or planned electrical devices, fixtures, apparatuses and/or systems in the District Office Facility.

The contractor providing this service must meet all state and local requirements for Electrical Contracting.  All work done by this contract is to be done by a qualified electrical technician and/or an electrical helper being supervised by a qualified electrical technician. The following tasks are required for this contract.

- General Electrical Inspection:  The contractor shall make a minimum of one (1) scheduled yearly electrical inspection at the PennDOT Engineering District 8-0 office locate at 2140 Herr Street, Harrisburg, PA, 17103. This inspection shall include:

- A full color thermal inspection of all electrical equipment including; switch gear, electrical panels, and transformers.

- A visual inspection of all electrical systems, devices, fixtures and apparatuses.

- Routine Repair and Maintenance:  The contractor shall furnish the personnel, equipment, and materials to maintain, service, repair, replace or relocate existing or planned electrical devices, fixtures and apparatuses at the PennDOT Engineering District 8-0 office located at 2140 Herr Street, Harrisburg, PA, 17103.

All repairs and system upgrades shall have prior approval of the District Contract Administrator hereafter DCA.

This contract shall provide the needed repairs to any and all of the of the Engineering District 8-0 electrical system by way of part replacement or part repair as deemed acceptable by the DCA or designee.

All contractor materials and work shall be guaranteed for a period of one (1) year.

All contractor repairs shall have a written quote provided to the DCA or designee prior to any work being performed.  All quotes will be provided without charge.

A Material Contingency will be provided for each Purchase Order.

The contract period will be for less than one (1) year with the option of four (4) one (1) year renewals by mutual consent.

Requirements

- Contractor shall sign in at the Visitor Counter upon arrival during normal business hours (Monday – Friday 7:30 AM – 4:30 PM.).

- After hours Contractor shall be escorted onto and off the premises by the contract administrator or designee (Friday 4:30 PM- Monday 7:30 AM) and all Department recognized holidays:

New Year’s Day

Dr. Martin Luther King Jr. Day

President’s Day

Memorial Day

Independence Day

Labor Day

Columbus Day

Veteran’s Day

Thanksgiving Day

Day after Thanksgiving Day

Christmas Day

- All bid prices shall include all labor, equipment and mobilization. No travel time expense shall be paid.

- All materials and parts shall be invoiced at the Contractors cost plus a maximum ten (10) percent markup.

- All labor and materials shall be documented on the OS-501 (Confirmation of Service) and authorized by the DCA or designee signatures.

- All materials exceeding $300 must have prior approval by the DCA or designee.

- Call out during normal business hours (Monday - Friday 7:30 AM – 4:30 PM) Contractor shall be on site within one (1) business day.

- Call out during non-business hours (Friday 4:30 PM – Monday 7:30 AM) and all Department Holidays the Contractor shall be onsite with two (2) hours.

- Contractor shall be available 365 days a year on a 24-hour basis.

- Contractor shall be responsible for all approvals and permits prior to the start of any work by the DCA or designee.

- Contractor shall supply the name and contact number of any personnel to be contacted for non-normal hours call out.

- All permit approvals, warranties and OEM manuals shall be supplied to the DCA or designee.