SCAFFOLDING SPECIFICATIONS

PROJECT: Baylor Lake Stone Arch Repair/Preservation

Project Location: S.R. 4002 (Farnham Rd) Benton Township, Lackawanna County, PA

Project Narrative:

The Baylor Lake Stone Arch project is a preservation repair to an existing stone arch culvert at the outlet end of Baylor Lake on S.R. 4002, Farnham Road, in Benton Township, northern Lackawanna County.

Because of the historical significance of the structure (dating back to the mid-1800s) the stone arch culvert is being preserved rather than being replaced. The culvert has undergone major structural repairs over the last several years. Underpinning of the existing culvert barrel was performed and scour walls were poured to prevent future erosion of the culvert barrel. The roadway above the culvert was excavated and the structure fill removed. The spandrel walls were dismantled to expose the top of the culvert barrel. The barrel was steel reinforced and concrete encased to insure structural stability. The spandrel walls were reconstructed using the field stone recovered from the structure and dry stacked to the horizontal and vertical profile of the original culvert structure. Geosynthetic reinforced soil was used to backfill and stabilized the stone walls to the underside elevation of the culvert slab.

The remaining work on the culvert will require a scaffolding system for the entire length of each spandrel wall (approximately 75 L.F. +/- each wall). The scaffold will be utilized for personnel and materials to install deck and parapet formwork, working platform access for deck and parapet concrete pours and for installation of stone veneer on the exterior of the parapets.

The estimated start date of the project is May 13, 2019. This work is anticipated to be completed no later than October 31, 2019.

Scaffold Requirements:

Vendor to design, furnish, erect and dismantle scaffolding system for stable working access to the specific areas on both sides of the culvert for concrete formwork and stone masonry. The proposed scaffold system should conform to the following requirements, guidelines and standards:

- Conform to the horizontal contour/curvature of the existing spandrel walls.

- Scaffolding to be installed/erected to accommodate all changes in vertical topography.

- Scaffolding posts and/or end bucks to be set on base plates and/or adequate sills or pads to prevent slipping and sinking.

- Provide a 2’-0 wide continuous walkway/working platform capable of supporting a minimum 50 lb./S.F. The walkway/working platform should be unobstructed and free of any interference (e.g. end bucks) by means of cantilever frames or outriggers. Platform height to be set at 1’-0 +/- below top of the existing culvert walls.

- Provide a 5’-0 wide continuous material staging platform capable of supporting a minimum of 75 lb./S.F. at a vertical height between 2’-6” to 3’-0 above the height of the working platform.

- Scaffolding system to be compliant with all OSHA codes and standards and all state and local code requirements.

- Erection and dismantling of the scaffolding system to follow the ‘Code of Safe Practices’ developed by the Scaffolding, Shoring and Forming Institute (SSFI) and the Scaffolding Industry Association, Inc. (SIA)

- Vendor to provide a competent person for periodic (minimum once per month or as may be required) inspections of the scaffolding system for the duration of the rental period. These periodic inspections are intended to identify any settlement/instability of the system and any missing/damaged system components that may adversely affect the integrity of the system and/or jeopardize the safety of the workers utilizing the system.

- Vendor to provide price to furnish, erect and dismantle (FED) the scaffolding system for an initial period of 28 calendar days.

- Vendor will provide separate pricing for the rental of the scaffolding system for additional 28  day intervals or part there of after the initial FED period (28 days) ends.

- Vendor to provide all necessary insurances as indicated on attachment OS-52.

A copy of the ‘Final Signed Drawings’ has been included and should be considered part of the bid documents.

Vendors are encouraged to visit the project site to become familiar with site conditions prior to formulating their proposal.