Scope of Work

Pennsylvania Correctional Industries, a Bureau of the Pennsylvania Department of Corrections is establishing a Heavy-Duty Vehicle Refurbishing Plant within the confines of SCI-Forest located in Marienville, Pennsylvania. This scope of work is to cover welding equipment needed in the Welding Classroom area of the Plant.

The equipment shall conform to the requested specifications and shall be new and of good quality. All equipment shall be provided complete including freight to the Pennsylvania Plant site located at 153 Woodland Drive, Marienville, PA, 16239.

- Lincoln Electric Power MIG 350MP, Model K2403-2 or approved equal.

Package includes:

- Magnum PRO Curve 300 Gun, 15ft.

- 0.035/.045 in. (0.9/1.2 mm) Drive Rollsand Guide for Steel

- Gas Regulator and Hose

- Work Clamp and Cable

- 230V Input Cord and Plug

- 115V AC Auxiliary Power Receptacle

- Lockable Storage Compartment with Tool Tray

Bid Quantity- 4 units

- 150 Amp Air-cooled TIG Torch 12.5 ft, Model k1782-2 or approved equal

Bid Quantity- 4 units

- Foot Pedal for TIG Torch, Model K4361-1 or approved equal

Bid Quantity- 4 Units

- Tomahawk 625 Plasma Cutter with Hand Torch, Model K2807-1 or approved equal

Bid Quantity- 1 Unit

- Precision TIG 225 TIG Welder Ready-Pak With Cart, Model K2535-2 or approved equal

Package includes:

- Torch Parts Storage Compartment

- Torch Hanger

- 10 ft. (3.0 m) Work Cable & Clamp

- Removable Lift Eye

- 9 ft. (2.7 m) Input Power Cord with NEMA 6-50P Plug

- NEMA 6-50R Receptacle

- TIG Procedure Guide

- GTAW (TIG) Handbook

- PTA-17 150 amp TIG torch w/ 1 pc. cable

- 12 ft. (3.6 m) Ultra-Flex™ Cable

- Twist Mate™ Adapter

- 3/32 in. (2.4 mm) 2% Ceriated Tungsten

- Collet & Collet Body

- 7/16 in. (11.1 mm) Alumina Nozzle

- Long Back Cap

- Gas Regulator with Hose

- Foot Amptrol™ with 25 ft. (7.6 m) cable assembly (K870)

- Understorage Cart (K2348-1)

Bid Quantity- 1 Unit

- Hydroguard Bench Electrode Welding Oven, Model K2942-1 or approved equal.

Bid Quantity- 1 Unit