2020 Ford Super Duty F-650 XL 2WD Regular Cab Diesel Specifications – NO Substitute

2WD Class 6, Type 1, Regular Cab,

Dual Rear Wheel, 26,000# GVWR, Diesel Engine

Two Wheel Drive Cab and Chassis with Stake Body

Ford Truck / Super Duty F650 XL

Engine: 6.7L Power Stroke V8 Turbo Diesel - 300 HP @ 2500 RPM

700 lb-ft Torque @ 1600 RPM-inc:

Engine Exhaust Brake and Manual Regen Capability

50-State Emissions

Engine Block Heater, Phillips, 120 Volt/750 Watt

Transmission: Ford TorqShift HD 6-Speed Automatic - Double Overdrive

Wheels: Front 22.5 x 8.25 White Powder Coated Steel

Tires: Front (2) 11R22.5G Goodyear Endurance RSA

Wheels: Rear 22.5 x 8.25 White Powder Coated Steel

Tires: Rear Four 11R22.5G Goodyear G182 RSD (Traction)

Air Dryer, Bendix AD/IP w/Heater

Air Brakes - Straight Truck

8,500 lb Cap Non-Driving Dana D-850F

Taper-Leaf Springs, Parabolic - 8,500-lb Cap.

Lube, Front Axle, EmGard 50W, Synthetic Oil

Front Stabilizer Bar

21,000 lb. Single Reduction - Locking - Dana / Spicer 21060D

Multi-Leaf Springs - 19,000-lb Cap.

Shock Absorbers, Rear - Double Acting

Lube: Rear Axle, Emgard 75W-90, Synthetic Oil

5.57 Axle Ratio

200" Wheelbase/126" CA/75" AF/314" OAL

533 Single Channel - Straight "C" 10.75 SM, 80,000 PSI

Exhaust: Under Cab, Vertical Outlet, Right Side, Switchback-S

Fuel Tank - LH 50 Gallon Rectangular – Aluminum

12 Gal. Single Tank Fuel Fill. Mandatory Charge Applied

200 Amp Denso SC5 Heavy Duty Alternator

Jump Start Stud - Remote Mounted

Battery - Two 900 CCA, 1800 Total, Includes Steel Battery Box

Body Builder Wiring - At End of Frame, Separate

Daytime Running Lamps

Voltmeter

Seats: 30/70 Air Ride Driver & Fixed 2-Passenger Bench – Cloth

Preferred Equipment Package-inc:

- Bumper, Front - Black, Full Width

- Wheel Seals, Front - Oil lubricated, SKF ScotSeal

- Wheel Seas, Rear - Oil lubricated, SKF ScotSeal

- Painted Grille - Plastic

- Lights - Roof Marker/Clearance - Amber Lenses (5)

- Tow Hooks, Front (2) - Frame Mounted, Black

- Four Body Builder Switches - Mounted in Center I/P

- Floor Covering - Black Vinyl

- Intelligent Oil Life Monitor

- Steering Column - Tilt

- Steering Wheel - Black PVC w/Integral Cruise Control

Power Equipment Group-inc:

- Power Windows & Door Locks

Radio: AM/FM Stereo w/Aux Audio Input Jack & Clock-inc:

- (2) Speakers

Remote Keyless Entry w/2 Key Fobs-inc:

- SecuriLock Passive Anti-Theft System

Interior Rear View Mirror

Horn, Air - Black, Single Trumpet

Mirrors, Dual - Heated Rectangular, XL2020 - 96" Width

Pre-Delivery Inspection

Ship-Thru - NFS National Fleet Services

Paint Type - Environmentally Friendly, "3 - West System"

Stake Body with Aluminum Construction

- 16' long x 8' wide

- .156" Aluminum Diamond Plate Floor

- 4" Crossmembers on 12" Centers

- 1/2" x 3" Mounting Flats, Full Length set at 34" apart

- Oak wood fillers and tie-down bars

- 3-1/2" wide x 5-1/2" high side and end rails

- NO stake pockets

- NO rub rails

- NO bulkhead

- 1" DOT marker lights

- ICC bumper

- Spare Tire Carrier

- Red/white conspicuity tape

- Mud flaps w/anti-sail brackets in front and behind tires

Wheel: Spare 22.5x8.25 White Powder Coated Steel, 10-Hole

- Tire: Spare 11R22.5G Goodyear Endurance RSA

Aluminum Underbody Toolbox