Scope of Work

Pennsylvania Correctional Industries, a Bureau of the Pennsylvania Department of Corrections is establishing a Heavy-Duty Vehicle Refurbishing Plant within the confines of SCI-Forest located in Marienville, Pennsylvania. This scope of work is to cover equipment needed in the Metal Fabrication area of the Plant that will be utilized for the fabrication of replacement parts for snowplows.

The equipment shall conform to the requested specifications and shall be new and of good quality. All equipment shall be provided complete including freight to the Pennsylvania Plant site located at 286 Woodland Drive, Marienville, PA, 16239. Final hook up of equipment to utilities and equipment anchoring to be handled by others. Awarded vendor is responsible for machine startup, testing and demonstration. Customer will be responsible to provide the hydraulic fluid for the equipment per the manufacturers specifications.

Bidders must return with their bid a detailed equipment layout sketch and the data for utility connections (water, compressed air, exhaust air, make-up air, electric, gas etc.). Bidders must include with their bid the lead time upon receipt of a Purchase Order and cost for weekly and monthly storage of the equipment in case of construction delays. The deadline for delivery of the equipment to the Marienville location is 4/1/20

The plant has two loading docks, one with a ramp and the garage doors are 12’W x 14’H. Also available are two additional garage doors at ground level which are 16’Wx 14’H. The overhead doors being 14’ are the lowest obstruction in getting equipment to its destination.  Bidders must include pre-installation information, foundation plans for all equipment to include specifications for the anchoring hardware.  The Iron Worker, and Plate Roller must be flush mount on the floor.

This bid shall be awarded by Lots (2 Lots total):

- Lot 1 Ironworker

- Lot 2 Plate Roller

Pricing should be bid as FOB destination. Award will be made to the supplier offering the lowest price per lot.

There will be a non-mandatory site visit scheduled at SCI-Forest, 286 Woodland Drive, Marienville, PA 16239 for 10:00 on December 5th. Anyone wishing to attend the site visit must register with Timothy McKinney via phone (814-621-2110, ext 1617) or email and must complete the attached Clearance Check form. This form must be completed for anyone wishing to attend the site visit and scanned back to Timothy McKinney, @ timckinney@pa.gov by 11/25/19.

# Lot 1- One (1) New 132 TON Hydraulic Ironworker with Dual Operator Stations

# Features:

- Dual hydraulic cylinders for dual operators with two moveable foot pedals.

- Five workstations: punch, plate shear, angle shear, bar shear, notcher and press brake attachment.

- Hydraulic material hold down at shear stations

- Oversize tables with quick adjust material stops

- Worktable to accommodate and support handling of large sheets of 7GA steel

- Electronic stroke control

- Swing away material stripper

- Quick release coupler for each tool changeover

- Electric back gauge

- Material waste bins

- Safety interlock switches

- Halogen workstation light

- 15HP, 220V 3-phase operation

Punch:

- Punch Tonnage- 132

- Punching Thickness- 1.125” x 1.062”

- Punching Diameter- 2” x .625”

- Throat Depth- 16”

- Stroke Length- 0” to 3”

- Cycles/Minute- 30@15mm

- Working Height up to Die- 41.3”

Flat Bar Shear:

- Flat Bar Shearing- 18.1” x .75”

- Blade Length- 18.3”

- Angle Flange Trim- 4”

- Working Height- 30.3”

Angle Shear:

- Capacity 90 Deg.- 6” x 6” x .6”

- Working Height- 39”

Bar Shear:

- Round- 1.75”

- Square- 1.75” x 1.75”

Notching:

- Rect.Notcher (W x D x T) – 2” x 3.5” x .5”

- Working Height- 41.3”

Other Information:

- Motor- 15HP

- Weight- 9,460 lbs.

- L x W x H- 85.5” x 44” x 80.7”

- Oil Capacity- 64 Gal.

Proposals shall include the manufacturers standard warranty periods. Cost Submittal Optional Items shall include costs for extended warranties, costs for on-site training at our Marienville location and any available off-site training. Also included as an Optional Item in the cost submittal is price for awarded vendor to provide all rigging services and equipment to offload the machine at time of delivery and spot it in the plant per the Architectural drawings.

Vendors shall include their standard die package.

Motor shall not exceed 15HP, 220V 3phase.

# Make/Model Number: BAILEIGH/SW-132 or approved equal.

.

Lot 2 One (1) new Four-Roll Hydraulic Powered Plate Rolling Machine

# Standard Features:

- Induction Hardened Rolls

- Electronic Parallelism

- Digital Display

- Cone Bending Device

- Two Speed Control

- All rolls are made of special steel.

- Machine body is steel construction (ST52).

- All rollers mounted in bearing.

- Separate control panel.

- Drop-end controlled from control panel in order to release easily bended metal sheet.

- Movement and parallelism adjustment of the rollers controlled from the control panel.

- Ergonomic designed control panel which allows to control all the functions of the machine is independent from the machine.

- Central rolls are driven with hydraulic motor and reducer.

- Electrical and hydraulic protection against overloads.

- CE approved

# SPECIFICATIONS:

- Working Length	16’

- Maximum Thickness Yield Point 	36,000 PSI Pre-Bending-5/16”, Bending-3/8”

- Number of Rolls	4

- Motor HP	15HP

- Rolling Speed up to 	16’ per minute

- Top Roll Diameter	14.2”

- Pinch Roll Diameter	13”

- Side Roll Diameter	10”

- Machine Length	22’

- Machine Height	66”

- Machine Width	74”

- Machine Weight	49,600lbs.

Please provide pricing for available optional features:

Proposals shall include the manufacturers standard warranty periods. Cost Submittal Optional Items shall include costs for extended warranties, costs for on-site training at our Marienville location and any available off-site training. Also included as an Optional Item in the cost submittal is price for awarded vendor to provide all rigging services and equipment to offload the machine at time of delivery and spot it in the plant per the Architectural drawings.

Motor shall not exceed 15HP, 460V/3/60Hz.

Make/Model Number: AKYAPAK9-/AHS-5008 or approved equal.