Appendix C – Bottom Rails

| Front of Shelter L J I H G F E D K C B A 00 |
| --- |
| 8’H x 8’W x 12’L A = 3” Rail Height B = 2” Rail Width C = 54” Between Rails D = 1-1/4” Hole Diameter 6 Sets of Holes/Rail Front Edge of Rail to Front Edge of Hole: E = 15-3/4” F = 25-3/4” G = 35-3/4” H = 107-3/4” I = 117-3/4” J = 127-3/4” Overall Rail Length - 145” K = ½” Bottom edge of rail to bottom of hole. L = 92” Hole Set Spacing | 8’H x 8’W x 10’L A = 3” Rail Height B = 2” Rail Width C = 54” Between Rails D = 1-1/4” Hole Diameter 6 Sets of Holes/Rail Front Edge of Rail to Front Edge of Hole: E = 3-3/4” F = 13-3/4” G = 23-3/4” H = 95-3/4” I = 105-3/4” J = 115-3/4” Overall Rail Length - 121” K = ½” Bottom edge of rail to bottom of hole. L = 92” Hole Set Spacing | 8’H x8’W x8’L A = 3” Rail Height B = 2” Rail Width C = 54” Between Rails D = 1-1/4” Hole Diameter 2 Sets of Holes/Rail Front Edge of Rail to Front Edge of Hole: E = 1-3/4” H = 93-3/4” Overall Rail Length - 97” K = ½” Bottom edge of rail to bottom of hole. L = 92” Hole Set Spacing | 8’H x6’W x8’L A = 3” Rail Height B = 2” Rail Width C = 54” Between Rails D = 1-1/4” Hole Diameter 2 Sets of Holes/Rail Front Edge of Rail to Front Edge of Hole: E = 1-3/4” H = 93-3/4” Overall Rail Length - 97” K = ½” Bottom edge of rail to bottom of hole. L = 92” Hole Set Spacing |