SCOPE:   The vendor shall clean the commercial HVAC systems ductwork for the MHU 2nd Floor - Medical Services at SCI Rockview.

- The service must comply with the ACR 2021 NADCA standard.

- Vendor must be NADCA certified, bonded, insured for general liability and workman's compensation.

- The air system must be put under continuous negative air pressure using large vacuums while airborne contaminants are removed using high pressure air whips, scrubbers, brushes and HEPA Vacuums.

- The service must complete the process of source removal duct cleaning.

- Inspection of the work must be completed to include taking pictures/videos before and after cleaning and must be provided by vendor upon request.

- The quote must include all labor and material itemized as individual line costs.

- Work will be conducted during the hours of 2100 – 0530

- Site visit mandatory to be scheduled with CFMM3 Hayles 814-355-4874 x 208 or CFMM1 Sampsel x 467.

- Centralized Clearance checks must be submitted and cleared for all individuals entering the facility.

- Itemized tool inventory sheets submitted and approved by facility.