Specifications for Disease Sampling Trailers

- Mobile refrigerated trailer

- Suitable to be towed with a ½ or ¾ ton pickup with trailer hitch

- Brakes to accommodate travel without payload

- Trailer box approximately 16’ long x 8’ high x 6’ wide for WM (towing as w/above pickup)

- Trailer box approximately 12’ long x 8’ high x 6’ wide for SERO and SCRO

- Refrigeration to run on standard household electric (20 amps), including all cables, plugs, cords

- Audible alarm on refrigeration unit if temperature rises above threshold

- Lockable, double doors in the rear

- Panic button or bar inside door to prevent someone from accidentally being locked inside trailer

- Waterproof, textured, slip proof duty floor

- Waterproof ceiling and walls to enable washing and disinfecting

- No wood or permeable surfaces inside trailer

- Spare tire assembly

- Interior lights

- trailer frame to be galvanized instead of painted steel

- Exterior flood light lighting at rear of trailer

- Front and rear stabilizer jacks

- Ceiling-mounted Meat Rail System

  - 2 flat track rail systems

    - Positioned 9” from rear wall, 9” from side wall, and extending forward as far as possible to within 9” of front wall

    - Each flat track rail system must support 2,000lbs.

  - 30 rail trolley hooks capable of supporting 200lbs. per hook

  - Walls and ceiling capable of supporting 4,000lbs.

- Eye bolt on ceiling, centered above rear door, 9” from opening that can support 300lbs.

- Aluminum loading ramp capable of supporting 600lbs.

  - Length of 6-8’

  - Top of ramp even with floor of trailer

  - Ramp should be hook into a slot or other system to prevent tipping if weight on edge

  - Ramp storage underneath floor for transport is preferred.

Delivery

Training manuals