Attachment A - Specifications

- Trap Net Size of Barge

  - The barge should be 24 feet long by 8 ½ feet wide.

  - ¼ inch thick hall 5052 alloy for the shell.  6061 alloy 1.58in x 4in. channel will be used for framing and will be welded and bolted using 3/8in. stainless steel bolts.  The top edge will be wrapped in 1/4in x 3 in angle 6061 alloy. Each side will be plated with 1/4in x 6in flat bar near the bottom.

- Motor

  - 90 Hp prop

- Helm

  - Should be in the center stern of the boat.

- Recessed area for tanks in front of helm.

  - Two 72”x30” recessed areas in front of helm. (both areas should be side by side) Recessed areas should be 3 inches deep for Fish transport tanks

  - Drain in recessed area

- Deck surface

  - Minimum work surface of 15 feet from helm without tanks.

  - No edge on platform/edge of boat.

  - Top of deck surface no higher than 30 inches above water line.

- Canopy cover

- Bolt down a frame for a canvas cover around the helm.

- Storage area for nets and other gear

  - Dedicated area on the stern of boat for standing net storage and catch poles

- Pump on the rear of the boat

  - 1 hp 2-inch line pump. To provide water for our fish on board.  The vendor must plumb it so the fish tanks have a fresh supply of water.

- 4 dock tie downs

- Minimum 20 years of experience building barges