October 2022	ATTACHMENT “A”

## ENGINEERING DISTRICT 1200

# Specification for Pesticide Application

# Equipment and Personnel

(Which Includes Parts I, II, III, IV & V)

I.	Description

A.	This work shall consist of furnishing all specified materials, equipment, personnel, liability insurance, safety equipment and practices necessary for the professional applications of pesticides to roadsides or other areas in accordance with the PA Pesticide Act and as specified in Chapter 13.4 of the current PENNDOT Maintenance Manual, or as otherwise directed by the District Roadside Specialist (DRS).  This work will be conducted throughout the Counties as specified or required.  Four pesticide application trucks as described herein with shadow vehicles as outlined in PUBLICATION 212 & 213 (copies can be purchased from the Department or accessed on the Department Website at the address on the first page of the publication) will be required.

The Department reserves the right for an additional pesticide application unit that is equivalent to either type of the currently working units.  Payment for this unit will be at the lowest contract unit price for the same type.  This unit shall be available to the Department within thirty- (30) calendar days of a written request.

B.	The number of hours of work is dependent on satisfactory work performance, program demands and funding.  The Department reserves the right to increase or decrease the number of hours scheduled for these complements or to terminate this work for reasons as determined by the District Roadside Specialist.

C.	The pesticide program for the District is outlined on County Maps available for review in the office of the District Roadside Specialist and all inquiries relative to the technical aspects of the program shall be directed to that office.

D.	Prior to the award of contract, the contractor will be required, at his expense, to assemble his proposed equipment and personnel.  The District Roadside Specialist will review the equipment and personnel in reference to these specification requirements.

Page 1 of 16

ATTACHMENT “A”

A list of equipment modifications and additional personnel training, if needed, shall be developed. This demonstration shall take place at a time and place determined by the Department; within ten working days of the bid opening date. The DRS, according to their schedule, will make site selection. Follow-up reviews shall be conducted at the discretion of the Department; the contractor shall be notified prior to a follow-up review.

E.	By mutual consent of both parties, this contract is renewable for two additional Two-year periods.   Each renewal will receive a Four percent (4%), increase over the current unit prices. The Department reserves the right, upon notice to the contractor, to extend the term of the purchase order for up to three (3) months upon the same terms and conditions to prevent a lapse in service.

- Pre-qualification of contractors is not required.

- The contractor applicator licensing form (attachment “A” page 16 of 16) shall be completed and submitted with the contractors bid, and as otherwise indicated for the Departments review.

- Subcontracting of work to be performed under this contract will not be permitted.

- The contractor is to summit a copy of their PESTICIDE BUSINESS LICENSE and complete and return their APPLICATOR LICENSING RECORD FORM with their bid.

If you have trouble attaching your documents, please contact the Supplier Service Center at (877) 435-7363 and choose option #2. If you are still unable to upload documents and are the apparent low bidder, you can submit the required documents to the purchaser of record within two business days of a request from the purchaser for the documents.

II.	Material and Equipment

  - Pesticide concentrates required for the specified pests (weeds, brush, insects, etc.) along with the required petroleum carriers, where required, will be furnished to the contractor at the respective county maintenance garage.  The contractor shall furnish all equipment, materials, including lubricants, anti-freeze, and fuel.  The contractor’s representative and the District Roadside Specialist shall mutually agree upon the source of water used for this pesticide application.

Page 2 of 16

ATTACHMENT “A”

  - The material contingency item of this contract will be utilized for pesticides (not listed on the Department of General Services herbicide material contract and on the approved NPDES permit material list), fertilizer or other types of material or specialized equipment when necessary to complete required projects. Equipment will be paid hourly at a negotiated rate. All material will be paid for at invoice price plus 15% and documented on the District1200 Roadside Daily Cost Report Form.

  - The Department will utilize returnable / refillable pesticide material containers under this contract. The contractor shall as an integral part of this contract provide per complement the following equipment for handling of these containers as approved by the DRS:

    - A minimum of Three (3) Truck mounted container-holding brackets designed so the returnable / refillable container fits inside and remains stable under driving conditions.

    - A Permanently mounted Twelve-volt (12V) Electric material handling pump, minimum of four (4) gallons per minute (4 GPM) with pressure switch, necessary suction and discharge hose and all special connections as required.  In addition to the Pump, a hard-wired Twelve-volt (12V) connection to operate this pump shall be constructed on the truck in the container holding bracket area.

    - Up to two hand pumps for low usage product mounted on the necessary drum coupler with discharge hose.

The preferred location of the above-mentioned equipment is on the spray truck; this shall be considered during equipment preparations.

The contractor shall provide a means of safely loading these fifteen (15) gallons containers onto their equipment.

The contractor shall be held financially responsible for the care of these containers while they are in their possession.

- Liability

A.	The contractor shall provide all insurances as listed.  An insurance certificate verifying this insurance coverage shall be furnished to the District Roadside Specialist Office prior to the start of contracted operations in the District.

  - Except as otherwise herein above specified, the contractor shall also be responsible for damage claims as provided for in Section 107.14 of the current PENNDOT Specifications, PUB 408.

Page 3 of 16

ATTACHMENT “A”

  - Additional insurance certificate to indemnify and save harmless the state, the Department, and all suits, action, or claims.  Refer to Section 107.14 of the current PENNDOT Specifications, PUB 408.

- Safety

A.  The contractor shall place their company name on both sides of all vehicles used on this contract in letters at least three (3”) inches in size; also, provide, all necessary warning lights, flags; top mounted rotating amber flashing lights and signs and/or shadow vehicle.  The contractor shall exercise all precautions to minimize interference with the normal flow of traffic.  Where reasonably feasible, all pesticide application operations shall be conducted from off the traveled lanes.  All traffic control shall be in accordance with PUB 212 & 213 and any supplements.

  - A shadow vehicle will be required when applying pesticide as a moving operation along all routes.

All shadow vehicles shall be equipped with a lockable, fully enclosed storage box for pesticide storage, the minimum size of this storage box will be 48” long by 30” wide by 30” high.  These storage boxes shall be mounted on the truck bed so as the top of the box is not higher than 36” from the truck bed. These boxes are to be watertight.

This storage box shall only be used for secured storage of Pesticide Material supplied by PENNDOT or other material that the contractor is directed by PENNDOT to Purchase under the material contingency. Any additional storage that the contractor needs for additional tools, parts equipment, or other items related to performing this work shall be in addition to this requirement.

The contractor will use the appropriate shadow vehicle (s) as required by publication 213.

The contractor may use more than is required for the maintenance and protection of traffic only when this is practical due to roadway conditions; however, the Department will only pay for the item that is required.

  - The contractor shall comply with all State and Federal laws and with OSHA safety requirements.

  - Spill kit for each truck as approved by the District Roadside Specialist.

Page 4 of 16

ATTACHMENT “A”

- Non-Compliance

  - If, for any reason, the contractor fails to comply with the requirements of this contract, Section 108.09 of the current PennDOT Specifications, PUB 408, shall prevail.

  - In no case, will the complement operate when one member is missing.  The contractor shall not permit this condition to exist for more than one day in any workweek.  This contractor shall be responsible for prompt notification of the District Roadside Specialist of any absenteeism by 9:00 AM on the day of occurrence.

- Basis of Payment

Where more than one truck of a specific type is required, if all units are not working, the Department shall utilize the lowest priced unit of the same type. The contractor may utilize either piece of equipment; however, Payment for this unit will be at the lowest contract unit price for the type utilized.

INVOICE AND BILLING INSTRUCTIONS

The Contractor shall complete a Roadside Activity Report (Form M-609) in the format directed by the DRS at the completion of each day’s work.  The schedule for submission of the M-609 to the Department will be established during the pre-service meeting by the DRS.

NOTICE—IMPORTANT CHANGE IN CONTRACT ADMINISTRATION

While the Department reserves the right to request submission of the M-609 in other formats in the future as detailed below, the Department intends to replace paper Form M-609s with a mobile application (hereinafter the “application”), effective immediately for this procurement.  Any reference throughout this document to the M-609 shall mean the PennDOT Form M-609, which shall be completed by the Contractor via the Department’s application unless directed otherwise by the DRS.  To that end, the following requirements apply:

- The Contractor shall become a PennDOT Business Partner obtain credentials to utilize the application and follow the Attachment   titled “Accessing PennDOT iPad Applications for Business Partners.”  Attachment V provides guidance on registering to become a Business Partner and using the application.

- The Contractor shall be responsible for the purchase, maintenance, and operation of all hardware, including devices such as but not limited to compatible cellular telephones or tablets, necessary to utilize the application.

Page 5 of 16

ATTACHMENT “A”

- The Contractor shall submit all Form M-609s to Department via the application.

- Once registered as a Business Partner, the Contractor shall have the ability to use the application statewide for roadside maintenance work and, as directed by the Department and its authorized personnel, including without limitation the DRS, complete Form M-609 electronically, with the same binding legal effect as though certified in writing.

DISTRICT 1200 DIRECTIONS FOR PAYMENT

A.	The Contractor may invoice the Department only after acceptance of the completed contract work.

B.	The Contractor shall prepare the current version of the District 1200 Roadside Daily Cost Report Form (attached to these specifications) daily, or as directed by the Department. The contractor’s representative must sign this report.  These reports will serve as the basis for payment. The original District 1200 Roadside Daily Cost Report Form (s) along with a completed Confirmation of Services Form (Form OS-501) completed by county or crew (as directed by the Department) is to be forwarded to the District Roadside Unit at the end of each calendar week. The contractor should make appropriate copies for their records.

All payrolls and invoices shall be correlated with the Payment paperwork and processed through the Address listed on the Purchase Order for payment. NO INVOICING IS PERMITTED PRIOR TO THE CONTRACTOR RECEIVING notification that the completed work has been accepted.

C.	Payment shall be based on the total number of item hours worked per specification requirements as reported on the District1200 Roadside Daily Cost Report Form and verified via GPS report (s) and tracking.

The DRS will notify the Contractor if corrections are needed.  Each Form OS-501 shall be itemized, include sufficient detail, and coordinate with the line items on the Purchase Order.  Untimely or incomplete submissions of Form OS 501 and required supporting documentation (including M-609s) may delay processing of a “proper invoice” as required by the Payment section of the Terms and Conditions.

Invoices shall be submitted by the Contractor on a “Per approved weekly submitted OS-501 package” (with support documentation).  For further instructions regarding invoicing, see the Billing Requirements section of the Terms and Conditions.

Page 6 of 16

ATTACHMENT “A”

D. 	CLARIFICATION OF BILLABLE / NON-BILLABLE CONTRACT OPERATIONS

A.		Billable” Hours To The Department Will Include:

    - Time spent applying pesticides as directed.

    - Filling tanks with water at Department facilities, or from bodies of water within the boundaries of the PennDOT District 12-0 region and/or at other approved sites within the PennDOT District 12-0 region.

    - Acquiring, loading, and mixing pesticide concentrates within the PennDOT region 12-0 boundaries.

    - Routine calibration of equipment which is required in Attachment “A” section XVIII.

    - Meeting with Department representatives in the field other than the pre-season meeting as described in Attachment “A” section XII.

    - Minor equipment repairs not to exceed 15 minutes per occurrence and not to exceed a total time of 30 minutes per day.

    - Time spent traveling from one work location to another work location or “deadheading” during the course of the workday.  Deadheading shall be minimized and if, in the DRS’s opinion, this is being abused by a spray crew, billable hours may be reduced, and the crew may be suspended from further work.

    - Reasonable time spent for crew bathroom breaks.

    - When directed by the DRS, up to 1 hour to flush the spray system when switching between spraying programs.

    - When directed by the DRS, up to 1 hour to complete the set-up of equipment for a different spray program other than in the pre-season meeting as described in Attachment “A” section XII.

    - Reasonable time spent completing required M-609 documentation while in the field and the District1200 Roadside Daily Cost Report Form.

    - Reasonable time spent completing required maps while in the field.

    - Reasonable time spent contacting individuals on the hypersensitivity list while in the field. Document you call history including time spent completing call or other communication format in the comment section of the M-609 for that day’s work.

B.		Non-Billable” Hours Will Include But Not Be Limited To:

1	Travel to the work site or county office before the start of work.

2.	Travel from the work site to the crew’s home base at the end of a workday.

a.	For 1 and 2 above, approximately 15 minutes’ leeway will be given prior to the start of work and the conclusion of work from the start and stop GPS locations for the set up to begin work and ending work including necessary paperwork.

Page 7 of 16

ATTACHMENT “A”

3	Equipment failure lasting more than 15 minutes or more than two occurrences of 15 minutes during the workday.

4.	Lunch breaks.

5.	Crew foreman is responsible to review weather prior to start of workday. Waiting for roads or vegetation to dry in the morning after arriving to the work area and finding it to be too wet to work or after rainfall during the workday.

6	Filling tanks and mixing/loading at locations not approved by the DRS or outside of the PennDOT 12-0 boundaries.

7.	Contractor initiated safety inspections of crews during the workday.

8.	Filling out and completing any paperwork for the contractor’s organization that is not required by the Department.

C.	Filling of Spray tanks at Department Facilities

1.	When Filling at Department Facilities billable time is capped by the requirements of Attachment A Part I paragraph E.

2.	Travel time from Department facility to assigned program area if it exceeds Attachment A Section VI Subsection D Paragraph B item 2. A.

VII.	Contract Administration

The Contractor shall assign one person as the Departments sole contact person for all contract related activity. This person will be the District Roadside Specialists contact person for all scheduling, programming, and other related contract activities. This person shall have the authority to make all contract related decisions and other contractor personnel shall not change these decisions.

The contractor shall notify the District Roadside Specialist in writing of any change of status regarding this position.

###### VIII.	General Equipment Requirements

The Contractor shall provide all equipment utilized on this contract in sound

mechanical condition, good working order, with a uniformly painted neat and clean appearance.

The contractor shall notify the District Roadside Specialist of all equipment related lost working time.

The contractor shall repair all minor equipment malfunctions within forty-eight hours of their occurrence.

Page 8 of 16

ATTACHMENT “A”

Once the Department has calibrated Spray trucks, the contractor shall notify the Department of any repairs or changes to the Computer flow control system prior to returning to any Department funded work.

The contract Administrator shall notify the District Roadside Specialist of any major equipment malfunctions upon their occurrence and provide a timetable for the repair. The contractor then must have the equipment back into service by the agreed upon time.

Failure to provide repaired equipment within the set time frames may result in program (s) scale back or elimination and entry into the contractor responsibility data base and not in compliance with specifications.

The Department reserves the right to remove unreliable equipment from this contract and the contractor shall replace the unreliable equipment with equipment that meets the requirements of these specifications. This replacement shall occur within five calendar days of the Departments’ request; if replacement does not occur, the contractor may be entered into the contractor responsibility data base as not in compliance with specifications. The Department shall determine a piece of equipment unreliable upon the second occurrence of the contractor’s failure to repair equipment in a timely manner.

During the pre-award equipment inspection, the DRS may reject or state specific corrections to equipment based on their review.

###### IX.		Hours of Work

Each week the Department expects forty hours of production work per application crew.

The Department is aware of time and equipment constrains in the chemical application area of the Vegetation Management industry. The contractor shall be permitted to work an extended workday, providing that, the quality and quantity of work delivered during the extended workday is acceptable to the Contracting Officer or his designate and it is in the best interest of the Department.

The Department reserves the right to limit the workday to eight hours if the Contracting Officer or his designate believes it is in the best interest of the Department.

In the event of programming needs, weather conditions or major equipment malfunction that affects the application timing of the herbicide programs, the contractor at the Departments discretion shall be required to work more than the normal forty-hour work week. This shall require an extended workday and up to a six-day workweek. This additional work shall be paid at the normal contract unit prices.

Page 9 of 16

ATTACHMENT “A”

# X.		Contract Personnel Retention Requirements

Certified Commercial pesticide applicators assigned to this contract shall not be replaced, unless authorized by the DRS, during the duration of the contract and its renewals so long as the contractor employs them in an applicator position.

XI.		Documentation Requirements / Schedule

The following information shall be supplied to the DRS prior to April 01 of each pesticide application season:

    - A Revised Contractor applicator licensing form for the new season.

    - Complete Cell Phone Telephone Number list, listing all contract personnel: including applicator name, county of operation and truck assignment.

    - Contractor contact personnel including the contractors Contract Administrator, Invoice Personnel And Emergency Contacts; include all applicable telephone numbers and E-mail addresses.

    - A copy of your current Pennsylvania Department Of Agriculture (PDA) “PESTICIDE APPLICATION BUSINESS LICENSE” and a copy of valid applicator licenses for each assigned applicator.

XII. 	 	Meeting Attendance and Start-Up

The contractors’ applicators shall attend the Districts annual pesticide-training seminar held each year. Meeting Attendance shall be considered an integral part of this contract and no payments will be made to the contractor for this required attendance.

In addition, all contract personnel shall attend the District 1200 spray season kick-off meeting; this meeting shall be limited to four (4) hours maximum and be followed by spray season start-up / calibration. Meeting Attendance shall be considered an integral part of this contract and no payments will be made to the contractor for this required attendance. After conclusion of District 1200 spray season kick-off meeting, and only after successful calibration of the spray truck will Department paid time begin. If any truck does not properly calibrate, as Determined by the Department, no payment will be made. Calibration will be rescheduled and only after the truck property calibrates will it be released for work paid by the Department.

The Department reserves the right for one additional seasonal meeting for up to four hours for all contract personnel, this meeting will be an integral part of this contract and no payments will be made to the contractor for this required attendance.

Page 10 of 16

ATTACHMENT “A”

###### Cellular Telephone Requirements / Restrictions

###### &

###### Truck-To-Truck Communication

The Contractor shall provide for their contract administrator and each application complement an unrestricted cellular telephone (with telephone numbers available to all crewmembers for family emergencies) as a means of communication with the District Roadside Specialist.

Each application crew must call the District and/or the county office every morning to report work locations.

Crewmember Personal cell phones shall not be in an “on” status in any contract application equipment during hours of work paid by the Department.  The Contractor’s management and supervision is responsible for enforcing this provision. The contractor supplied cell phone should be sufficient for any needed emergency communication between the Department, contract personnel, the contractor’s office or for family emergencies.

A permanently mounted system of truck-to-truck communication shall be provided in all vehicles utilized on this contract; this may be CB radio, or another type system as approved by the District Roadside Specialist.

If the contractor uses their own radio system, one portable handheld unit shall be available for the Departments use when required.

XIV.	Special Requirements

The Department reserves the right to have any contractor employee removed from this contract when it is in the best interest of the commonwealth.

Equipment assigned to this contract once contractually inspected and approved shall continue in its assigned location. When equipment is rotated due to traffic safety requirements, the approved equipment shall return. The contractor may request the Department to contractually inspect

additional pieces of equipment; these additional inspections will be done according to the availability of the District Roadside Specialist. No uninspected equipment shall be permitted.

Page 11 of 16

ATTACHMENT “A”

XV.	Other Work

Spray trucks assigned to this contract shall not perform other work outside of this contract unless released by the DRS. Prior to being released by the Department the contractor shall transfer all mixed material and return all unmixed material to the Department as directed by the DRS; this shall be done completely at the contractors’ expense.  Upon return all tanks shall be empty and cleaned. The spray truck shall have all application equipment adjusted as it was prior to leaving and be properly calibrated before returning to the District program. The Department reserves the right to inspect, adjust or calibrate the unit prior to it returning to Department paid status.

XVI.	GPS Location and Monitoring System

All vehicles delivering pesticides used with Parts I, and II, shall be equipped with, at the contactors expense, a real-time GPS (Global Positioning System) Location Verifying Unit Receiver Signal System to record the location of the spay vehicles using GPS satellites.  The spray vehicle computer and GPS Location Verifying Units shall be supplied, maintained, and installed by the contractor, at their expense, for the duration of the Purchase Order. The GPS Location Verifying Units system shall be capable of real-time and historic tracking of all spray trucks at the same time collectively or individually.  The Department reserves the rights to download any stored or recorded information within the vehicles spray monitoring or location monitoring units at any time during the term of the Purchase Order.  The contractor is responsible for providing The Department with a website access location to view the GPS location, of any

spray truck, at any time, in real-time.  The website shall be compatible with

Google Chrome and Microsoft Edge and newer versions and be compatible with Smartphone’s using the iPhone, Android, and Windows Systems.

The GPS Units should be capable of accuracies of ten to fifteen meters uncorrected and five meters when differentially corrected.  The mobile units must contain a data dictionary capable of collecting and delivering a summary of each day’s activities in the form of a printed-out report and map which will be correlated with the form M-609 and used as a basis of payment for work performed. This summary must be submitted to the District Roadside Specialist each day work is completed.  The GPS unit printed reports submitted must show the following information:

Page 12 of 16

ATTACHMENT “A”

    - State Routes traveled.

    - Locations along the traveled state routes.

    - Direction of travel along the state routes.

    - Location and time correlated.

    - Contract name, date, and applicators name.

This information must be formatted into a file format compatible with the Department’s existing software.  The contractor will be required at their expense to provide all necessary software to provide the above-mentioned data.  This material will be supplied by the contractor and shall include the following:

- Tracking Units.

- GPS antennas.

- Power cords.

- Download cables.

- Mapping software.

XVII	PENNDOT’S NATIONAL POLLUTANT DISCHARGE ELIMINATION SYSTEM PERMIT (NPDES PERMIT NO: PA0270792) REQUIREMENTS

Satisfying National Pollutant Discharge Elimination System Permit # PA0270792 (NPDES PERMIT NO: PA0270792) regulations, Record Keeping, by documenting contractor herbicide work.

NPDES PERMIT NO: PA0270792 (including Renewals or Replacement Permits) Requirements are made a part of this contract.

XVIII.    All spray equipment shall be calibrated a minimum of one time each week and at the beginning of a new spray program.  All spray equipment shall also be calibrated upon starting work in a different County; except when doing same program main roadway work in multiple counties in the same day.  Calibrations shall be documented on the days M-609 Application.

If spray equipment fails to calibrate within the first fifteen minutes, the applicator shall notify the District Roadside Specialist immediately.

Page 13 of 16

ATTACHMENT “A”

XIX.	LIST OF SPARE PARTS AND TOOLS REQUIRED FOR EACH SPRAY TRUCK

- Two (2) translucent 5-gallon buckets with 0.25-gallon graduations.

- One (1) 128 fluid ounce liquid measure measuring pitcher with graduations of 2 ounces marked on the pitcher

- One (1) 64 fluid ounce liquid measure measuring pitcher with graduations of 2 ounces marked on the pitcher

- All personal protective equipment as required by the pesticides being applied.

- Guiderail Application System:

- Two (2) spare nozzles of each design type and size of each type used including the nut:

  - Off Center Nozzles that must be available

    - OC20

    - OC30

    - OC40

    - OC60

    - OC80

  - One ¾ Inch Nozzle body with cap nut

- Nutating Application Spray System:

- Two (2) spare nozzles of each design type used

- One extra set of nozzles for Boom #7 & #8 that are double    	the flow capacity of the existing nozzles.

- Three (3) Spare 90-degree elbows of each design used in the application head

- One (1) set of large channel lock type pliers to address system strainers

- Two (2) Pipe wrenches: one (1) - 14” inch and One (1) - 12” pipe wrench

- Two (2) Adjustable crescent wrenches: one 15”and one 10”

- Two (2) Philips’s screw drivers

- Two (2) standard screw drivers

- Four (4) worm gear type hose clamps to fit each type of hose size

- One (1) large funnel

- A spill kit of sufficient size to effectively contain a spill based on the size of the tanks

- Fire extinguisher / First aid kit / Eyewash

- Nut drivers and wrenches of various sizes to adjust or remove nozzles and hose clamps

- Two extra check valves of the same design used on the truck

- Small assortment of commonly used pipe fittings, hose bibs, quick couplers ETC…

Page 14 of 16

ATTACHMENT “A”

XX.	A spill response and adverse incident response plan developed by the contractor in accordance the most current PennDOT NPDES permit to include:

- Background and applicable regulations.

- Incident reporting chain of command.

- Spill preparedness checklist.

- Spill response/control methods.

- Spill response procedures.

XXI. Contractor Equipment Storage

Storage of contractor equipment during non-working hours shall be the responsibility of the contractor. Parking of contractor equipment in Department facilities will only be permitted with management approval. That approval may change at any time due to the needs of the Department or other circumstances.

This is a district wide procurement and permission to park in a County or a particular County stockpile does not give permission to park in other stockpiles within the same County or other counties within the District.

Page 15 of 16

ATTACHMENT “A”

CONTRACTOR APPLICATOR LICENSING FORM

Pennsylvania Pesticide Business License Number________________ List all current Certified Commercial Applicators names and license numbers in the table below and return it with your bid: In Addition, Enclose With Your Bid, A Copy Of Your Current Pennsylvania Department Of Agriculture “PESTICIDE APPLICATION BUSINESS LICENSE”.

| NAME Last First M | LICENSE NUMBER | CATEGORIES | EXPIRATION DATE |
| --- | --- | --- | --- |

CONTRACTOR SIGNATURE				DATE

## Page 16 of 16

Attachment “A”

Part I

The Department of Transportation’s desire is to utilize a tank mixed pesticide application unit with computer flow control, with an additional optional use positive displacement pressure side single injection unit.  This unit shall be capable of independent pattern control of an eight pattern Nutating Spray Head with a two (2’) foot to thirty-two (32’) foot wide no streak pattern. The flow control system shall utilize all factory systems for injection and boom control. Two trucks of this design will be required.

II.	Equipment Requirements: Truck, Tanks and Pump

A.	One (1) truck of sufficient size to legally haul all required equipment and supplies:  truck bed for sufficient size to accommodate sprayer(s). All equipment shall be in accordance with Attachment “A”, Section VIII.

All equipment must have a current Pennsylvania Pesticide Application Business License number on the side of the vehicles.  A copy of the Business license shall be on file in the District Roadside Specialist office.

This work will require a 1000 gallon or larger capacity truck mounted sprayer with independently separate, (free standing and not connected) dual tank capability.  The smaller tank will have a minimum capacity of 200 gallons and a maximum capacity of 300 gallons. The large tank shall be designated as Tank #1 and the smaller Tank shall be designated Tank # 2 regarding all labeling.

Both tanks will be equipped with mechanical or hydraulic agitation, a bottom sump from which the pump influent line (the line that connects the tank to the suction side of the pump) shall connect. Tanks of a manufactured design that have self-supporting feet shall have an agitation system that directs internal agitation into each supporting Foot of the tank to prevent the buildup of chemical residue or other residue from accumulating.

All valves used to shut off system flow at tanks, solenoid valves and other areas of the system shall be quarter turn one way ball valves.

Valves used to divert system flow downstream of the solenoid valves may be two- or three-way valves.

.

Page 1 of 8

Attachment “A”

Part I

All valves on the spray truck shall be permanently labeled to indicate their operational function

The pumping system shall be of a high volume-low pressure design powered by a minimum twelve (12.0) horsepower engine with an in cab electric starting system equipped with an emergency kill switch. The System shall be in sound mechanical condition with working factory muffler system and a pump to engine pulley ratio producing a system capable of discharging the required quantity of spray mixture at the specified pressure.

An in-line filter with interchangeable manufactures recommended mesh size screens shall be installed between the tank and pump. Mesh screens of 30, 50, 80 and 100 mesh shall be on each truck.

The pump return line to the tank shall be of the same size as the pump effluent housing. A metal ball valve and a liquid filled system pressure gauge, approved by the Roadside Specialist, shall be installed using metal pipe in the return line as close to the pump effluent housing as possible for regulating and reading pressure.

All plumbing shall be assembled to function as recommended by the Nutating spray head manufacturer and the computer flow control system manufacturer.

The spray unit shall have at least one hose connection point that is independent of the computer flow control and injection systems. This port is to be used for handgun spot treatment in conjunction with the other application systems.

Pesticide Storage Container:  A lockable, fully enclosed storage box for pesticide storage, the minimum size of this storage box will be 48” long by 30” wide by 30” high.  These storage boxes shall be mounted on the truck bed so as the top of the box is not higher than 36” from the truck bed. These boxes are to be watertight.

This storage box shall only be used for storage of Pesticide Material supplied by PENNDOT or other material that the contractor is Directed by PENNDOT to Purchase under the material contingency. Any additional storage that the contractor needs for additional tools, equipment, parts, or other items related to performing this work shall be in addition to this requirement.

Page 2 of 8

Attachment “A”

Part I

Equipment Requirements: Sprayer Control System

B. 	Unit to be equipped with a sprayer control system capable of; automatically maintaining application rate, a vehicle speed sensor which is a radar type sensor, a minimum of ten separate boom widths; two different application ratios and a manual setting for spot spraying. This system shall also be integrated with a positive displacement; pressure side single injection unit, with a chemical injection tank, injection tank capacity minimum of twelve (12) gallons and a maximum of twenty-five (25) gallons. The injection unit shall be operated by a single switch to engage or disengage the injection system to be able to inject under normal spray operational conditions and speeds.

The sprayer shall be equipped with manufacturer recommended solenoid valves regulators and a manual Shut off valve preceding the solenoid to individually control each of the required ten (10) spray boom width.

Equipment Requirements: Rear Mounted Fixed Nozzles

C. 	 A nozzle system for applying non-selective herbicide to guiderail and other areas as directed by the District Roadside Specialist.  This system shall contain a check valve on each individual nozzle assembly immediately preceding that

nozzle assembly. This system shall be capable of simultaneously spraying both the guiderail and the roadway shoulder. This system shall be permanently mounted on both sides of the application unit with both sides able to be operated simultaneously.

All Guiderail and Shoulder Nozzle Assemblies shall be adjustable both in and out, up, and down along both the vertical and horizontal axis’s utilizing square tubing of appropriate sizes that one square tube tightly fits inside of another, while still retaining the ability to be moved freely, with lockable adjustments and must be able to remain in a steady and stable position while driving. Each nozzle assembly must be designed to overlap each adjacent nozzle. Any nozzle break-away system proposed by the contractor shall be approved by the District Roadside Specialist prior to final equipment inspection.

The Guiderail Nozzle Application System shall be constructed of solid metal pipe and pipe fitting and permanently attached to the square tubing. The system is to utilize two nozzles pointed toward the Guiderail using ¾ inch nozzle body assemblies that can be set at up to 70° degrees from a point that is perpendicular to the direction of travel (allowing up to 140° between nozzles), to provide coverage inside and behind guiderail posts and be capable of spraying an eighteen to thirty-six-inch-wide pattern. These nozzles shall be fixed mounted with no movement that will affect the spray pattern from bounce or distortion. All outside Guiderail Nozzle assemblies shall be capable of extending out from the side of the truck at least eighteen inches (18”).

Page 3 of 8

Attachment “A”

Part I

The Shoulder Nozzle Application System shall be constructed of solid metal pipe and pipe fitting permanently attached to the square tubing to utilize four (4) three-quarter inch (¾”) nozzle body assemblies. Each nozzle assembly shall spray an eighteen to thirty-six-inch pattern behind the truck to completely cover the area between the left and right guiderail application nozzles

Each truck shall have at least one spare set of adjustable bars for the outside guiderail nozzles to facilitate field repairs if needed during a workday. If the spare set is utilized, it shall be replaced within forty-eight hours.

Equipment Requirements: Nutating Spray Head

D.      The herbicide application unit is to be equipped with an eight (8) boom Nutating spray head, capable of delivering a no streak pattern of two (2) feet to thirty-two (32) feet using all brass or stainless-steel nozzles. All booms shall operate independently

or simultaneously to apply the necessary spray widths as needed.  The application system shall have an oscillating motion on booms one through four; these nozzles must be electrically driven by a 12-volt system. The unit to provide a uniform spray pattern while providing spray drift control. The Nutating Spray Head shall be capable of applying thirty-five gallons per acre at vehicle speeds of up to 11 miles per hour.

The Department reserves the option to request additional nozzles to reconfigure patters for special applications. The contractor will be given a minimum of two weeks’ notice of any additional nozzles required.

Sprayer to be equipped with various size orifice nozzles for all application devices and include the spare nozzles and caps listed in Attachment A section XIX.

## The Nutating spray head shall be capable of mounting on each side of the truck bed according to the manufacturer’s instructions. The mounting point shall be at a point half the length of the total truck bed length. The hoses providing material to the Nutating spray head shall be no larger than one-half inch (½”) diameter.

The Nutating spray head is to be equipped with remote controlled swing (in – out); when constructed the (in) setting of the spray head shall face the rear of the spray vehicle, minimum rotation 90 degrees (90°) and an (up – down) movement, minimum of 30 degrees (30°). All required spray head movement shall be controlled from the applicators seat through electrical or hydraulic controls.

Page 4 of 8

Attachment “A”

Part I

Equipment Requirements:  Refill Pump and other

E.	Auxiliary refill system shall include a separate refill pump with adequate check valves, suction line (pump influent) shall be a minimum of 20’ in length and the same size of the pump influent housing, capable of refilling tank(s) (1000 Gallon) from roadside streams in 30 minutes or less. Refill time includes set-up and tear down of pump and hoses. Pump effluent hose shall be at a minimum the same size as the pump effluent housing and a minimum of 25’ in length. Metal pipe tank fill tubes of the same size as the refill pump effluent housing shall be permanently mounted on the spray truck for all tanks and shall be constructed as to have a visual air gap (minimum air gap six inches) between the end of the fill tube and the tank opening.

One Birchmeier BCS backpack or equivalent backpack spray unit shall be available at all time as an integral part of complement operations, an additional Birchmeier BCS backpack or equivalent backpack spray unit shall be supplied during low volume applications for each person on the spray crew. All backpacks shall be equipped with quick couple devices to be able to switch between three application devices. One each for low volume foliar, low volume Basal and the general use wand supplied with the backpack.

Low volume foliar Application: Capable of instantaneously switching between a minimum of two different application patterns

Low volume Basal application: Ultra-low volume wand 24” length with shutoff in unit tip

Incidental equipment and tools required shall include, but not be limited to two hundred feet of PVC/ POLYURETHANE blended core Double nylon braid 1/2" Electric reel mounted hose with a 600-pound pressure rating, wands, handguns and booms for special projects, pressure nozzles with orifice size calculated for specific operation.

Handgun Requirements:

Handguns Shall be capable of variable patterns; (Gun 1 from a wide cone angle spray to a straight stream spray) utilizing handgun trigger in a one hand motion.

Gun 1 Quantity one (1) Per Complement: Handgun Reference TeeJet GunJet Type 43L with extension length of 13" or 22" with Orifice Disc's D6 - 1.3 Gallon per minute (GPM) and D8 - 2.5 GPM.

Gun 2 Quantity One (1) minimum per contract or quantity needed to simultaneously maintain field operations: Reference TeeJet GunJet Type 43LC-1/2 equipped with extension of appropriate length and able to be fitted with ¾ inch nozzle body assemblies to utilize Guiderail OC nozzles.

PENNDOT Contractor Administrator approved equals are acceptable.

Page 5 of 8

Attachment “A”

Part I

III.	Personnel Requirements

A.	Certified Commercial Pesticide Applicators

Certified Commercial pesticide applicators assigned to this contract shall not be replaced, unless authorized by the DRS, during the duration of the contract and its renewals.

Two (2) persons are required with this item.  The applicator shall possess a current Pennsylvania certified commercial applicator’s license with valid certification in categories 10 and 23.  A copy of each applicators license shall be on file in the District Roadside Specialist office prior to the start of spraying operations. The applicator must demonstrate the ability to operate, calibrate and perform field maintenance on all equipment associated the spraying complement.

The Certified Applicator on this complement shall be responsible for the following:

1.	Varying the rates of application based upon all site conditions such as spray material, pest being controlled, weather, speed of equipment, wind speed, direction of traffic and other factors in accordance with the product label.

2.	The daily recording on County Maps (supplied by the District Roadside Specialist) of routes completed, water fill sources discovered, and the scheduling of pesticide spraying within the individual county as coordinated with the District Roadside Specialist and County Maintenance Manager.

3.	Reviewing work with the County Maintenance Manager or District Roadside Specialist, prior to working in a County, and resolving the sequence of pesticide application; the routes or areas to be treated and respective traffic controls and protection equipment and devices required.

4.     The Certified Applicator doing the actual application shall have a complete understanding of the procedure for reporting work using the electronic M-609 process. An understanding of the Departments Roadway Management System (RMS) for documentation purposes in the M-609 system.

5.	The Department will continue to utilize the “Right Turn System” while performing this work. The applicator shall have the total ability to understand and document within the RMS system and perform this project with as little “dead heading (driving on Department Paid time while not applying herbicides) as possible. Excessive dead heading will not be permitted.

Page 6 of 8

Attachment “A”

Part I

6.		The Certified applicator is required to do the Pesticide application. Intermittent application by Non-certified individuals will be permitted under this procurement by PENNDOT for training purposes only. When this occurs, it shall be documented as required by Recordkeeping requirements in PDA title 7 chapter 128.35.

7.	The Certified applicator is required to review daily Weather and understand the District work rules as identified at the District 1200 spray season kick-off meeting.

8.	A complete understanding of the Pesticide products used in the Districts Herbicide program.

B.	Spray Truck Driver and Field Repairs

The spray truck driver shall meet all licensing requirement and can operate the spray truck is close proximately to fixed objects within the highway right-or-way for extended periods of time.

At least one (1) member of the crew must possess knowledge and ability to maintain and make field adjustments to the equipment in order to attain a continuous and productive operation.  Assigned personnel must possess technical ability to distinguish between desirable and undesirable vegetation as specified by the District Roadside Specialist.

C.

Worker Protection Act

Pursuant to Executive Order 2021-06, Worker Protection, and Investment (October 21, 2021), the Commonwealth is responsible for ensuring that every Pennsylvania worker has a safe and healthy work environment and the protections afforded them through labor laws. To that end, contractors and grantees of the Commonwealth must certify that they are in compliance with all applicable Pennsylvania state labor and workforce safety laws. Such certification shall be made through the Worker Protection and Investment Certification Form (BOP-2201) and submitted with the bid, proposal, or quote.

## Page 7 of 8

Attachment “A”

Part I

IV.	Training Requirements

Certified Commercial Pesticide Applicators

Training of all contractor applicator personnel in computer flow control programming, adjustment, troubleshooting and operation, spray head set-up/ nozzle adjustment, proper calibration and material mixing is mandatory.

The Department reserves the right to question applicators, either verbal or written, on the proper use of the required spray equipment, the contractors contract administrator may be present; but will not assist the applicator in answering. An applicators failure to properly set up and calibrate their equipment shall result in their removal from all application work on a spray unit until they demonstrate to the DRS that their ability has increased to an adequate level.

## Spray Truck Driver

Training of contractor’s drivers to read and understand the Departments maps which use the Roadway Management System in regard to The State Route (SR’s) system and measurement of SR’s in the segment / offset system.

## Page 8 of 8

Attachment “A”

# Part II

I.	 Overview

The Departments desire is to utilize a smaller version of the same type Equipment and Personnel as specified in Attachment “A” Part I.

This complement type will be used for routine work as well work in high traffic small workspace areas.  Two (2) trucks of this design will be required.

II.	Equipment Requirements

- One (1) truck of sufficient size to legally haul, but not oversized as to defeat the intent of the smaller design, all required equipment and supplies: truck bed of sufficient size to accommodate sprayer(s) and storage box. All equipment shall be in accordance with Attachment “A”, Section VIII.

The Spray unit shall be Equipped with a 500 to 525-gallon capacity spray tank, with all equipment as specified in Attachment “A” Part I.

B.	Two Birchmeier BCS backpack or equivalent backpack spray unit shall be available at all time as an integral part of complement operations, an additional Birchmeier BCS backpack or equivalent backpack spray unit shall be supplied during low volume applications for each person on the spray crew. All backpacks shall be equipped with quick couple devices to be able to switch between three application devices. One each for low volume foliar, low volume basal and the general use wand supplied with the backpack.

Low volume foliar application: 		Capable of instantaneously switching between a minimum of two different application patterns

Low volume basal application: 	Ultra-low volume wand 24” length with shutoff in unit tip

C.       Pesticide Storage Container:  A lockable, fully enclosed storage box for pesticide storage, the minimum size of this storage box will be 48” long by 30” wide by 30” high.  These storage boxes shall be mounted on the truck bed so as the top of the box is not higher than 36” from the truck bed. These boxes are to be watertight.

This storage box shall only be used for storage of Pesticide Material supplied by PENNDOT or other material that the contractor is Directed by PENNDOT to Purchase under the material contingency. Any additional storage that the contractor needs for additional tools, equipment, parts, or other items related to performing this work shall be in addition to this requirement.

Page 1 of 2

Attachment “A”

# Part II

III.	Personnel

- Two (2) people will be required with this item; one person must possess a current Pennsylvania certified commercial applicators license with valid certification in categories 10 and 23.

- The applicator shall have the same responsibilities as listed in Attachment “A”, Part I, Section III, Paragraph A1.

The Driver, in addition to Attachment A Part I Section III paragraph B, must, at a minimum be a pesticide application technician with the required training in low volume basal, low volume foliar, and general-purpose applications and equipment use.

- A copy of Department of Agriculture technician registration card shall be required prior to start of work for any Registered Technician working on this contract.

IV.	Training Requirements

Certified Commercial Pesticide Applicators

Training of all contractor applicator personnel in computer flow control programming, adjustment, troubleshooting and operation, spray head set-up/ nozzle adjustment, proper calibration and material mixing is mandatory.

The Department reserves the right to question applicators, either verbal or written, on the proper use of the required spray equipment, the contractors contract administrator may be present; but will not assist the applicator in answering. An applicators failure to properly set up and calibrate their equipment shall result in their removal from all application work on a spray unit until they demonstrate to the DRS that their ability has increased to an adequate level.

## Spray Truck Driver

Training of contractor’s drivers to read and understand the Departments maps which use the Roadway Management System in regard to The State Route (SR’s) system and measurement of SR’s in the segment / offset system.

## Page 2 of 2

## Attachment “A”

Part III

I. 	Shadow Vehicles

Shadow Vehicle - A vehicle positioned within the activity in advance of the workspace and work vehicles. The primary purpose of the shadow vehicle is to provide advance information to approaching drivers while protecting workers and work vehicles. Any vehicle can be used as a shadow vehicle as long as it is equipped with a flashing, oscillating, or revolving yellow light which is visible from any direction (360° visibility) and is not being used as a work vehicle. The yellow light must be activated within an active work zone.

The following conditions apply to shadow vehicles used on freeways and expressways

1.	Shadow vehicle 1 & 2, as identified in PATA 600 Series shall be equipped with a Truck Mounted Attenuator (TMA) rated for the work zone.

2.	Shadow Vehicles equipped with a Truck Mounted Attenuator as stated in Publication 213: Definition Section.

Truck Mounted Attenuators (TMA) - Shall be mandatory for placement on shadow vehicles utilized on freeways and expressways, including exit and entrance ramps. The TMA is optional on all other highways. When a TMA is used, the weight of the shadow vehicle must be greater than the minimum weight specified by the TMA manufacturer.

3.	WHILE DOING WORK ON THE FREEWAY AND EXPRESSWAY; ENTRANCE AND EXIT RAMPS; one Truck Mounted Attenuator shall be required. Since driving between interchanges at normal highway speeds is routine in this operation the Department is specifying that a towable style attenuator that can travel at normal highway speeds be required. This Shadow Vehicles equipped with a towable Attenuator shall meet the requirements for TMA as stated in Publication 213.

II.	Personnel

One person is required with each vehicle used under this item.  The driver will possess a current driver’s license with all required endorsements as required by the current laws.

## PAGE 1 0F 2

## Attachment “A”

Part III

III.	Equipment Requirements

- One (1) truck of sufficient size to haul legally all required equipment and supplies:  All equipment shall be in accordance with, Section IV; paragraph “B” and Attachment “A” Section VIII.

- Seating space within the cab shall be provided for a Department Inspector if assigned to this operation.

IV.	Availability of equipment

This equipment shall be available within forty-eight (48) hours of verbal notification to the crew foreman.

## V.	Material Storage Box

All shadow vehicles shall be equipped with a lockable, fully enclosed storage box for pesticide storage, the minimum size of this storage box will be 48” long by 30” wide by 30” high.  These storage boxes shall be mounted on the truck bed so as the top of the box is not higher than 36” from the truck bed. These boxes are to be watertight.

Page 2 of 2

Attachment “A”

Part IV

I. I.	Shadow vehicles

A.  Shadow Vehicle - A vehicle positioned within the activity in advance of the workspace and work vehicles. The primary purpose of the shadow vehicle is to provide advance information to approaching drivers while protecting workers and work vehicles. Any vehicle can be used as a shadow vehicle as long as it is equipped with a flashing, oscillating, or revolving yellow light which is visible from any direction (360° visibility) and is not being used as a work vehicle. The yellow light must be activated within an active work zone.

B. This vehicle shall be equipped as Stated in “Work Zone Traffic Control Guidelines” Publication 213 PATA 300 series: Conventional highways – Mobil Operations.

C. All Shadow Vehicles shall be equipped with Flashing arrow panel in the appropriate mode.

II.	Personnel

One person is required with this item.  The driver will possess a current driver’s license with all required endorsements as required by the current laws.

III. 	Equipment Requirements

A.	One (1) truck of sufficient size to legally haul all required equipment and supplies:  All equipment shall be in accordance with, Attachment “A”; Section IV; paragraph “B” and Attachment “A” Section VIII.

B.	Seating space within the cab shall be provided for a Department Inspector if assigned to this operation.

## IV.	Material Storage Box

All shadow vehicles shall be equipped with a lockable, fully enclosed storage box for pesticide storage, the minimum size of this storage box will be 48” long by 30” wide by 30” high.  These storage boxes shall be mounted on the truck bed so as the top of the box is not higher than 36” from the truck bed. These boxes are to be watertight

Page 1 of 1

Attachment “A”

Part V

A1 - Roadside Activity Report (M-609) Guidance

PennDOT Contractors/Business Partners Using the Mobile M-609 app and Web Portal

CWOPA, c-usernames and associated emails are no longer valid in the M-609 Mobile App and M-609 Web Portal. To acquire or retain access to the current release of the M-609 Mobile App and M-609 Web Portal, register with the steps below.

The current Mobile M-609 app (version 1.10) is now available in the Apple App store for download and will include the implementation of a new Business Partner (BP) log-in entitled Enterprise Application Security Solution (ESEC).

The M-609 Web Portal URL has also changed and should be updated to: https://mobile.penndot.gov/m609/resources/view/undefined#/Login

# Step One – Register your organization

- COPY AND PASTE this URL into your web browser: https://idservices.penndot.gov/iam/im/BusinessPartnersPub/pd/index.jsp?task.tag=PD UserSelfRegistrationBOMOMobile&application=PD-BOMOMobile&flag=false

Page 1 of 2

Attachment “A”

Part V

# Step Two – Register a Delegate Administrator for your organization

- The Delegate Administrator User will manage the general users of the organization.

- More than one User can be designated as a Delegate Administrator User.

- All Users must provide a unique personal email to receive temporary passwords for their new b-username account.

- The new b-username account is used to login to the M-609 Mobile App and M-609 Web Portal.

- COPY AND PASTE this URL into your web browser: https://idservices.penndot.gov/iam/im/BusinessPartnersPub/pd/index.jsp?task.tag=PD UserSelfRegistrationBOMOMobile&application=PD-BOMOMobile&flag=false

- Request access to the M-609 app from the dropdown menu during registration.

# Step Three – Register general users of the organization

- COPY AND PASTE this URL into your web browser: https://idservices.penndot.gov/iam/im/BusinessPartnersPub/pd/index.jsp?task.tag=PD UserSelfRegistrationBOMOMobile&application=PD-BOMOMobile&flag=false

- Delegate Admins should use this link to approve/view their users, invite new users and reset passwords: https://idservices.penndot.gov/iam/im/businesspartners/

Contract users that have a current c-username need to list it in the justification block during registration. All b-usernames and new contractors/business partners also need entered in RoSA by PennDOT after receiving ESEC approval.

Page 2 of 2