Items to be purchased:

10	rifle-style wildlife immobilization dart projectors

10	pistol-style wildlife immobilization dart projectors

Bid Specifications:

Projectors must be capable of accurately propelling a 0.5cc-10cc drug-delivery dart (rifle) or 0.5cc-3cc drug-delivery dart (pistol) using a replaceable compressed air CO2 cartridge of 12g or more in which pressure is manually adjustable up and down while displayed on a visible gauge. Projector must also be equipped with a 39-inch (rifle) or 14-inch (pistol) barrel, a 3 x 9 x 32mm optical scope (rifle) or 1x holographic sight (pistol), have an all-black finish, and be compatible with type P Pneudart™ remote-delivery darts, including Pneudart™ 1cc to 3cc telemetry darts. A protective, foam-lined hard-sided case must be included with each projector.

Requested Bid Closing Date:

Wednesday, January 18, 2023

Point of contact:

Mark Ternent, (570) 398-4744 ext 30312