SGL 100

Maple Hill Herbaceous Openings

02/23/2023

GENERAL SPECIFICATIONS

I. SCOPE OF WORK:

The Pennsylvania Game Commission, Northcentral Region is requesting bids for the stump removal, rock picking, and disking 4 acres on SGL 100. This will also include improving 700’ of herbaceous roadway through the same means. Services shall include, but not be limited to, the furnishing of all labor, superintendence, tools and equipment for the removal of stumps from a timber sale, as well as disking and rock picking on 4 acres and 700’ of herbaceous road way on SGL 100, Burnside Township, Centre County. Detailed specifications are attached in the bid packet. All Purchase Orders require the contractor to provide the equipment, labor, insurance, and all miscellaneous expenses to complete the operation.

Any questions concerning the technical aspects of this bid should be directed to:

Shawn Seeley

Land Management Group Supervisor

Phone: 570-398-4744

Email: shseeley@pa.gov

II. CONTRACT TASKS:

There are four tasks which will be three-line-items bid.

1. Stump Removal of 4 acres -Bid per Acre

2. Disking and Rock Picking on 4 acres -Bid Per Acre

3. 700’ of Road leveling and rock picking-Bid as one price

4. Lime, seed, fertilizer spread on all disturbed areas-Bid as on Price

The first task will be to removal of all stumps within the 4 acres. The contractor will be required to removal all stumps and large roots left behind with an excavator or dozer and root rake in a manner where minimal topsoil will be lost. All debris removed from the 4 acres will be disposed of on site at location determined by the LMGS.

The second task is to disc or grade 4 acres where the stumps were removed. The contractor will be required to level the area with a heavy or forestry disc or similar implement so that the area can be farmed with traditional agricultural equipment.

After leveling, pick or screen the surface of the 4 acres and remove all rocks greater than 6”. A location to dispose of the collected rock will be determined on-site by the LMGS.

The third task will be the grading and stone picking and small tree removal on approximately 700’ of a herbaceous road way. The contractor will be required to cut and stump or push out approximately 15 small trees to widen the road and then grade the road to a level running surface and remove all rock larger than 6” and all trees and stumps. All material removed will be disposed of on site at a location determined by the LMGS. This should all be done in a manner to minimize any topsoil removal.

The fourth task will be to spread lime, seed, and fertilizer on the identified 4 acres. This will also include lime, seed, fertilizer, and straw mulch on the 700’ of herbaceous roadway. See Attachment 1 for specific rates of lime seed and fertilizer required.

- Project Location:

• State Game Lands 100, Burnside Townships, Centre County.

• Map of the location are included in the bid packet.

- SITE INSPECTION AND ASSISTANCE:

The PGC will conduct a one-time-only guided tour of the work sites for prospective

bidders on March 16, 2023 beginning at 9:00 AM. The tour will start with a review

of the site. We will meet on Sand Road just off ST Rt. 144.

Contractors are permitted to visit the project site on any date on their own time to

further inspect the site.

III. OPERATOR QUALIFICATIONS:

To bid on this project, an Operator must have the office, maintenance facilities,

equipment, employees, and qualified equipment operators and mechanics, and have

tools, equipment, and spare parts for the make and type of equipment indicated in these

specifications.

IV. CONTRACT REQUIREMENTS:

A. All work can be started any time after a PO has been awarded. Work must be completed by the termination date: June 23, 2023. No contract extensions will be approved.

CONTRACT REQUIREMENTS:

- Remove all stumps and debris within the identified 4 acres and 700’ of roadway so that it can be disced and farmed with traditional agricultural equipment.

- Level or grade the identified 4 acres so that it can be farmed with

traditional agricultural equipment.

- Discing is the preferred method of leveling but other methods may be

approved by the LMGS. No method that scrapes or pushes the topsoil

to the edges of the field will be permitted. Surface soils must remain on

the delineated 4 acres.

- Level or grade and rock pick the identified 700’ of identified roadway in a manner to preserve as much topsoil as possible.

- The operator will rock pick or screen all rocks greater than 6”. Picked

rocks can be placed on site at a location determined by the LMGS.

- Any trees or tree seedlings that are marked yellow are to be removed and

remain onsite at a location determined by the LMGS.

- Any trash resulting from the Operator’s operations must be removed

from the area and properly disposed.

- The contractor is responsible for the control and collection of fluids leaking

from any equipment used on the site. The contractor must have a spill

containment and cleanup kit appropriate for the equipment being used. At a

minimum, the kit will contain plugs and clamps to control hydraulic line

breaks, a container to collect leaking fluids, fluid absorbent pads and a

shovel. Operating any equipment noticeably leaking fluids is prohibited. The

contractor must collect, and control fluids leaking from any equipment and

dispose of properly.

- The Operator shall not block any roads or trails in the area during

performance of this contract. The Operator shall not in any way hinder the

progress of any Timber Sale Contracts in these areas.

- All labor, equipment, tools, etc., needed to complete contracted

projects are to be provided by the Operator.

- As a further guarantee of faithful performance of the conditions set forth in this Contract, the Successful bidder hereby agrees to furnish the Commission with Cashiers or Treasurers Check, Letter of Credit, or Insurance Bond payable to the Pennsylvania Game Commission, in the amount of $1,000.00.

- Failure to comply with any of the terms or conditions of the Contract will result in

cancellation of the agreement.

V. INSURANCE REQUIREMENTS:

- The contractor will provide Workmen’s Compensation insurance sufficient to cover all the employees of the contractor working to fulfill this contract.

B. Comprehensive General Liability Insurance, including bodily injury and property damage insurance, to protect the Commonwealth, and the contractor from claims arising out of the performance of the contract. The amount of Bodily Injury Insurance shall not be less than $300,000.00 for injury to or death of persons per occurrence. The amount of Property Damage Insurance shall not be less than $300,000.00 per occurrence.

Such policies shall name the Commonwealth as an additional insured.

Prior to the commencement of work under this contract, the contractor must provide the

Commonwealth with current Certificates of Insurance. These Certificates shall contain a

provision that coverage afforded under the policy shall not be canceled or changed until at least thirty (30) days prior written notice has been given to the Commonwealth.

VI. HOLD HARMLESS:

The contractor shall be responsible for and agrees to indemnify and hold harmless the

Commonwealth from and against damages to property or injuries (including death) to any persons and other losses, damages, expenses, claims, demands, suits, and actions by any party against the Commonwealth in connection with the work performed by the contractor.

VII. DAMAGE TO PROPERTY:

The Contractor shall be responsible for any damage to Commonwealth property resulting from the improper use of equipment for this project. The Contractor will be given one (1) written warning that damage is becoming excessive and if the action continues damages will be assessed.

PROPERTY INFRASTRUCTURE - Contractor shall immediately repair, in a manner

that meets with the approval of the Officer in Charge, any damage to administrative

roads and other facilities, including access roads, resulting from their use for this

operation, general wear, and tear is accepted. Officer in Charge may notify the

Contractor in writing to temporarily discontinue use of any of the above whenever, in

their opinion, such action is necessary to prevent serious damage.

VIII. BID AWARD:

The bid shall be submitted on a dollars per acre basis by line item. Bids will be awarded

on a per acre basis. The Operator shall complete the electronic invitation for bid to

be found at www.pasupplierportal.state.pa.us, for award of the bid. Bids will be publicly opened on April 3rd, 2022 at 2:00 PM, at the Pennsylvania Game Commission, 2001 Elmerton Ave., Harrisburg, PA 17110-9797. Failure to sign the IFB will be reason for rejection of the bid and bids received after the due date or due time will not be accepted. The per acre price shall include the cost of equipment, labor, insurance, and 3be in dollar and cents only. The quantities herein are only estimates and may increase or decrease dependent upon the needs of the Commission. Operator shall be paid at the unit price bid for actual services performed. The Commission reserves the right to reject any and all bids and to choose the bid that, in its sole opinion; best meet the needs of this project.

ALL VENDORS WHO CONDUCT BUSINESS WITH THE PENNSYLVANIA GAME

COMMISSION MUST HAVE A VENDOR NUMBER ASSIGNED TO THEM IN ORDER TO RECEIVE PAYMENT FROM THE COMMONWEALTH.

Vendors may access the website www.pasupplierportal.state.pa.us or phone (877) 435-7363 or (717) 346-2676 or email ra-srmhelp@state.pa.us for assistance to register as a new vendor or, if you are an existing vendor, to change a main or remit to address. This is a Dept of General services (DGS) website, so you need to contact them directly if you have any problems with the website.

IX. CONTRACT TERM:

The contract term shall commence upon contractor’s receipt of the approved Purchase

Order(s), receipt of performance bond, and proof of insurance. This also includes a notice to proceed February 20, 2023 and terminate June 23, 2023. All contractors, subcontractors and consultants of the Buyer must be pre-approved by the Commission. The Commission reserves the right to reject any subcontractor at its sole discretion. If Contractor enters any subcontract(s) not previously approved by the Commission, the Commission shall have the right to require the Contractor to terminate such contracts.

- OPERATIONS AND NON-WORKDAYS

a) No operations will be permitted on the following days:

1. The opening day and all Saturdays during spring turkey season, including the youth spring gobbler hunt.

b) The contractor, employees, and sub-contractors may not hunt to, from, or at the job site when the work location is beyond a gated road that is closed to public traffic. The contractor may travel to and from the work location on no-work days to check on the condition of equipment.

X. PAYMENT TERMS:

Payment shall be on a reimbursement basis for actual services performed. Payment

will be made on the basis determined by the Commission’s surveyed acreage

treated. Only work successfully completed to the specifications will be paid for by the agency.

Attachment 1:

Maple Hill Herbaceous Openings

- GENERAL SPECIFICATIONS:

- Approximately 4 acres of previously timbered SGL openings will be stumped by excavator or with a dozer with root rake to remove all stumps and large root debris so that minimal topsoil is lost.

- Approximately 4 acres after being stumped will be graded as well as rock picked to allow the areas to be farmed with traditional agricultural equipment.

- 700’ of skid trail will have 15 trees marked with yellow paint removed and stumped to widen access. The road will be graded, rock picked, and debris removed similarly to the 4 acres of openings.

- Upon completion of all grading, leveling, rock picking, and debris removal of the 4 acres and 700’ of roadway it will all be seeded according to the to following rates.

  - 700’ Roadway-0.20 acres                                               Total

    - 100 LBS oats or wheat/acre                                  20 lbs.

    - 300 lbs. 10-20-20 Fertilizer/ acre                           60 lbs.

    - 2 Tons Lime/ acre                                                  0.40 Tons

    - 1.25 Tons/50 Bales Straw Mulch                           0.25Tons/10

  - 4-acre herbaceous openings                                          Total

- 100 LBS oats or wheat/acre                                  400 lbs.

- 300 lbs. 10-20-20 Fertilizer/ acre                           1,200 lbs.

- 2 Tons Lime/ acre                                                   8 Tons

Attachment 2:

Maple Hill Herbaceous Openings

Project Location Map