Rototiller specs.

- Working width 230 CM

- Weight 778 Kg

- Category II

- Tractor HP 60-130

- PTO shaft with slip clutch

- Transmission Speed RPM- 540/1000

- Maximum working depth 25 cm

- Rear hydraulic packer roller attached to back

- Quick release blade system

- Blades arranged helically around rotor

- Central chassis one-piece construction made of 4 mm-thick steel

- Hydraulic bonnet adjustment with leveling bonnet with strengthen bar

- Single bolt quick system for setting side skids to control working depth

- Side chain drive with 4-heavy duty gear drive.