BID PROPOSAL

CONTRACT NO. DMVA 42220144

NOTICE TO BIDDERS

Department of Military and Veterans Affairs, Bureau of Office Services, Procurement and Contracting, Building 0- 47, Fort Indiantown Gap, Annville, Pennsylvania 17003-5002.

Project.    ......................................................42220144 Range Road Re-Paving Area 19

Location………………………………………. Fort Indiantown Gap, Annville, PA. 17003-5002

Agency......................................................... ……… ...Department of Military and Veterans Affairs

Description………………………………… The project consists of full depth removal of existing paving materials approximately 30’ wide by 13”-14” depth on Range Road Station 41+56.75 to Station 63+58.05. Compact and test subgrade. Remove and replace unsuitable subgrade material (unsatisfactory soils). Repave Range Road 24’

wide with 8” subbase course, 4” base course, tack coat, and 1-1/2” wearing course. Install PennDOT Type 3 shoulder 3’ wide each side. Tie into existing paved and gravel roads and parking lots via saw cut or compacted excavation as shown. Restore construction disturbance beyond shoulders. Complete line painting as required.

Contracting Officer:………………………..Tina Rebuck

Questions Due……………………………..APRIL 11, 2023 BY COB 4:30PM

Opening Date and Time............................ APRIL 21, 2023 AT 2:00PM

Contract Number.............................………DMVA. 42220144

Proposed Date of Completion ..............120 Calendar Days from the Notice to Proceed Period……………………………………….60 Days allowed from Bid Opening until Award of Contract

MANDATORY Vendor Registration: All Bidders must be registered to secure plans and specifications and must have a current, active vendor number. Register at www.pasupplierportal.state.pa.us.

All bids must be submitted electronically through the www.pasupplierportal.state.pa.us site. If at any time you are experiencing difficulties uploading your bid documents, please call the Help Desk at 877-435-7363.