PROJECT STATEMENT and SCOPE OF WORK

FOR MOBILE INCINERATOR

FOR THE PENNSYLVANIA DEPARTMENT OF MILITARY AND VETERANS’ AFFAIRS

- Objectives.

- General. The Department of Military and Veterans Affairs (DMVA) is seeking to award a purchase order (PO) for the Pennsylvania Counterdrug Joint Task Force (PACJTF) covers the requirements for a mobile incinerator in accordance with this Project Statement.

- Specific. PACJTF is located at Building 8-47, Engineer Road, Fort Indiantown Gap, Annville, PA 17003. PA-CJTF provides support for Law Enforcement Agencies (LEA) by producing solutions for the disposal of RX drugs.

The PO will cover:

- Mobile Waste Incinerator:

Waste Type: Mixed Type 0, 1, 2, 3, and 4 general waste and waste oils

Waste Density: 7 to 22 lb/ft³

Waste CV: 5,750 BTU/lb (solid waste) 10,000 BTU/lb (liquid waste)

Moisture Content: 20-50%

Estimated Ash Residue: 5-10%

Nominal Throughput: 110lbs/hour batch load up to 8 hours

Incinerator Capacity: 500lbs

Fuel: Diesel

- Incinerator:

Skid Mounted adapted to suit the vehicle trailer

Vertical solid hearth, refractory lined primary combustion chamber

Full sized interlocked bulk load/ash removal door

45 gallon (170 litres) integral fuel tank

5kW diesel generator ▪ 1 off diesel fired ignition burner – temperature controlled

1 off combustion air supply fan and distribution system, automatic control

High-capacity secondary combustion chamber

1 off diesel fired afterburner – temperature controlled

Control panel – automatic operation

Temperature indication primary and secondary chambers 0-2200°F

Stack air dilution plenum

Hinged/Removal stainless steel stack to a height of 9 feet.

- Trailer:

14ft length.

GVWR 10,000lb.

Additional steelwork to secure the incinerator.

Tarpaulin cover.

- One year (1) warranty on all parts and equipment.

- Maintenance replacement parts.

- Installation:

Start-up technician will perform the following: • Calibrate Incinerator Settings • Commission the System.

- Training:

Basics of operating and troubleshooting. In addition to the training, the awarded contractor shall provide a written instruction manual with pictures.

- DMVA Contracting Officer. The DMVA Contracting Officer responsible for the solicitation and PO award is:

Lori Richards, Procurement Specialist

Procurement & Contracting

Bldg. 0-47

Fort Indiantown Gap

Annville, PA 17003-5002

Phone: 717-861-8805

Fax: 717-861-2932

Email: rlori@pa.gov

- Method of Award and Term of PO. DMVA shall award the PO to the lowest responsive quote. In order to be deemed responsive, the bidder must be able to perform the required services as outlined in the project statement and in accordance with the terms and conditions.

- Pricing.  Potential bidders shall submit pricing for all line items/services requested by DMVA. All rates include all incidentals to include overhead and travel.  No separate travel time only hours performed on site shall be reimbursed and will be verified against appropriate sign in logs. Any items billed outside of items defined within this scope will be at the cost of the awarded contractor and not be the responsibility of DMVA.

- Project Statement.

- Product Requirements.  The awarded contractor shall provide the mobile incinerator and must be installed as a complete mobile unit. With all working parts mounted, unit running as should, and is road ready.  No substitutions of products will be allowed.

- Maintenance. The awarded contractor shall provide spare replacement parts:

If there are parts on the mobile incinerator that are consumable or tend to wear more       frequently, we require spare parts. So, we may continue mission as required.

- Undue Delay.  If the Awarded Contractor fails to respond within the required time period of the initial call, it will be deemed an undue delay.  An undue delay in performing the services will justify DMVA to contact another contractor to perform the services.  The Awarded Contractor will be responsible for the damages, that is, the difference in hourly cost between the original contract price and the cost to have the work completed.  DMVA will submit a bill with justification for the difference in cost to the Awarded Contractor.

- Warranty.  Awarded Contractor shall warranty the mobile incinerator, parts and equipment for (1) year from date of shipment.

- Final Inspection.  DMVA reserves the right to conduct a final inspection and acceptance test of all work or deliverables acquired under this PO.

- Facility Security Procedures. Each time the awarded contractor’s employees provide services for DMVA, they will be required to sign in at the security desk at the main entrance of the facility, obtain contractor identification badges, and report to DMVA POC, prior to the provision of services under this PO. Upon completion of the services, the awarded contractor’s employees must return to the security desk, sign out, and return all badges issued to them. The awarded contractor shall follow all required security procedures of each location within the facility in addition to any other pertinent identification or requirements as deemed necessary by DMVA. Particularly sensitive areas may require DMVA staff to accompany the awarded contractor’s employees. These procedures may vary from work location to work location and must be adhered to. The awarded contractor will provide all necessary paperwork for facility designee to sign verifying services rendered.

- Fort Indiantown Gap (FTIG) Access Control. Fort Indiantown Gap is an access-controlled installation and all awarded contractor employees, subcontractors, partners, and delivery personnel shall be required to complete a National Crime Information Center (NCIC) security check and be cleared prior to entering the installation. All personnel shall present a valid United States government issued form of identification at the access control point. Examples of a government issued identification include a valid driver’s license, a state identification card, a passport, or federally issued identification cards. DMVA retains to the authority to deny access based on the presented credentials. Long-term contractor personnel may be issued an identification card for future use if approved by DMVA. Personnel may be required to be escorted for access to the installation. The awarded contractor shall provide personnel that meet the requirements to access FTIG for the provision of all services and deliveries at Fort Indiantown Gap. All requirements of Federal Regulations DodM 5200.08 1.1a(2), DodI 5200.08 Chapter 3 S. 3.2 and DoD DTM 09-012 shall apply.

- Pennsylvania Worker Protection and Investment

- The awarded contractor must maintain compliance with all Pennsylvania state labor and workforce safety laws for the duration of the contract, including, but not limited to:

- Construction Workplace Misclassification Act.

- Minimum Wage Act.

- Prevailing Wage Act.

- Equal Pay Law.

- Employer to Pay Employment Medical Examination Fee Act.

- Seasonal Farm Labor Act.

- Wage Payment and Collection Law.

- Industrial Homework Law.

- Construction Industry Employee Verification Act.

All bidders shall submit the Worker Protection and Investment certification with their bid.

- Billing.  The awarded contractor shall invoice DMVA for services provided under the PO. Renewal year pricing will be maintained at each renewal period. The awarded contractor may be required to provide verification of costs.

The awarded contractor shall submit a monthly invoice for all inspections, maintenance and on-call repair services. The monthly invoices will contain an itemization as defined in the Commonwealth Terms & Conditions.

If the invoice does not contain the minimum information set forth as defined in the Commonwealth’s Standards Terms & Conditions, the Commonwealth may return the invoice as improper.  If the Commonwealth returns an invoice as improper, the time for processing a payment under the Commonwealth’s Standard Contract Terms and Conditions for POs, will be suspended until the Commonwealth receives a correct invoice. The awarded contractor may not receive payment until the Commonwealth has received a correct invoice.

- Estimated Quantities and Like Services.  Quantities will be estimated. The Department reserves the right to increase or decrease quantities based on actual need.  The vendor will be paid for services and supplies satisfactorily delivered.  The Department Reserves the right to include additional like services to the contract if future needs arise.

- Background Check Certification.  The awarded contractor shall certify that a background check has been performed on each of the contractor’s employees not less than five (5) days prior to that employee providing services. If an employee of the awarded contractor has not been a resident of Pennsylvania for at least two (2) consecutive years prior to providing services, the award contractor shall also have an FBI check conducted on the employee. The awarded contractor shall complete and return the background certification form to DMVA’s point of contact (POC) prior to commencement of services and annually thereafter. The awarded contractor shall complete and return the background certification form and the RFQ to DMVA’s POC prior to commencement of services and annually thereafter.

- Contacts.  The awarded contractor shall provide all required documentation throughout the term of the executed PO to the PACJTF POC:

SSG Joseph Madrigale, Engineer Support NCOIC

Department of Military & Veterans Affairs

Pennsylvania Counterdrug Joint Task Force

Office: (717) 861-3288, Monday - Friday 0700-1600

Email: c-jmadriga@pa.gov