BID PROPOSAL

CONTRACT NO. DMVA 42220145

All bids must be submitted electronically through the www.pasupplierportal.state.pa.us site. If at any time you are having problems uploading your bid documents, please call the Help Desk at 877-435-7363.

NOTICE TO BIDDERS

Department of Military and Veterans Affairs, Bureau of Office Services, Procurement and Contracting, Building 0- 47, Fort Indiantown Gap, Annville, Pennsylvania 17003-5002.

Project.    ......................................................42220145 Repave Artillery Road, Fort Indiantown Gap, Annville, PA

Location………………………………………. Fort Indiantown Gap, Annville, Lebanon County

Agency......................................................... ……… ...Department of Military and Veterans Affairs  Description………………………………… Replace 15” CMP with 15” HDPE and two type DW endwalls. Replace 30” CMP with 30” HDPE, 2 type DW endwalls, and Double Type M Inlet and box. Extend 18” HDPE and install Type DW endwall. Replace existing endwall with Type DW endwall on existing 24” HDPE pipe. Replace existing inlet with Type M inlet and box on existing 12” PVC pipe. Install Rip Rap Swale (95 LF). Install Rip Rap Aprons. Remove and replace 24 ft of concrete curb. Tie into existing paving or concrete with clean saw cut and seal. Tie into gravel paving with compacted material as noted. Full depth removal (approx. 13-1/2 inches) of paving materials (4,155 SF) as shown on the plan. Compact and test subgrade. Remove and replace unsuitable subgrade materials (unsatisfactory soils). Repave with 8” subbase course, 4” base course, tack coat, and 1-1/2” wearing course, as shown on the plan and details. Full depth removal of concrete tank pad paving materials (3,610 SF) as shown on the plan. Compact and test subgrade. Remove and replace unsuitable materials (unsatisfactory soils). Repave with concrete as shown on the plan and details. Full depth removal of paved shoulder (2,235 SF) as shown on the plan at 4 ft to 5 ft width. Compact and test subgrade. Remove and replace unsuitable subgrade materials (unsatisfactory soils). Repave as shown on plan and details. Mill 1-1/2 inch of existing paving materials (33,875 SF) as shown on the plan. Repave as shown on plan and details. Complete line painting – two single white lines and single double-yellow line. Restore construction disturbance beyond edges of road.

Contracting Officer:………………………..Tina Rebuck

Site Visit…………………………………….Wednesday May 17, 2023 at 9:00AM

Questions Due……………………………..May 30, 2023 by COB 4:30PM EST

Opening Date and Time............................ June 9, 2023 at 2:00PM

Contract Number.............................………DMVA 42220145

Proposed Date of Completion ..............120 Calendar Days from the Notice to Proceed Period……………………………………….60 Days allowed from Bid Opening until Award of Contract

MANDATORY Vendor Registration: All Bidders must be registered to secure plans and specifications and must have a current, active vendor number. Register at www.pasupplierportal.state.pa.us.