PA Game Commission

Bureau of Wildlife Management

SGL 67

Deer Fence Installation

GENERAL SPECIFICATIONS

- SCOPE OF WORK:

  - The Pennsylvania Game Commission, Bureau of Wildlife Management, requires woven wire deer exclosure fence installation. Services shall include, but not be limited to, the furnishing of all labor, superintendence, material, tools and equipment for the installation of Woven Wire Deer Exclosure Fence as per attached Installation Specifications.

  - Any questions concerning the technical or administrative aspects of this bid should be directed to:

Justin Vreeland

Wildlife Management Supervisor

PA Game Commission 8627 William Penn Highway

Huntingdon, PA 16652

833-PGC-WILD extension 40412

jvreeland@pa.gov

Questions concerning the Purchase Order should be directed to Bobbi Mercer at 717-787-4250.

### CONTRACT TASKS:

  - Project Location:

    - Approximately 7,000 linear feet of perimeter on four units (identified on the attached maps) near Coalmont, Huntingdon County.

  - Contractor shall comply with Attachment I, Fence Installation Specifications.

### SITE INSPECTION AND ASSISTANCE:

An optional site inspection tour may be conducted by contacting Justin Vreeland at the above contact information to make an appointment. The site is located on State Game Lands 67, Burma Road, Huntingdon County; and identified on attached map (coordinates 40.250°/-78.179°).

### CONTRACT REQUIREMENTS:

  - The contractor agrees to comply with specifications in all attachments.

  - All work must be completed by the termination date: October 13, 2023.

- INSURANCE REQUIREMENTS:

  - The contractor will provide Workmen’s Compensation insurance sufficient to cover all the employees of contractor working to fulfill this contract.

  - Comprehensive General Liability Insurance, including bodily injury and property damage insurance, to protect the Commonwealth, the landowner, and the contractor from claims arising out of the performance of the contract. The amount of bodily injury insurance shall not be less than $300,000.00 for injury to or death of persons per occurrence. The amount of Property Damage Insurance shall not be less than $300,000.00 per occurrence.

Such policies shall name the Commonwealth as an additional insured. Prior to the commencement of work under this contract, the contractor must provide the Commonwealth with current Certificates of Insurance. These Certificates shall contain a provision that coverages afforded under the policy shall not be canceled or changed until at least thirty (30) days prior written notice has been given to the Commonwealth.

##### HOLD HARMLESS:

  - The contractor shall be responsible for and agrees to indemnify and hold harmless the Commonwealth and landowner from and against damages to property or injuries (including death) to any persons and other losses, damages, expenses, claims, demands, suits, and actions by any party against the Commonwealth in connection with the work performed by the contractor.

### BIDDING:

  - RECEIVING AND OPENING BIDS - Bids must be submitted via the PA Supplier Portal, to be found at www.pasupplierportal.state.pa.us  Faxed bids and mailed bids will NOT be accepted.

Bids will be publicly opened at the Pennsylvania Game Commission, 2001 Elmerton Ave., Harrisburg, PA 17110-9797.

The price per linear foot of fencing shall include all labor, equipment, tools, insurance, materials disposal and all items necessary for the completion of the project.

Prices bid shall be in dollar and cents only.

  - BID RESULTS - Bidders can obtain results at www.emarketplace.state.pa.us/bidtabs.aspx

The posted results will contain the information of the apparent bidders, and all bids are under review until final award of the purchase order.

Quantities herein are only estimates and may increase or decrease dependent upon the needs of the Commission. Operator shall be paid at the unit price bid for actual services performed.

The Commission reserves the right to reject any or all bids and award contracts as it determines to be in the best interest of the Commission.

- PERFORMANCE SECURITY:

  - As further guarantee of faithful performance of the conditions set forth in this contract, the Contractor hereby agrees to furnish the Commission with Certified Check, Savings Account, Irrevocable Letter of Credit, or other security acceptable to the Pennsylvania Game Commission, in the sum of $3,000.00.

ANY SECURITY POSTED MUST HAVE AN EXPIRATION DATE A MINIMUM OF ONE YEAR BEYOND THE EXPIRATION DATE OF THE CONTRACT.

  - Performance Security is due no later than 30 days after written notice of the bid award. Time is of the essence with regard to the provision of Performance Security. At the option of the PGC, failure to provide an acceptable Surety within 30 days will result in cancellation of the contract and the PGC may declare the bidder ineligible on future projects.

  - Failure to comply with any of the conditions of the contract herein mentioned may result in cancellation of the agreement and claim may be made against the surety or the security for all or part of the damages sustained by such noncompliance.

### OPERATOR REFERENCES

After bid opening and prior to awarding the Purchase Order(s), the Commission has the right to request three (3) references (name, addresses and telephone numbers) of similar work performed in the previous two (2) years as proof of qualifications to perform the work involved in the project(s).

### CONTRACT TERM:

The contract term shall begin upon notification of award. Installation of the fence must be completed by October 13, 2023.

- PAYMENT TERMS:

Payment shall be on a reimbursement basis for actual lineal feet installed as measured by a PA Game Commission employee unless otherwise agreed to by the Commission.

### PURCHASE ORDER(S) TERMINATION

The Commonwealth may terminate the Purchase Order(s) for its convenience if the Commonwealth determines termination to be in its best interest. Operator shall be paid for work completed.

##### ATTACHMENT I

Fence Installation Specifications

- HAZARD TREES

  - After the location of the fences have been determined, all hazard trees posing a danger to the erected fence, within tree length of the fence, must be felled. Hazard trees are dead and dying trees, split trees, heavily leaning trees, and/or root sprung trees, which are in a position to fall across the fence.

  - A PA Game Commission representative will consult with the vendor to determine which trees are to be considered hazard trees.

##### CLEARING FENCE AREA

  - It is the responsibility of the contractor to clear and level a path only as wide as necessary to erect the fence, minimizing soil disturbance when possible, but not more than eight feet wide, of all brush, stumps, rocks, or other obstructions.

  - Obstructions, which in the opinion of the PA Game Commission representative will cause greater installation or maintenance problems, may be left in place.

  - This path will lie outside of the fence and will serve as the access corridor for equipment during installation, serve as a level location for the fence to be erected, and as a maintenance corridor.

  - Disturbance of the entire perimeter may not be necessary. In those areas where the ground is naturally level, free of stumps, and/or free of rocks, no disturbance will be required.

  - A bulldozer of the Caterpillar D4 class should be adequate in completing the required fence line clearing.

  - The contractor will be responsible for, and may be invoiced for, damage to standing trees. Tree damages will be calculated by using the PA Game Commission - Forestry Division's timber stumpage values for the Region. The stumpage value will then be tripled. The severity of negligence will be determined by the PA Game Commission representative. The minimum charge for any commercial, non-commercial, merchantable, or non-merchantable tree shall be twenty-five dollars ($25.00). The PA Game Commission will have the final determination in all damage disputes.

##### EROSION AND SEDIMENTATION CONTROL

  - Equipment will not be operated when ground conditions are such that excessive damage will result.

  - The contractor will be required to install waterbars, silt fence, silt socks, and/or straw bales in disturbed areas of sufficient slope to prevent erosion and soil loss. Erosion control devices must be secured to the ground (i.e., staked) to ensure they remain in place during run-off events. The contractor will repair any areas that become rutted, and seed and mulch these areas according to the following specifications:

3 lbs per acre - Timothy

5 lbs per acre - White Clover - innoculated 10 lbs per acre - Crimson Clover - innoculated 25 lbs per acre - Wheat

The entire fence path will be seeded with 25 pounds/acre of Wheat.

##### FENCE SUPPORTS

  - The contractor will erect the fence by fastening the fence to posts or trees that have been marked with yellow paint. All trees will be protected by having a 2" x 4" board of sufficient length placed between the fence and the tree and the fence will be attached to the board. Contractor will attempt to avoid affixing boards to oaks, hickories, and cherries.

  - Posts that must be added to serve as in-line posts must be 4" x 4" treated square posts, four-inch round treated posts, or steel posts that weigh two pounds/foot. Line posts are to be ten feet long and placed in the ground at least two feet. Corner posts must be at least a 6" x 6" treated post, or five-inch round treated post and braced or supported in place. Bracing and/or guy wires may be used to support the corner post(s), but must be sufficient to prevent the post from bending or pulling free of the ground.

  - All bracing or guy wires outside the fenced area must be clearly marked to prevent a safety hazard to any and all persons.

##### FENCE MATERIALS

  - The completed fence will be approximately seven feet high using two, four (4)-foot rolls or one, eight (8)-foot roll of galvanized steel woven wire or fixed knot fencing. Wire fencing materials will have no more than six inches between stay wires and have at least ten graduated line wires. The top and bottom wires will be at least 12-1/2 gauge wire and stay wires will be at least 14-1/2 gauge wire. Products deemed equal may be approved at the discretion of the PA Game Commission.

##### FENCE STRETCHING

  - The finished fence will be seven feet high with approximately a one foot overlap on the ground pulled to the outside of the fenced-in area. The fence will be stretched so that the wire is pulled against a corner or turning support. Maximum distance between fence supports will be no greater than 30 feet between posts and 40 feet between trees.

  - The top and bottom rolls of fence will be fastened to each other every three feet by twisting, tying, or fastening the bottom wire of the top roll to the top wire of the bottom roll. Where a post is used, the top wire of the top roll must be secured to the post. Each roll of fence will be fastened in three places: Top, middle, and bottom. Ties to secure the fence to metal poles will be 14-1/2 gauge galvanized or stainless steel wire ties or other commercially suitable ties. Stainless steel or galvanized hog rings may be used to fasten the top fence to the bottom fence. Twisting the bottom wire of the top fence section and the top wire of the bottom fence section may be used. Ties may also be used to secure the two sections together but must be 14-1/2 gauge stainless steel or galvanized wire. The PA Game Commission may specify the point where fence stretching begins. This is to facilitate the driving of deer from the fenced area.

##### No aluminum may be used in the installation of the fences.

- FASTENERS

  - Staples will be one and one-half inch galvanized steel. No staples will be driven into trees.

  - The nails used to fasten the 2" x 4" board to the trees have no specifications but must hold the board securely to the tree while the fence is being stretched. The nails used should be long enough to securely hold the 2" x 4" in place and still leave approximately one inch exposed to facilitate eventual removal. Nails used must be larger than #8 common.

##### SECURING FENCE BOTTOM

  - The fence must be installed so that deer will be unable to crawl under the fence. A one-foot overlap on the ground on the outside of the fence will be established. The fence is to be anchored to the ground with stakes or stapled to sound wood every ten feet. Stakes must be driven into the ground 12 inches.

  - Gaps between the ground and the fence of over three inches in height and six inches in length will be filled with sound wood and the fence will be stapled at the bottom to the wood. Other means may be used if approved by the PA Game Commission representative.

##### ACCESS GATES

  - Five (5) walk-through type gates (see attached diagram) will be required. Specific locations for walk-through gates will be indicated on-site by marked flagging. Walk-through gate construction specifications are attached. All walk-through gates will be primed and painted yellow.

  - No vehicle gates are to be installed, but each fence will have a length of excess overlapping, 7-foot-tall panel at least 12 feet wide. Overlap must be secured as per above fastening instructions. This overlap is to allow vehicle access that can be easily refastened.

##### OPERATING AREA

  - The contractor may operate vehicles on the cleared fence path. Vehicles may not travel into the area to be fenced in.

##### DEBRIS AND GARBAGE

  - The contractor will remove all trash and garbage generated during the completing of this contract. This is to include all materials generated from the installation of the fence and items generated from the personal use by the contractor's employees.

##### DEER DRIVE

  - The contractor must drive all deer from the fenced area prior to the closing of the fence. The contractor will notify the PA Game Commission representative 48 hours prior to conducting the deer drive. The deer drive must be conducted with a PA Game Commission representative on site. The fence will be closed the same day that the deer drive takes place.

##### WORK SCHEDULE

  - The contractor will notify the PA Game Commission representative three days prior to beginning work on the project. The contractor may work at times other than the schedule of the PA Game Commission representative. The contractor may be present at the final inspection.

Attachment: Aerial map showing locations of proposed fences. Locations are approximate and on-the-ground adjustments are expected. Contractor will be paid for linear footage of installed fence as determined by a PGC representative.

Attachment: Topographical map showing locations of proposed fences. Locations are approximate and on-the-ground adjustments are expected.