# COMMONWEALTH OF PENNSYLVANIA

COMMERCIAL PRINT SPECIFICATION FORM

| Agency: Health | Title: Death Certificate Paper |
| --- | --- |
| Agency Form No: H105.905 |  |
| Material No: 355429 |  |
| Contract No: 4400020046 |  |
| Contract Line No: 14 | Spec. Date: 05/31/2023 |

Description:	Certificate Paper for vital records

Flat Size:  	8.5" x 11" (long grain)

Paper:	Must be produced at a fully secured mill, approved by the U.S. Treasury or another equivalently recognized and certified independent entity. Mill must be 100% secured by perimeter fencing.  

Paper is to be 24# bond, have an extended "shelf life" (100 years) with a minimum of discoloration and fiber breakdown.  Paper must contain the following security features:

Fourdrinier Watermark:  The unique pattern "chainlink" has been agreed upon by the vendor and the Department of Health, and will be viewable when the paper is held to light.  Alternate Designs for Watermark must be approved by the Dept of Health.  The watermark must appear as an overall pattern on the document.

Chemical Sensitization:  The paper must be sensitive to five chemical families.  The paper must react with colored stain if chemicals from these five families are used to alter the document.  The five families are polar solvents,  non-polar solvents, acids, oxidizing agents, and strong bases.  In addition, the paper, as manufuctured by the mill, will have a hidden indicia feature incorporated that will appear if alteration by chemical means is attempted.

Invisible Fibers:  The paper must have two colors of invisible fibers imbedded in the paper.  The fibers become visible when exposed to ultraviolet light.

Toner Retention:  The paper must be coated front and back to enhance toner retention and deter removal of toner images.

Ultraviolent Dull Paper:  The paper must contain no optical brightening agents.  This facilities viewing the fluorescent features under an ultraviolet light.

Ink(s):	Front:  2 heat resistant inks as follows:
    - Royal Blue for border design, type, etc., including micro printed text and
     "VOID" pantograph in pattern SSAG-12.
    - Red ink to be used for numbering.

Back:  1 heat resistant ink as follows:
    - Gray (PMS 422) for laid lines (which are to be unevenly spaced and intermingled
       with text lines making it difficult to cut and paste information without detection.

Registration:	Registration of the copy on the form must be consistent throughout the entire order.

Embossing:	The Seal of the Commonwealth of Pennsylvania, Department of Health will be embossed on each sheet.  Embossing will be at least 5 thousandths in height.

Consecutive Numbering:	A consecutive control number printed in  red ink and located in the upper left front of the form, typically 8 digits. Vendor must absolutely guarantee NO MISSING NUMBERS.  The starting number for each printing will be identified on the purchase order.

Security:	All spoilage during make-ready and press run must be securely destroyed under confidential measures on vendor premises.  Vendor must utilize the same security measures as used in his plant to manufacture negotiable instruments such as checks, money orders, etc.  Plant security should include armed guards and camera surveillance.  All art work plantes, etc., are to be retaiend in a locked vault.  All art work and graphics are the sole property of the Commonwealth of Pennsylvania and shall be returned to ordering agency under secure conditions when order is complete.  Destruction of plates is to be certified by the vendor at completion of job.

Artwork:	All artwork for border, phantom pantographs and etc., will be supplied by the Commonweath.  The vendor may be required to set type and rules.   The vendor will add a latent image to the border of the document.  Further details on the latent image will be defined at a design meeting at a later date.

All artwork and type must be printed in high resolution to ensure top quality appearance and details.  Latent image and micro text must be readable under magnification.

Specimen:	The word "SPECIMEN" must be printed or punched thereon.  Vendor must ship so that receipt by the Department of Health occurs at least 48 hours in advance of the main shipment, via bonded courier.  Specimens will be numbered separately from main run.  Delivery address will be provided to successful vendor.  Up to 100 specimen sheets may be required per printing.

Over/Under Runs:	No over or under runs will be accepted unless authorized in writing by the Department of Health.  Vendor may NOT print in larger quantities and warehouse.

Security Tape:	Carton tops and bottoms are to be sealed up to 4 inches down the sides, with a 2-ply security tape with a custom printed, ballpoint ink-receptive, non-smear surface outer band which, if removal is attempted, will result in the activation of a blind message indicating that an attempt to open the sealed carton has occurred.  The activation of the seal reveals the formerly blind message in 2 forms: 1) a permanent, residual solid type remaining on the carton while 2) the back of the outer band reveals the same message in open-face type. Once the message is activated, the seals cannot be reassembled to hide intrusion.  Print the outer band with a cautionary phrase plus an area for date, signature and the sequential numbers involved.  The residual message is a notice of intrusion such as, "If seal is broken, tampering may have occurred".  Lesser security tapes such as those leaving a message printed on a polyester liner affixed to the carton are unacceptable due to the potential to remove said liner from carton and reseal with no visible sign of intrusion.

Packaging:	Forms must be packed to ensure against damage in transit.  Cartons must be clearly labeled to show PO number, serial # (starting and ending number), form number, and quantity. Forms must be packed with face side down and lowest number on top.  Forms are to be shrink wrapped in packages of 100 and packaged in cartons of 2,000.

All other packaging and labeling to follow standards established in "Supplier Shipping and Receiving Guidelines".

Delivery:	Printed material to be delivered to DGS facility in exclusive sealed trucks. Trucks cannot be opened until DGS employee is present to verify truck has not been opened prior to arrival.

DGS Warehouse
905 Elmerton Avenue
Harrisburg PA  17105

# Text boxes

Department of General Services

Bureau of Publications

717/704-1029