SPECIFICATIONS FOR PROCUREMENT AND DELIVERY OF ALUMINUM ENCLOSED CAR TRAILERS FOR STATEWIDE AND REGIONAL LAW ENFORCEMENT USE

SPECIFICATIONS: The PA Game Commission (PGC), Bureau of Wildlife Protection (BWP) is issuing an Invitation for Bid (IFB) to procure five (5) 8.5 x 20 Aluminum Enclosed Car Trailers – Aluminum Wheels and one (1) 8.5 x 20 Aluminum Enclosed Car Trailers – Aluminum Wheels with Special Specs to be retrofitted by the Bureau’s preferred contractor post-delivery to contain telecommunications components and to serve as Law Enforcement Command Centers for Regional and Statewide use. Interested bidders must read and agree to meet the specifications listed below and submit a workplan accompanied with product brochures containing specifications for proposed trailers to be constructed or ordered from vendor’s existing inventory. Bidders please note, that bid submissions for this project must include the total cost of the trailer including, but not limited to, applicable set-up fees, delivery costs, etc., which may alter the final cost of the bid.

(Qty 5) 8.5 x 20 Aluminum Enclosed Car Trailers – Aluminum Wheels

Rear Ramp Door and Side Door, Brakes, Deck 96" W x 20'L, Rear Door 90" W x 83” T, Side Door 32" W x 76" T, Interior Height 83", 5200Ib Torsion Axles, Tires 22575R15 Radials, 2-5/16" Coupler, Plywood Walls, Advantech Floor, All Aluminum Trailer, Aluminum Wheels, Screwless Exterior.

Axle: Dual

Rear Door/Gate: Ramp Door

Side Door/Gate: Side Door

Gross Vehicle Weight Rating: 9990 lbs.

Empty Weight: 2748 lbs.

Load Capacity: 7242 lbs.

Color: White or Light Grey

(Qty 1) 8.5 x 20 Aluminum Enclosed Car Trailer -Aluminum Wheels

2-Side Doors (Passenger Side) NO REAR DOOR, Brakes, Deck 96” W x 20’ L, Rear Door 90” W x 83” T, Side Door 32” W x 76” T, Interior Height 83”, 5200lb Torsion Axles, Tires 2257R15 Radials, 2-5/16” Coupler, Plywood Walls, Advantech Floor, All Aluminum Trailer, Aluminum Wheels, Screwless Exterior.

Axle: Dual

Side Door/Gate: 2 Side Doors

Gross Vehicle Weight Rating: 9990 lbs.

Empty Weight: 3262 lbs.

Load Capacity: 6726 lbs.,

Color: White or Light Grey

No substitutions will be accepted, the only bid that will be accepted, and awarded, is to the lowest responsible bidder capable of delivering a product that matches the listed specifications above and meets the Terms of Contract listed below. Please see the attached images on pg. 4 for visual reference prior to submitting bid proposals.

TERMS OF CONTRACT: The terms of contract will commence on the Effective Date of the fully executed purchase order following the IFB being awarded, which will be no sooner than, with two (2) additional one-year options for renewal upon mutual agreement between the PGC, BWP and the Vendor. Once awarded, the Vendor is to have the requested trailers assembled and delivered to the Pennsylvania Game Commission Harrisburg Headquarters, along with the Certificates of Origin for the trailers within thirty (30) working days of the Bid being awarded; with the acceptance of final product dependent upon visual inspection and approval of the Project Manager, Lieutenant Colonel Mark Rutkowski. Invoices for payment are to be submitted to both the Project Manager via email at mrutkowski@pa.gov; and the Pennsylvania Dept of Budget, either by email at 69180@pa.gov, or by mail at Commonwealth of Pennsylvania, PO Box 69180, Harrisburg, PA 17106 with remittance of payment by the PGC to be expected within thirty (30) business days following the acceptance and receipt of final product.

All questions and concerns regarding these conditions and specifications should be addressed to the Project Manager:

Lieutenant Colonel Mark Rutkowski

Bureau of Wildlife Protection

Pennsylvania Game Commission

2001 Elmerton Avenue

Harrisburg, PA 17110-9797

Telephone: (717) 787-4250 x 73503 / Email: mrutkowski@pa.gov

VISUAL REFERENCE