Bid Specifications for Male Wild Turkey Backpack GPS Transmitters.

Mary Jo Casalena – Wild Turkey Biologist

Ken Duren – Game Bird Section Supervisor

6/22/2023

The Pennsylvania Game Commission is collecting bids for one hundred (100) GPS Transmitters to be used on male eastern wild turkeys (Meleagris gallapavo).

Proposed Timeline:

- Order of 100 to be Placed: Sept 7, 2023

- Order of 100 to be Received at Harrisburg, PA: At least ½ (50) by November 7, 2023; the remaining (50) by December 7, 2023.

Each GPS radio transmitter must:

- Be designed for use as a backpack on free-ranging wild turkeys, and upon request, be supported with examples of their use on current turkey studies.

- Use GPS technology to collect accurate locations and transmit location data daily using a satellite connection.

- Consist of a GPS receiver, and a primary cell battery as a power source (not solar).

- Be programable such that it has a primary schedule of 3-4 GPS locations per day with downloads in real-time and 4 hours of VHF per day, and up to 3 auxiliary schedules with easy switching between schedules.

- Satellite acquisition rate of 90% or higher.

- Have a battery life of at least 1 year.

- Have nonvolatile memory of at least 500,000 locations.

- Contain a mortality sensor and send priority notifications of mortalities via email and/or text.

- Weight not to exceed 140g.

- Have dimensions (l x w x h) 8.2 x 3.5 x 3.4 cm or less.

- Have 4 attachment points for a backpack set up to accommodate shock cord diameter of 1/8” (0.32 cm).

- Be able to access data through a secure data portal.

- Operational temperature to -40C.

- Be dark brown in color or similar color to blend in with turkey feathers.

Bids should also include:

- all costs associated with use of the transmitters,

- including any activation fees and data transmission plans that the Game Commission could set up with the third-party.

Questions concerning specifications should be directed to:

Mary Jo Casalena

717-433-8776  mcasalena@pa.gov