COMMONWEALTH OF PENNSYLVANIA

DEPARTMENT OF ENVIRONMENTAL PROTECTION

Division of Source Testing & Monitoring

2575 Interstate Drive, Harrisburg, PA  17110

SPECIFICATIONS: OGI Camera with OGI Camera Accessories

- Provide Six (6) Optical Gas Imaging (OGI) Cameras* that provide thermographic imaging, gas leak detection, gas quantification, with built in Wi-Fi, GPS, hotspot, and Bluetooth capabilities.

  - Each camera shall include:

    - Two (2) batteries.

    - One (1) battery charger cradle.

    - One (1) carrying case.

    - One (1) glare shield (if applicable).

    - One (1) shoulder strap.

    - One (1) lens cleaner.

    - One (1) USB A to mini B cables.

- Training for fifteen (15) people, with each attendee receiving certification.

*Minimum OGI Camera Specifications:

- The OGI camera must be able to operate in the following environmental conditions:

  - Operate in temperatures from - 20oC to + 50oC.

  - Stored in temperatures from - 40oC to 70oC.

  - Intrinsically safe for explosive environments.

- The OGI must have a minimum gas leak protection performance:

  - Operate under advanced and enhanced modes.

  - A spectral filter of 3.2uM to 3.4uM.

- The OGI Camera must have video and audio recording capability:

  - Digital video recorder build-in generating a .ts format video on all modes.

  - Snapshot command generating a .jpg file on all modes.

  - At least 20 hours of video storage with at least 64GB solid state memory.

- Communication Interfaces:

  - USB data transfer, video streaming, and video images file transfer.

  - WiFi with at least 2.4 GHz video streaming and file transfer capabilities.

  - Bluetooth capabilities.

  - GPS capability.

- Imaging Performance:

  - Thermal sensitivity of at least <12mK 25oC.

  - Optics with a or 30mm lens or similar.

  - Built in visible camera.

- OGI Detector:

  - Cooled high sensitivity, 320 x 240 pixels minimum.

  - A spectral range of 3 to 4.4 µm.

- Power Input:

  - 12 VDC.

  - Greater than 4.5 hours continuous operation.

- Physical Characteristics:

  - Tripod mounting rotation safe.

- Thermography:

  - Spot temperature measurements.

  - Range a minimum of -20oC to +350oC.

  - Accuracy at least ±1oC (0-100oC), 2% (>100oC), ±2oC (-20 to 0oC).

  - At least 6 color palettes.

- Quantification:

  - Image processing VOC gas quantification for desktop or handheld must be provided with each camera.

- Instructions to Bidders:

  - The Department of Environmental Protection (DEP), Bureau of Office Services, is requesting price bids for the following items listed in the Invitation for Bid (IFB) item list section. The bidder must supply a price for all items. THIS IS A NO SUBSTITUTION PROCUREMENT. Award will be made based on the lowest grand total price.

- Delivery:

  - Physical delivery location: DEP, Source Testing & Monitoring Division, RCSOB 16th Floor, 400 Market Street, Harrisburg, PA 17101, ATTN: Bryon Richwine.

  - Please include all costs including shipping/handling within the costs of the line items supplied, i.e. bid prices must be FOB destination. No additional costs will be allowed.

- Agency Contacts:

  - Technical questions should be directed to Bryon Richwine, phone: (717) 783-9479 email: brichwine@pa.gov. Email communication is preferred.

  - Bidding procedures questions should be directed to Brady Fries, phone (717) 783-8381, email bfries@pa.gov. Email communication is preferred.

- Bid Submission:

  - All Bids must be submitted electronically through the Department of General Services’ (DGS) eMarketplace website. The eMarketplace website is located at http://www.emarketplace.state.pa.us. DEP is not responsible for the maintenance of the eMarketplace website.

  - DGS’s Supplier Service Center https://www.dgs.pa.gov/Materials-Services-Procurement/Supplier-Service-Center/Pages/default.aspx is available to assist vendors with registration, bidding, and account management. For questions regarding registration help, send an email to RA-PSC_Supplier_Requests@pa.gov or call (877) 435-7363, choose option 1. For questions regarding bidding help, send an email to srmhelp@pa.gov or call (877) 435-7363, choose option 2.

  - DEP is not responsible for the support or functionality of any Department of General Services website.

- Estimated Quantities:

  - The quantities contained in the IFB section are estimated only and may increase or decrease dependent upon the needs of DEP. Ancillary items may be added to this acquisition (purchase order) at the discretion of both parties at a mutually agreed upon price.

  - The contractor shall be paid at the unit bid price for the quantities supplied.

- Award:

  - Award will be made to the responsible, responsive bidder based on the lowest grand total price.

  - Bidders are required to complete and return the “Reciprocal Limitations Form” electronically attached to the IFB file. Reference see Title 62 Pa C.S. Section 107.

- Payment Terms:

  - Payment shall be made upon satisfactory receipt of items ordered and invoice submitted.