1.SCOPE/OVERVIEW:

This Invitation for Bid (IFB) issued by the Commonwealth of Pennsylvania, Department of Transportation (PennDOT), Bureau of Maintenance shall provide a quote to purchase and install twelve (12) 696 series 96’’Knapheide steel service bodies and seventeen (17) A698 series 96” aluminum service Knapheide bodies on 1-ton 4x4 single rear wheel crew cab pickup trucks to be utilized by PennDOT road foremen personnel as their primary work vehicle.

This bid solicitation has been reserved for Small Business Contracting. Only those Bidders certified as DGS Small Businesses through the Small Business Contracting Program may submit a bid for these services.

2.WORKER PROTECTION AND INVESTMENT CERTIFICATION

Pursuant to Executive Order 2021-06, Worker Protection and Investment (October 21, 2021), the Commonwealth is responsible for ensuring that every Pennsylvania worker has a safe and healthy work environment and the protections afforded them through labor laws. To that end, contractors and grantees of the Commonwealth must certify that they are in compliance with all applicable Pennsylvania state labor and workforce safety laws. Such certification shall be made through the Worker Protection and Investment Certification Form (BOP-2201) and submitted with the bid, proposal or quote.

3.QUALIFICATION/ REQUIRMENTS

This contract will be 1 year with 1 year renewal. The vendor must be able to receive one truck or multiple trucks at a time and is expected to complete one (1) truck per three business days once the delivery date and work schedule is set.

The successful bidder must have adequate space and insurance to fully protect the vehicles while on their property and when being transported for delivery. This includes a minimum of $600,000 in Garage Keeper Insurance in all locations in which the vehicles are stored. This insurance must be valid for the total length of the contract.  Proof of insurance must be provided with submission.

4.REJECTION OF BIDS

The Issuing Office reserves the right to reject any and all Bids, to waive technical defects or any informality in Bids, and to accept or reject any part of any Bid if the best interests of the Commonwealth are thereby served.

5.TIE BIDS

All tie bids will be broken by the Issuing Office.

6.AWARD

This bid will be awarded to the lowest responsive and responsible bidder. This bid solicitation has been reserved for Small Business Contracting. Only those Bidders certified as DGS Small Businesses through the Small Business Contracting Program may submit a bid for these services.

Unless all Bids are rejected, and except as otherwise provided by law, award will be made through the issuance of a contract/purchase order in accordance with the method of award. As a condition for receipt of award of a contract/purchase order, the Bidder must be registered in the Commonwealth of Pennsylvania's Vendor Master file. In order to register, bidders must visit the Pa Supplier Portal at https://www.pasupplierportal.state.pa.us/ or call the Customer Support Center at 877-435-7363 or 717- 346-2676.

7.PROMPT PAYMENT DISCOUNTS

Prompt payment discounts will not be considered in making an award. If prompt payment discounts are offered by any Bidder, however, the Issuing Office will take advantage of such offer.

8.EQUIPMENT SPECIFICATIONS

- Remove existing pickup truck bed. Install 696 series 96” Knapheide Steel service bodies on model year 2023-2024 1-ton 4x4 Ford, Chevy or Ram single rear wheel crew cab pickup trucks. (Total of twelve (12) pickup trucks).

- Remove existing pickup truck bed. Install A698 series 96” Knapheide Aluminum service bodies on 1-ton 4x4 single rear wheel crew cab pickup trucks. (Total of seventeen (17) pickup trucks).

Upfit Specifications Below:

- 696 Knapheide Steel Service Bodies

Install Knaphedie Steel 696 Service Body to Include:

- Exterior Painted Color Code of Truck.

- Galva, Grip Bumper with Hitch Recess.

- Class V Hitch,

- Backup Alarm,

- Two Chrome Grip Handles

- Two Louver Vents

- 2.5in To 2in Receiver Tube Adapter

- 15" Heavy Duty Aluminum Shovel Box (Penndot Spec)

- Center Cargo Area shall have a Linex brand sprayed bed liner no substitutes. Shall cover floor and all sides including tailgate interior. Shall be a minimum of 150 Mils. Thickness. Material shall have No VOCS and be applied utilizing a high pressure spray.

Safety Whelen Led Strobe Lights

- PD2023PADOTSY5          Sys, Crew Cabs, Foreman, Service

- 01-066A797-A1N            Assy, Lthead M6 Sync Amb/Amb (2)

- 01-066B160112H            Assy, Lthead M6 Back-Up 12v (2)

- 01-066B1866R1K            Assy, Lthead M6 Btt 12v Red (2)

- 01-0486152-01E              Kit, 3-Lt M6 Housing Black (2)

- ION AMBER                   Mounted in grill and sides of body over fenders. (4)

- R10PADOT                      Responder mini light bar (1)

- 01-0687178                     Assy, Single Flood Light PADOT (1)

Reflective tape for single rear wheel service bodies. Includes:

Diagonal alternating lime green and red conspicuity tape on rear of compartments, and two inch red/white striped conspicuity tape downside of body and truck.

Install Rear Flush Mount Cam Kit on Pickups

PennDOT Yellow to Match Chassis. Material and Supplies

Aluminum treadplate on top of right service body compartment

Fleet series drill-free light bar cab mount for pickup trucks

- A698 Knapheide Aluminum Service Bodies

Knaphedie Aluminum A698 Service Body To Include:

- Exterior PAINTED Color Code Of Truck

- Galva, Grip Bumper with Hitch Recess. Class V Hitch

- Backup Alarm

- Two Chrome Grip Handles.

- Two Louver Vents

- 2.5inch to 2 inch Receiver Tube Adapter

- 15" Heavy Duty Aluminum Shovel Box (Penndot Spec)

- Center Cargo Area shall have a Linex brand sprayed bed liner no substitutes. Shall cover floor and all sides including tailgate interior. Shall be a minimum of 150 Mils. Thickness. Material shall have No VOCS and be applied utilizing a high pressure spray.

Safety Whelen Led Strobe Lights

- PD2023PADOTSY5          Sys, Crew Cabs, Foreman, Service

- 01-066a797-A1n            Assy, Lthead M6 Sync Amb/Amb (2)

- 01-066b160112h            Assy, Lthead M6 Back-Up 12v (2)

- 01-066b1866r1k            Assy, Lthead M6 Btt 12v Red (2)

- 01-0486152-01e              Kit, 3-Lt M6 Housing Black (2)

- Ion Amber                      Mounted In Grill And Sides Of Body Over Fenders. (4)

- R10padot                         Responder Mini Light Bar (1)

- 01-0687178                     Assy, Single Flood Light PADOT (1)

Reflective tape for single rear wheel service bodies. Includes:

Diagonal alternating lime green and red conspicuity tape on rear of

compartments, and two inch red/white striped conspicuity tape downside of body and truck

Install Rear Flush Mount Cam Kits on Pickups

PennDOT Yellow to Match Chassis. Material and Supplies

Aluminum treadplate on top of right service body compartment

Fleet series drill-free light bar cab mount for pickup trucks

9.DEIVERY

PennDOT will deliver each truck to the awarded vendor. When work is completed, all trucks must be delivered back to Fleet Management at 1700 Arsenal Blvd Harrisburg, Pa. 17120 at the vendor’s expense.

PennDOT will inspect each truck after completion for workmanship and compliance with the specification as written. Any deficiencies found will require the vendor to repair at Fleet Management or transport back to the vendor facility, then return the truck(s) to Fleet Management at the expense of the vendor for re-inspection. Location of repair must be approved by PennDOT. Payment will not be authorized until all deficiencies are corrected.

10.BIDDER INSTRUCTIONS:

- Bids are due by 10:59 AM EST on October 26, 2023.

- Bid unit prices shall be inclusive of all charges.

- No additional charges will be permitted.

11.QUESTIONS AND ANSWERS:

Vendor questions are due by 3:00 PM EST September 28, 2023.

Submit questions via email to Denny Koozer, Pennsylvania Department of Transportation, Bureau of Maintenance, Section Chief at dkoozer@pa.gov.

All questions and answers will be responded to via an addendum to this solicitation by 3:00 PM EST October 2, 2023