SOLICITATION ADDENDUM

| Date: | 3/18/2024 |
| --- | --- |
| Subject: | Game Commission F 350 Trucks |
| Solicitation Number: | 6100060524 |
| Due Date/Time: | 4/05/2024 |
| Addendum Number: | 02 |

To All Suppliers:

The Commonwealth of Pennsylvania defines a solicitation “Addendum” as an addition to or amendment of the original terms, conditions, specifications, or instructions of a procurement solicitation (e.g., Invitation for Bids or Request for Proposals).

List any and all changes:

We have received a couple of questions, here are the answers.

- Would you have information on cab to axle measurements on these three vehicles

A:  This information would come from Ford.

- What length of the beds you want?

A: BEDS:

SRW Stake

Heavy-duty 9’ x 80” (minimum) stake body. Platform constructed of seasoned and weather protected 1 1/8” hardwood or 2” (nominal) treated dense pine, tongue and groove or shiplap, attached to cross sills with flush, self-tapping screws. Five (5) inch structural steel longsills with 18” crossmember spacing. Steel platform rubrail. Removable, interlocking stake sections, 26” minimum height, constructed of formed metal with formed metal uprights and spring-loaded rack connectors. Spring loaded mechanism to securely lock stake section into stake pocket. Frame mounted ICC step type rear bumper constructed of 4” structural steel channel. DOT approved lighting. All body lighting shall be LED. Rectangular drop in bulkhead with screened window cut[1]out, approximate cab height.

DRW F-350 Stake and Utility trucks

Heavy-duty 9’ x 96” (minimum) stake body. Platform constructed of seasoned and weather protected 1 1/8” hardwood or 2” (nominal) treated dense pine, tongue and groove or shiplap, attached to cross sills with flush, self-tapping screws. Five (5) inch structural steel longsills with 18” crossmember spacing. Steel platform rubrail. Removable, interlocking stake sections, 26” minimum height, constructed of formed metal with formed metal uprights and spring-loaded rack connectors. Spring loaded mechanism to securely lock stake section into stake pocket. Frame mounted ICC step type rear bumper constructed of 4” structural steel channel. DOT approved lighting. All body lighting shall be LED. Rectangular drop in bulkhead with screened window cut[1]out, approximate cab height.

Standard Utility Body constructed from 12, 14 or 16 gauge galvanneal steel and welded into one integral unit, 108” length, 48” inside width, 25” (approximate) height above floor. Safety tread floor, standard safety step bumper. One (1) removable right side mount ladder rack, three (3) weathertight compartments each side, recessed paddle handles, slam action locks keyed alike, two (2) removable shelves with adjustable dividers in left and right front compartments, one (1) removable shelf with adjustable dividers in each horizontal compartment. Compartment layout to be selected by ordering agency from manufacturer’s standard configurations. All body lighting shall be LED.

Type of Solicitation:  Electronic Bid (SRM) - Review the Questions section of your solicitation response to ensure you have responded, as required, to any questions relevant to solicitation addenda issued subsequent to the initial advertisement of the solicitation opportunity.

Except as clarified and amended by this Addendum, the terms, conditions, specifications, and instructions of the solicitation and any previous solicitation addenda, remain as originally written.

Respectfully,

Name: 	Dan Covell

Title: 	Commodity Specialist

Phone: 	717–346-3828

Email:  	dcovell@pa.gov