Attachment A

Patcher with Operator - Rental Specifications

Location

To be operated within the confines of Pike County on an as needed basis.

Equipment Requirement

Contractor to provide one (1) Mobile Road Patcher with all required safety and operational equipment, work lights, reverse direction alarm and a revolving or strobe warning light provided by Contractor. Unit should also have a minimum 5 cubic yard aggregate hopper.  The unit must be able to move while patching.

The Contractor must supply all asphalt, oil, and washed aggregate.  The aggregate must be Bulletin 14 approved and obtained from a Bulletin 14 approved source.  The emulsion oil must be Bulletin 15 approved.  The Contractor will also ensure that proper oil and aggregates are used to guarantee positive chemical bond of oil and aggregate.  The materials provided shall be appropriate for the particular project, regardless of temperature.

Additional Equipment Required

Maintenance of equipment, fuel, lubrication, and all safety items necessary to operate the unit(s).

Contractor is also responsible for proper disposal of waste products created during machine clean out.

PennDOT will not be responsible for time required for equipment servicing/maintenance.

The Contractor must furnish a copy of vehicle registration cards where applicable prior to execution of Purchase Order.

Operator Requirement

Contractor to provide an experienced operator (per unit) who possesses CDL qualifications appropriate to vehicle classification.

Mobilization

Contractor shall obtain all permits required for the transporting of the equipment and is responsible to ensure all equipment is in conformance with applicable Pennsylvania Motor Vehicle Laws.

Contractor is responsible for transporting the equipment to the initial jobsite, and from job site to job site, as directed by the PennDOT County Manager or designee.

Payment will not be made for downtime, preparation time, travel time, scheduled breaks, or time required for equipment repair/service.

Contractor must be available to work at any time of year regardless of temperature and must be available to work days, nights and weekends on an as needed basis.

Disposal

PennDOT is responsible to dispose all material during operational use hours at an approved facility in accordance with all State, Local and Federal Regulations.

The Contractor will be responsible to contact PennDOT Pike County for the disposal of the material created during machine clean out.

Warranty

Roadway repairs made by contractor must carry a one (1) month minimum warranty.

Call Out Response Time

Contractor is expected to provide the equipment within two (2) calendar days’ notice.

PennDOT will be responsible for Work Zone Traffic Control during all operations.

Quote Award

One (1) unit will be bid. Award will be based upon lowest total quote.   This will be a small business reserve bid.

Call Out Period

Call out period will Monday through Friday with possible weekends.

Contractor must be available to supply services during day, night, and weekends.

Schedules are subject to change.

Scheduled Call-Outs

For Scheduled Callouts the Contractor will be given two (2) calendar days’ notice.

The Contractor is expected to report to the job site or designated area and begin at times determined by the PennDOT County Manager or designee and indicated by the schedule.

The PennDOT County Manager or designee may restrict work times on certain highway networks to accommodate the traveling public.

No payment will be made for cancellations to any Scheduled Call-Out if at least four (4) hours notification of cancellation is provided by the PennDOT.

Contractor will be guaranteed a minimum of two (2) hours for each Scheduled Call-Out cancelled with less than four (4) hours notification of cancellation by the PennDOT.

Purchase Order Estimated Hours

All hours are estimated. The quantities shown are strictly an estimate. PennDOT reserves the right to increase or decrease the items of work during the duration of the purchase order. There is no assurance that PennDOT’s actual usage of the equipment will approximate this estimate.

Scheduled Services:				300 Estimated Hours per unit

Validity Periods

The Validity period will be from February 1, 2024 thru June 30, 2028

The performance time period specified in a Purchase Order may specify a service period of up to, but no longer than, ninety (90) days beyond the expiration date of ITQ Contract Number 3516T01.

Renewal Option

The Purchase Order may be renewed for a maximum of four (4) additional one (1) year term(s), so long as PennDOT provides written notice to Contractor of its intention to extend the Contract by letter prior to the expiration of the term of the agreement, or any extension thereof. PennDOT may exercise the renewal as individual year or multiple year term(s).

Any renewal will be under the same terms, covenants, and conditions, provided, however, that the rates under the contract will be increased by 3% during each renewal term. No further document is required to be executed to renew the term of the Purchase Order.

Extension Option

The PennDOT reserves the right, upon notice to the Contractor, to extend the Purchase Order for up to three (3) months upon the same terms and conditions.

Equipment Inspection

The apparent low bidder shall demonstrate to the County Manager or designee that the equipment proposed for use in meeting the requirements of the Statement of Work and the ITQ Terms and conditions is of sufficient capacity and quantity, and that all such equipment is in good working order.

Within 10 calendar days of notice of apparent low bidder status, the County Manager or designee will notify the apparent low bidder regarding the date, time, and location of the demonstration.

At the discretion of the Equipment Manager or designee, the apparent low bidder may be provided with up to five (5) additional calendar days after an initial, unsuccessful demonstration of equipment and personnel acceptability to prepare for and satisfactorily complete a second demonstration.

If the apparent low bidder fails to demonstrate the acceptability of its equipment within ten (10) business days of PennDOT's initial notification of date and time of inspection, the apparent low bidder will be deemed nonresponsive and not responsible and its bid will be rejected.  The contract will then be awarded to the next lowest responsive and responsible bidder that successfully demonstrates the acceptability of its equipment and personnel.

PennDOT will provide the Contractor written communication regarding the outcome of the equipment demonstration.

Contractor Performance Issues

If a Contractor fails to provide the equipment, for whatever reason, the Contractor will be in default and the CPO subject to termination pursuant to Part IV, Paragraph 22 Invitation to Qualify (ITQ) for the Rental of Highway and Other Equipment, Number 3516T01.  PennDOT reserves the right not to execute any of the Renewal Options.

Insurance Requirements

The contractor must furnish a copy of their insurance certificate with PennDOT named as an additional insured in accordance with ITQ 3516T01, Part IV paragraph 45 and copies of vehicle registration cards where applicable prior to execution of Purchase Order.

Worker Protection and Investment

Pursuant to Executive Order 2021-06, Worker Protection, and Investment (October 21, 2021), the Commonwealth is responsible for ensuring that every Pennsylvania worker has a safe and healthy work environment and the protections afforded them through labor laws.  To that end, contractors and grantees of the Commonwealth must certify that they are in compliance with all applicable Pennsylvania state labor and workforce safety laws.

Such certification shall be made through the Worker Protection and Investment Certification Form (BOP-2201) and submitted with the bid, proposal, or quote.

PennDOT’s Strategic Environmental Management Program (SEMP) Requirements

PennDOT has implemented a Strategic Environmental Management Program (SEMP) which complies with the ISO 14001:2004 standard.  As part of SEMP, the Commonwealth of Pennsylvania has established a Green Plan Policy that can be found at:

www.dot.state.pa.us

Type in 'SEMP' in search field and select the magnifying glass.

Then select ‘Pollution Prevention' and review site.

The Green Plan Policy is designed protect the environment, conserve resources, and comply with environmental laws and regulations.

The Contractor shall ensure that its personnel are aware of the Commonwealth of Pennsylvania’s commitment to protecting the environment, are properly trained about the environmental impacts of their work and are competent (through appropriate work experience, job training or classroom education) to perform the work that they do