COMMONWEALTH of PENNSYLVANIA

DEPARTMENT of ENVIRONMENTAL PROTECTION

DIVISION of SOURCE TESTING & MONITORING

2575 Interstate Drive, Harrisburg, PA  17110

- SPECIFICATIONS

This is a NO SUBSTITUTION PROCUREMENT for Gas DetectIR VOC OGI Cameras with Accessories and Certified Training.

| Model# | Specifications |
| --- | --- |
| Gas DetectIR VOC | Part Number ICIGASDIR-VOC-24 Provide Six (6) Gas DetectIR VOC Optical Gas Imaging (OGI) Cameras that provide thermographic imaging, gas leak detection, gas quantification, with built in Wi-Fi, GPS, hotspot, and Bluetooth capabilities. Each camera shall include: Two (2) batteries. One (1) battery charger cradle. One (1) carrying case. One (1) shoulder strap. One (1) lens cleaner. USB 2.0 Specifications: Pixel Resolution: 320 x 240 Accuracy: ± 2°C (± 3.6 °F) or ± 2% Temperature Range: -20 °C to 160 °C (-4 °F to 320 °F) Operation Range: -15 °C to 50 °C( 5 °F to 122 °F) Storage Range: -40 °C to 70 °C (-40 °F to 158 °F) Detector Array: Type II SLS Focus: electric or manual FOV: 24° x 18° IFOV: 1.31 mrad Spectral Band: 3 μm to 5 μm Response Time: 0.001 ml/s Thermal Sensitivity (NETD): < (15 mK) 0.015 °C at 30 °C (86 °F) Frame Rate: 50 Hz Dynamic Range: 16-bit Humidity: 10% to 95% non-condensing Pixel Operability: > 99 % Shock/Vibration: 25 G/2.5 G Dimensions (without lens): 292 mm x 148 mm x 136 mm (L x W x D ± 0.5 mm) (11.50” x 5.83” x 5.35” (L x W x H ± 0.02”)) Power: 12V DC/AC adapter Battery: Li-ion, rechargeable/replaceable Operation Time: ≥ 3 Hours Charging Time: 3 Hours Start Up Time: ≤ 5 minutes Weight: ≤ 2.6 kg (5.73 lbs) Interface: USB 2.0 View Finder: color OLED Video Format: IRV or AVI Video Output: S-video/HDMI Image Format: IR IMA (with data) + visible JPG Image Polarity: 6 options Memory: SD Card (up to 32 GB) Screen: 4:3, 3.5” LCD screen, 640 x 480 Digital Camera: 5 MP Zoom: 1x - 8x continuous Emissivity Correction: 0.1 to 1.0 Voice Annotation: 60 seconds per image Protection: IP54, IEC 529, ATEX - explosion proof Laser: Class II 635 nm, < 1 mW Internal non-uniformity correction (NUC) Features: Unmatched gas detection ATEX certified - explosion proof Trace Mode for better visibility Detects over 18 gases Multiple video output options Rotating 3.5”, 640 x 480 LCD screen Tilting high-definition viewfinder 60 Seconds voice annotation per image Compact/portable Gases Detected: Benzene - 3.5 g/hr Ethanol - 0.7 g/hr Ethylbenzene - 1.5 g/hr Heptane - 1.8 g/hr Hexane - 1.7 g/hr Isoprene - 8.1 g/hr Toluene - 3.8 g/hr Methanol - 3.8 g/hr MEK - 3.5 g/hr Pentane - 3.0 g/hr Xylene - 1.9 g/hr Butane - 0.4 g/hr Ethane - 0.6 g/hr Methane - 0.75 g/hr Propane - 0.4 g/hr Ethylene - 4.4 g/hr Propylene - 2.9 g/hr MIBK - 2.1 g/hr Octane - 1.2 g/hr 1-Pentene - 5.6 g/hr |
| Certified Training | Part Number ICIGASDIR-VOC-24 Training for fifteen (15) people, with each attendee receiving Level I thermography certification. |

- INSTRUCTIONS TO BIDDERS

The Department of Environmental Protection (DEP), is requesting price bids for the items listed in the Invitation for Bid (IFB) Specifications section. The bidder must supply a price for all items. THIS IS A NO SUBSTITUTION PROCUREMENT. Award will be made based on the lowest grand total price.

- DELIVERY

  - Physical delivery location: DEP, Source Testing & Monitoring Division, RCSOB 12th Floor, 400 Market Street, Harrisburg, PA 17101, ATTN: Bryon Richwine.

  - Please include all costs including shipping/handling within the costs of the line items supplied, i.e. bid prices must be FOB destination. No additional costs will be allowed.

- AGENCY CONTACTS

- Technical questions should be directed to Bryon Richwine, phone: (717) 783-7723 email: brichwine@pa.gov. Email communication is preferred.

- Bidding procedures questions should be directed to Brady Fries, phone (717) 783-8381, email bfries@pa.gov. Email communication is preferred.

# BID SUBMISSION

- All Bids must be submitted electronically through the Department of General Services’ (DGS) eMarketplace website. The eMarketplace website is located at http://www.emarketplace.state.pa.us. DEP is not responsible for the maintenance of the eMarketplace website.

- DGS’s Supplier Service Center https://www.dgs.pa.gov/Materials-Services-Procurement/Supplier-Service-Center/Pages/default.aspx is available to assist vendors with registration, bidding, and account management. For questions regarding registration help, send an email to RA-PSC_Supplier_Requests@pa.gov or call (877) 435-7363, choose option 1. For questions regarding bidding help, send an email to srmhelp@pa.gov or call (877) 435-7363, choose option 2.

- DEP is not responsible for the support or functionality of any Department of General Services website.

# ESTIMATED QUANTITIES

The quantities contained in the IFB section are estimated only and may increase or decrease dependent upon the needs of DEP. Ancillary items may be added to this acquisition (purchase order) at the discretion of both parties at a mutually agreed upon price. The contractor shall be paid at the unit bid price for the quantities supplied.

# PAYMENT TERMS

Payment shall be made upon satisfactory receipt of items ordered and invoice submitted at the unit bid price for the quantities supplied.

# REQUIREMENTS

- See (page 1-3 of this specification) item list section for listing of parts.

- Keii Electro Optics Technologies is the requested manufacturer for all items contained in this bid. Substitution responses will not be accepted.

# AWARD

# Award will be made to the responsible, responsive bidder based on the lowest grand total price in accordance with the Specifications. Bidders are required to complete and return the “Reciprocal Limitations Form” electronically attached to the IFB file. Reference see Title 62 Pa C.S. Section 107.