PENNSYLVANIA STATE POLICE

DEPARTMENT HEADQUARTERS

1800 ELMERTON AVENUE

HARRISBURG, PA 17110

Contract Scope/Overview:

The Pennsylvania State Police (PSP) is issuing this Invitation for Bid (IFB) to procure one Tactical TSCM Kit (TTK) which is in a small deployment ready package. This Technical Surveillance Countermeasures (TSCM) survey equipment is a portable “bug” sweep kit. Included with this package is a MESA 2.0, ANDRE, ORION 2.4 HX CMA-100 and a thermal imager.

This is a no substitute bid for the TSCM kit and accessories listed in the specification.

Manufacturer Authorization Letter

If the bidder submitting a response to this IFB and is not the original manufacturer of the equipment being provided, the bidder must submit a Manufacturers Authorization Letter which clearly states the bidder is authorized to provide the OEM’s equipment and services required by this IFB. The Manufacturers Authorization Letter must reference “IFB 61000xxxxx – Tactical TSCM Kit.” As part of this letter the manufacture must also acknowledge their responsibility for any warranty issues for the weapon.

Contract Quantities

This is for one TTL tactical TSCM Kit including the MESA 2.0, Andre, Orion 2.4 HX, CMA and multimeter with thermal imaging. The kit is packaged in a Pelican  1535 Air maximum carry case.

Specifications for

MESA 2.0 – hand-held Spectrum Analyzer for portable RF analysis up to 6 GHz (12 GHz with Downconverter Antenna).

- 10kHz to 6GHz spectrum analyzer

- Sweeps 200GHz per second

- SmartBars® Mode (Patented)

- Mobile Bands Mode showing RF levels of customizable spans

- WiFi and Bluetooth modes to identify access points

- Full Touchscreen control, with visual, audible, and haptic vibration alerts

- MCP (Multi-Carrier Probe) – Carrier Current

- Data Logging

- Cached Peak Function (Patent Pending)

ANDRE - Broadband Detector for near field detection and location of RF transmitters up to 6 GHz (12 GHz with Downconverter Antenna).

- Broadband RF detection up to 12GHz with Downcoverting Antenna, plus Infrared and Visible Light

- Histogram Display showing RF levels over periods of time

- Signal information and band details generate a signal list of the strongest signals

ORION 2.4 HX - Non-Linear Junction Detector for finding hidden electronics (active and inactive) (FCC 3.3W or G 6.6W).

- Frequency band: 2.404 GHz – 2.472 GHz

- Transmit modulation: pulsing, digital spread spectrum 1.25 MHz bandwidth

- More than 60 available transmit channels

- Digitally correlated 2nd and 3rd harmonic response

- Touch screen display showing harmonic responses and a spectrum view of operation bands

- Visual, audible, and haptic vibration alerts

CMA - Countermeasures Amplifier for detecting wired surveillance devices.

- 110dB of Gain

- Built-in AC/DC voltmeter

- Ability to bias voltage between -15V and +15V DC

Multimeter with built-in thermal imaging.

Delivery Requirements:

The kit shall be delivered fully factory assembled and duty ready.  The TTK  must be delivered within 120 days after receipt of the purchase order to the below address:

PSP Bureau of Emergency and Special Operations

171 E. Hersheypark Drive

Hershey, PA 17033