PENNSYLVANIA STATE POLICE

DEPARTMENT HEADQUARTERS

1800 ELMERTON AVENUE

HARRISBURG, PA 17110

PSP IFB SPECIFICATIONS

IFB# 6100060665 - Troop C, Punxsutawney Garage Equipment

I-1.     Statement of the Project.

- The Pennsylvania State Police (PSP) is issuing this Invitation for Bid (IFB) to procure Equipment for the Troop C, Punxsutawney Garage.  These specifications and quantities are set forth in these specifications as for all related products and services. Substitutions of the products are permitted provided they meet the specifications listed for each unit.

I-2.	Specification and Quantity.

- Provide technical data and manufacturer limitations on items.

- 12K Hoist:  With installation (part# CL12A06)					Qty: 1

| Safety Lock Equipped | Yes |
| --- | --- |
| Lift Pad Height | 4 3/4 in. |
| Lift Safety Lock Release Type | Manual |
| Lift Drive Thru Clearance | 102 3/4 in. |
| Maximum Lift Height | 154 in |
| Lift Height of Rise | 79 1/2 in. |
| Lift Safety Locks Type | Mechanical Auto Engaging |
| Lift Arm Restraint Type | Gear Type |
| Lift Motor Size | 2 HP |
| Width Between Columns | 114 7/8 in. |
| Foldable | no |
| SDS Required | No |
| Lift Model | 2 Post |
| Lift Weight | 2250 lbs |
| Remote Control | No |
| Lift Capacity | 12000 lbs |
| Lift Height | 154 in. |
| Lift Type | 2-Post |
| Lift Equalization Type | Cable |
| Adjustable Legs | yes |
| Weight | 2240 lbs |
| Lift Width | 140 in. |
| Lift Drive Mechanism Type | Hydraulic |
| Contains VOCs | No |
| Lift Safety Lock Intervals | 3 3/4 in. After First 15 1/2 in. |
| Lift Electrical Requirements | 208/230 Volts 1PH |

- Tire Changer:   With installation (part# CL12A06)				Qty: 1

| Power Assist Tower Included | Yes |
| --- | --- |
| Power Source | Electric |
| Portable Or Fixed Mount | Fixed |
| Base Height | 87 in |
| Voltage | 220 V |
| On Board Storage | Yes |
| Wheel Clamping Method | External |
| Tire Changer Type | Manual |
| Hose Included | N/A |
| SDS Required | No |

- Wheel Balancer:  With installation (part# 13002DA)				Qty: 1

| Automatic Data Entry Distance/Diameter |
| --- |
| Standard Cone Set |  |
| 3rd Window Diagnostics |  |
| Wheel Balancer Maximum Tire Weight | 160 lbs |
| Wheel Balancer Height | 48 in. |
| Wheel Balancer Width | 6 ft Includes Work Area |
| Wheel Balancer Depth | 6 ft Includes Work Area |
| Wheel Balancer Maximum Tire Diameter | 44 in. |
| Wheel Balancer Cycle Time | 5 s |
| Wheel Balancer Application | Passenger Car, Light Truck |
| Wheel Balancer Type | Computer |
| Wheel Balancer Rim Diameter Range | 8 in. - 30 in. |
| Wheel Balancer Motor Size | 1.5 hp Direct Drive |
| Wheel Balancer Shaft Diameter | 40 mm |
| Wheel Balancer Modes | 8 Modes |
| Wheel Balancer Weight | 630 lbs |
| SDS Required | No |
| Wheel Balancer Electrical Requirements | 220 Volts, 1 ph |

- Air Compressor:   With installation,80 GAL, 7.5hp, 1 phase			Qty: 1

(Carlyle PREMIER SIMPLEX 89368VBTP) or (Ingersoll Rand45465556)

| Air-cooled After-cooler |
| --- |
| Electronic Drain Valve - Automatically Drains Water from The Tank |
| Low Oil Level Switch - Protect Pump from Running In A Low Oil Condition |
| 100% Cast Iron Pump for Durability |
| 100% Continuous Duty Rating - Designed to Run 24 Hours A Day |
| 175 Maximum Psi F |
| Twin Piston "v-style" Pump |
| Air Compressor Pump Material | Cast Iron |
| CFM Pump Displacement | 24 @ 175 PSI |
| Magnetic Starter Required | Yes |
| Air Compressor Maximum Pressure | 175 |
| Portable Or Fixed Mount | Fixed |
| Tank Position | Vertical |
| Air Compressor SCFM Rating | 24 |
| Air Compressor Horsepower | 7.5 |
| Number of Cylinders | 1 |
| Single or Dual Stage | Dual Stage |
| Lubrication System Type | Splash |
| Maximum Voltage | 460 V |
| Air Compressor Type | Reciprocating |
| # Stages | 2 |
| Air Compressor Tank Capacity | 80 gal |
| Contains VOCs | No |
| # of Cylinders | 2 |
| Air Compressor Series | Type 30 |
| Magnetic Starter Included | Yes |
| Air Compressor Phase & Voltage | 3/240 |
| Air Compressor Tank Type | Vertical |
| Air Tank Capacity | 80 gal (US) |
| Air Compressor Phase | 3 |
| Maximum Pressure | 175 lb/in² |
| Air Compressor Pump RPM | 1500 |
| Gas / Electric | Electric |

- Airline filter/lube: (part# 90-7961)							Qty: 1

| Filter Micron Size | 40 |
| --- | --- |
| Micron Filter Cleanable | Yes |
| Filter Material | Sintered Bronze |
| Filter Port Size | 1/2 in. NPT |
| Modular System Compatible | Yes |
| Bowl Maximum Pressure | 150 PSI |
| Wall Mounting Bracket | No |
| Filter Bowl Size | 5 oz |
| Drain Type | Manual Push Style |
| Bowl Type | Poly Carbonate Bowl & Guard |
| Filter SCFM Rating | 100 scfm |
| Metal Bowl Guard | Yes |

- Oil Drain station: (part# 815-1266)							Qty: 1

| Top mounted evacuation port |  |
| --- | --- |
| OSHA friendly labeling |  |
| Molded poly tool tray |  |
| Tank mounted fluid level sight gauge |  |
| Reinforced 16 inch deep drawn centered funnel |
| Ball valve seals drain when not in use to meet EPA requirements |
| Portable | Yes |
| Contain Drum | Yes |
| Fluid Capacity | 16 gal |
| Maximum Height Adjustment | 70 in. |
| Contain Rollers | Yes |
| Drain Pedestal Material | Steel |
| Minimum Height Adjustment | 50 in. |

- Air Operated 55-gal Lube pump: (part# 821-5461)				Qty: 1

| Measure Amounts | Yes |
| --- | --- |
| Air Hose Inlet Size | 3/8 in. FNPT |
| Pump Usage | Lubricants |

- Oil Hose Reel: (part# 823-1129)							Qty: 1

| Outlet | 1/2 in. Male NPT |
| --- | --- |
| Hose Size | 50' x 1/2" - 23/32" |

- Parts Washer: (part# SW428) 							Qty:1

| Weight Capacity | 500 lbs |
| --- | --- |
| Fluid Capacity | 25 gal (US) |
| Fluid Capacity | 25 gal |
| Pump Capacity | 300 gph |
| Tank Height | 42 in |
| Pump Included | No |
| Attached Brush | No |
| SDS Required | Yes |
| Heater Type | 110 Volts, 1000 Watt |
| Material | Metal |
| Flexible Hose | Yes |

- Floor Jack: (part# 791-6420)							Qty: 1

| Jack Raised Height | 21 in |
| --- | --- |
| Jack Closed Height | 3.5 in |
| Lift Capacity | 7000 lbs |
| Jack Lift Distance | 3.7 in. - 21 in. |
| Actuation Type | Hand |
| Jack Saddle Diameter | 5 in |
| Air Operated | No |
| Handle Included | Yes |
| Grade Type | Standard (9) |
| Jack Type | Service or Floor Jack |

- Headlight Aimer: (part# 03010000)						Qty: 1

An approved headlight testing device - SAE approved No. J600a for photo-electric type and J602c for mechanic aimers

| Portable | Beam Selection |
| --- | --- |
| Rotating Mast | Visual Assist Meter |

- A/C R134A Refrigerant Recovery/Recharge & Recy. Unit: (part# 34788NI)													Qty: 1

| Fully automatic operation  program for service, walk away and return when complete |
| --- |
| Includes an integrated refrigerant identifier that samples the refrigerant in the vehicles A/C system prior to recovery. |
| 98.5% recovery efficiency |  |
| Charge accuracy within +/- ½ oz |  |
| Automatic internal tank refill. No stopping to fill the internal tank during service, or before service. |
| Automatic oil drain shows how much oil was removed from the system during service. |
| Display Type | LCD |
| Moisture Indicator Included | No |
| Storage Tank Capacity | 20 lbs |
| CFM Rating | 1.5 CFM |
| SDS Required | No |
| Full Storage Tank Indicator Included | Yes |

- A/C R1234YF Refrigerant Recovery/Recharge & Recy. Unit: (part#AC12344)												Qty: 1

| Fully automatic operation  program for service, walk away and return when complete |
| --- |
| Includes an integrated refrigerant identifier that samples the refrigerant in the vehicles A/C system prior to recovery. |
| 98.5% recovery efficiency |  |
| Charge accuracy within +/- ½ oz |  |
| Automatic internal tank refill. No stopping to fill the internal tank during service, or before service. |
| Automatic oil drain shows how much oil was removed from the system during service. |
| Display Type | LCD |
| Moisture Indicator Included | No |
| Storage Tank Capacity | 20 lbs |
| CFM Rating | 1.5 CFM |
| SDS Required | No |
| Full Storage Tank Indicator Included | Yes |

- Waste Oil Tank, 500-Gallon:							Qty: 1

| lockable | level and leak gauges |
| --- | --- |
| emergency vents | 2in. suction tube with cam lock fitting |
| Ports provided on both inner and outer tanks for easy access | locking fill box with integrated filter drain |
| Heavy-duty forged steel port flanges | fill ports |
| Powder-coat finish | pumping equipment |

- Mezzanine Stairs:  With Installation						Qty: 1

| Material | Steel |
| --- | --- |
| Number of Steps | 11 |
| Handrails Included | Yes |
| Load Capacity | 450 lb |
| Climbing Angle | 45 ° |
| Step Tread | Serrated |
| Step Width | 24 in |
| Step Depth | 10 in |
| Base Depth | 105-1/2 in |
| Overall Height | 142-1/2 in |
| Standards | OSHA and ANSI |
| Overall Width | 30in |
| Top Step Height | 104-1/2 in |
| Handrail Height | 38 in |

- Mezzanine Landing:	With Installation						Qty: 1

| Material | Steel |
| --- | --- |
| Handrails Included | Yes |
| Load Capacity | 125 lb Foot squared |
| Overall platform Height | 9 feet |
| Standards | OSHA and ANSI |
| Handrail Height | 38 in |

- Drill Press:										Qty: 1

| Horsepower | 0.75 HP |
| --- | --- |
| Volts | 115 |
| Max. Speed | 3,630 rpm |
| 360 Degree Head Swivel | Yes |
| Speeds (qty.) | 16 |
| Vertical Stroke | 3-3/8 in |
| Drilling Capacity | 5/8 in |
| Chuck Size | 5/8 in |
| Light Included | No |
| Stand Included | Yes |
| Swing | 15 in |

- Emissions Tester: BNLPAS101							Qty: 1

Must meet Pennsylvania auto inspection requirements 67 Pa. Code § 177.406. Equipment. (pacodeandbulletin.gov)

- Hose reel: L8611Z									Qty: 1

Heavy Duty Steel Air Hose Reel & 1/2" X 50' Air Hose

- Workbench:										Qty: 1

5’X2’

Maple top

Metal legs

- 6 Ton Hydraulic Press:								Qty: 1

Benchtop mount

18” working range.

- Bench vice:										Qty: 1

Heavy Duty

5” jaw width

5” jaw opening

360-degree swivel base

Anvil

Rotating Utility Combination Pipe and Home Vise

I-3.	Warranty

- All parts and labor for this procurement shall be covered by a 5-year warranty.

I-4.	Manufacturer Authorization

- If the Offeror submitting a response to this IFB and is not the original manufacturer of the equipment being provided, the Offeror must submit a Manufacturers Authorization Letter which clearly states the Offeror is authorized to provide the OEM’s equipment and services required by this IFB. The Manufacturers Authorization Letter must reference “IFB 61000XXXXX – Name of IFB”

I-5.	Delivery/Service Location.

PSP Troop C, Punxsutawney

485 North Findley Street

Punxsutawney, PA 15767