|  | PENNSYLVANIA STATE POLICE DEPARTMENT HEADQUARTERS 1800 ELMERTON AVENUE HARRISBURG, PA 17110 |
| --- | --- |

NO SUBSTITUTION PROCUREMENT

Date:	3/14/24

To:	Offeror

From:	Jason P. Hildebrandt

Issuing Officer

RE:	No Substitution Procurement – IFB# 6100060665

The Department respectfully requests this purchase be completed as a No Substitute bid since these specific products are needed for this procurement.

- 12K Hoist:  With installation (part# CL12A06) 				Qty: 1

| Safety Lock Equipped | Yes |
| --- | --- |
| Lift Pad Height | 4 3/4 in. |
| Lift Safety Lock Release Type | Manual |
| Lift Drive Thru Clearance | 102 3/4 in. |
| Maximum Lift Height | 154 in |
| Lift Height of Rise | 79 1/2 in. |
| Lift Safety Locks Type | Mechanical Auto Engaging |
| Lift Arm Restraint Type | Gear Type |
| Lift Motor Size | 2 HP |
| Width Between Columns | 114 7/8 in. |
| Foldable | no |
| SDS Required | No |
| Lift Model | 2 Post |
| Lift Weight | 2250 lbs |
| Remote Control | No |
| Lift Capacity | 12000 lbs |
| Lift Height | 154 in. |
| Lift Type | 2-Post |
| Lift Equalization Type | Cable |
| Adjustable Legs | yes |
| Weight | 2240 lbs |
| Lift Width | 140 in. |
| Lift Drive Mechanism Type | Hydraulic |
| Contains VOCs | No |
| Lift Safety Lock Intervals | 3 3/4 in. After First 15 1/2 in. |
| Lift Electrical Requirements | 208/230 Volts 1PH |

- Tire Changer:   With installation (part# MAXX80220)			Qty: 1

| Power Assist Tower Included | Yes |
| --- | --- |
| Power Source | Electric |
| Portable Or Fixed Mount | Fixed |
| Base Height | 87 in |
| Voltage | 220 V |
| On Board Storage | Yes |
| Wheel Clamping Method | External |
| Tire Changer Type | Manual |
| Hose Included | N/A |
| SDS Required | No |

- Wheel Balancer:  With installation (part# 13002DA)			Qty: 1

| Automatic Data Entry Distance/Diameter |
| --- |
| Standard Cone Set |  |
| 3rd Window Diagnostics |  |
| Wheel Balancer Maximum Tire Weight | 160 lbs |
| Wheel Balancer Height | 48 in. |
| Wheel Balancer Width | 6 ft Includes Work Area |
| Wheel Balancer Depth | 6 ft Includes Work Area |
| Wheel Balancer Maximum Tire Diameter | 44 in. |
| Wheel Balancer Cycle Time | 5 s |
| Wheel Balancer Application | Passenger Car, Light Truck |
| Wheel Balancer Type | Computer |
| Wheel Balancer Rim Diameter Range | 8 in. - 30 in. |
| Wheel Balancer Motor Size | 1.5 hp Direct Drive |
| Wheel Balancer Shaft Diameter | 40 mm |
| Wheel Balancer Modes | 8 Modes |
| Wheel Balancer Weight | 630 lbs |
| SDS Required | No |
| Wheel Balancer Electrical Requirements | 220 Volts, 1 ph |

- Air Compressor:   With installation (part# 80 GAL, 7.5hp, 1 phase)		Qty: 1

(Carlyle PREMIER SIMPLEX 89368VBTP) or (Ingersoll Rand45465556)

| Air-cooled After-cooler |
| --- |
| Electronic Drain Valve - Automatically Drains Water from The Tank |
| Low Oil Level Switch - Protect Pump from Running In A Low Oil Condition |
| 100% Cast Iron Pump for Durability |
| 100% Continuous Duty Rating - Designed to Run 24 Hours A Day |
| 175 Maximum Psi F |
| Twin Piston "v-style" Pump |
| Air Compressor Pump Material | Cast Iron |
| CFM Pump Displacement | 24 @ 175 PSI |
| Magnetic Starter Required | Yes |
| Air Compressor Maximum Pressure | 175 |
| Portable Or Fixed Mount | Fixed |
| Tank Position | Vertical |
| Air Compressor SCFM Rating | 24 |
| Air Compressor Horsepower | 7.5 |
| Number of Cylinders | 1 |
| Single or Dual Stage | Dual Stage |
| Lubrication System Type | Splash |
| Maximum Voltage | 460 V |
| Air Compressor Type | Reciprocating |
| # Stages | 2 |
| Air Compressor Tank Capacity | 80 gal |
| Contains VOCs | No |
| # of Cylinders | 2 |
| Air Compressor Series | Type 30 |
| Magnetic Starter Included | Yes |
| Air Compressor Phase & Voltage | 3/240 |
| Air Compressor Tank Type | Vertical |
| Air Tank Capacity | 80 gal (US) |
| Air Compressor Phase | 3 |
| Maximum Pressure | 175 lb/in² |
| Air Compressor Pump RPM | 1500 |
| Gas / Electric | Electric |

- Airline filter/lube: (part# 90-7961)						Qty: 1

| Filter Micron Size | 40 |
| --- | --- |
| Micron Filter Cleanable | Yes |
| Filter Material | Sintered Bronze |
| Filter Port Size | 1/2 in. NPT |
| Modular System Compatible | Yes |
| Bowl Maximum Pressure | 150 PSI |
| Wall Mounting Bracket | No |
| Filter Bowl Size | 5 oz |
| Drain Type | Manual Push Style |
| Bowl Type | Poly Carbonate Bowl & Guard |
| Filter SCFM Rating | 100 scfm |
| Metal Bowl Guard | Yes |

- Oil Drain station: (part# 815-1266)							Qty: 1

| op mounted evacuation port |  |
| --- | --- |
| OSHA friendly labeling |  |
| Molded poly tool tray |  |
| Tank mounted fluid level sight gauge |  |
| Reinforced 16 inch deep drawn centered funnel |
| Ball valve seals drain when not in use to meet EPA requirements |
| Portable | Yes |
| Contain Drum | Yes |
| Fluid Capacity | 16 gal |
| Maximum Height Adjustment | 70 in. |
| Contain Rollers | Yes |
| Drain Pedestal Material | Steel |
| Minimum Height Adjustment | 50 in. |

- Air Operated 55-gal Lube pump: (part# 821-5461)				Qty: 1

| Measure Amounts | Yes |
| --- | --- |
| Air Hose Inlet Size | 3/8 in. FNPT |
| Pump Usage | Lubricants |

- Oil Hose Reel: (part# 823-1129)							Qty: 1

| Outlet | 1/2 in. Male NPT |
| --- | --- |
| Hose Size | 50' x 1/2" - 23/32" |

- Parts Washer: (part# SW428)

| Weight Capacity | 500 lbs |
| --- | --- |
| Fluid Capacity | 25 gal (US) |
| Fluid Capacity | 25 gal |
| Pump Capacity | 300 gph |
| Tank Height | 42 in |
| Pump Included | No |
| Attached Brush | No |
| SDS Required | Yes |
| Heater Type | 110 Volts, 1000 Watt |
| Material | Metal |
| Flexible Hose | Yes |

- Floor Jack: (part# 791-6420)							Qty: 1

| Jack Raised Height | 21 in |
| --- | --- |
| Jack Closed Height | 3.5 in |
| Lift Capacity | 7000 lbs |
| Jack Lift Distance | 3.7 in. - 21 in. |
| Actuation Type | Hand |
| Jack Saddle Diameter | 5 in |
| Air Operated | No |
| Handle Included | Yes |
| Grade Type | Standard (9) |
| Jack Type | Service or Floor Jack |

- Headlight Aimer: (part# 03010000)						Qty: 1

An approved headlight testing device - SAE approved No. J600a for photo-electric type and J602c for mechanic aimers

| Portable | Beam Selection |
| --- | --- |
| Rotating Mast | Visual Assist Meter |

- A/C R134A Refrigerant Recovery/Recharge & Recy. Unit: (part# 34788NI) 	Qty: 1

| Fully automatic operation  program for service, walk away and return when complete |
| --- |
| Includes an integrated refrigerant identifier that samples the refrigerant in the vehicles A/C system prior to recovery. |
| 98.5% recovery efficiency |  |
| Charge accuracy within +/- ½ oz |  |
| Automatic internal tank refill. No stopping to fill the internal tank during service, or before service. |
| Automatic oil drain shows how much oil was removed from the system during service. |
| Display Type | LCD |
| Moisture Indicator Included | No |
| Storage Tank Capacity | 20 lbs |
| CFM Rating | 1.5 CFM |
| SDS Required | No |
| Full Storage Tank Indicator Included | Yes |

- A/C R1234YF Refrigerant Recovery/Recharge & Recy. Unit: (part#AC12344)	 Qty: 1

| Fully automatic operation  program for service, walk away and return when complete |
| --- |
| Includes an integrated refrigerant identifier that samples the refrigerant in the vehicles A/C system prior to recovery. |
| 98.5% recovery efficiency |  |
| Charge accuracy within +/- ½ oz |  |
| Automatic internal tank refill. No stopping to fill the internal tank during service, or before service. |
| Automatic oil drain shows how much oil was removed from the system during service. |
| Display Type | LCD |
| Moisture Indicator Included | No |
| Storage Tank Capacity | 20 lbs |
| CFM Rating | 1.5 CFM |
| SDS Required | No |
| Full Storage Tank Indicator Included | Yes |

- Waste Oil Tank, 500-Gallon:							Qty: 1

| lockable | level and leak gauges |
| --- | --- |
| emergency vents | 2in. suction tube with cam lock fitting |
| Ports provided on both inner and outer tanks for easy access | locking fill box with integrated filter drain |
| Heavy-duty forged steel port flanges | fill ports |
| Powder-coat finish | pumping equipment |

- Mezzanine Stairs:  With Installation						Qty: 1

| Material | Steel |
| --- | --- |
| Number of Steps | 11 |
| Handrails Included | Yes |
| Load Capacity | 450 lb |
| Climbing Angle | 45 ° |
| Step Tread | Serrated |
| Step Width | 24 in |
| Step Depth | 10 in |
| Base Depth | 105-1/2 in |
| Overall Height | 142-1/2 in |
| Standards | OSHA and ANSI |
| Overall Width | 30in |
| Top Step Height | 104-1/2 in |
| Handrail Height | 38 in |

- Mezzanine Landing:	With Installation						Qty: 1

| Material | Steel |
| --- | --- |
| Handrails Included | Yes |
| Load Capacity | 125 lb Foot squared |
| Overall platform Height | 9 feet |
| Standards | OSHA and ANSI |
| Handrail Height | 38 in |

- Drill Press:										Qty: 1

| Horsepower | 0.75 HP |
| --- | --- |
| Volts | 115 |
| Max. Speed | 3,630 rpm |
| 360 Degree Head Swivel | Yes |
| Speeds (qty.) | 16 |
| Vertical Stroke | 3-3/8 in |
| Drilling Capacity | 5/8 in |
| Chuck Size | 5/8 in |
| Light Included | No |
| Stand Included | Yes |
| Swing | 15 in |

- Emissions Tester: (part# BNLPAS101)							Qty: 1

Must meet Pennsylvania auto inspection requirements 67 Pa. Code § 177.406. Equipment. (pacodeandbulletin.gov)

- Hose reel: (part# L8611Z)								Qty: 1

Heavy Duty Steel Air Hose Reel & 1/2" X 50' Air Hose

- Workbench:										Qty: 1

5’X2’

Maple top

Metal legs

- 6 Ton Hydraulic Press:									Qty: 1

Benchtop mount

18” working range.

- Bench vice:										Qty: 1

Heavy Duty

5” jaw width

5” jaw opening

360-degree swivel base

Anvil

Rotating Utility Combination Pipe and Home Vise

An Internationally Accredited Law Enforcement Agency