Group 1-6: Boat Spec Sheet

-18x60 TDX Series

-21" Sides

- T-Rail Gunnel

- Two Tie Down Eyes

-Two Rope Cleats

- Heavy Duty 3” Half Pipe Front Bumper

- 20" Transom

- 1/8” 5086 Marine Aluminum

-  1″ x 2″ extrusion welded ribs that run the full length of the boat

- 4 Foot Front Deck - Under Deck Storage

- Extended Front Deck to Cover Gas Tank

-  Pedestal Base

- Full Floor (No Gutters)

- Front Deck Access Hatch

-Spud Kit:

- Includes: Two Spud Poles, Sockets and Mount for Spud Pole Clips

- 6′ to 12′ Telescopic Push Pole with Duck Foot, Paddle Attachment & Holders

-  Center Console Steering Kit - Single Rig

- Boat Rigging

- Installation of options and accessories

- All electrical wiring ran, fused, wrapped and connected

- Hydraulic steering installed and tested

- Includes a Battery, Battery Switch (On/Off), Battery Box, 14 Gallon Gas Tank, Anchor Lights, Bilge Pump with Switch and Hose, and Navigation Lights. Mounted and Installed in Boat, Water Ready.

- 40 HP XRF Motor with Forward, Neutral, and Instant Reverse, long shank 20”,  full Power Reverse, Steering Ready, Hydraulic Power Trim, Tach/Hour meter

- 60” Bottom boat Aluminum Trailer, 3500lb axle, 14" wheels, Side Guides, Aluminum Spare, Mount and LED Light Package.

–Stainless Steel Boat Buckle Rachet Tie Downs